## Slide 1: Inhibiting of Microbial Growth in vitro
CLS 212
Notes: IN previous lecture we have talk about the factors that effect microbial growth and we use this factors in the laboratory ( they encourage the growth )
Today we will take about the way we use it in the hospital, icu , restaurant to inhibit the growth of microbes
Eg : in the hospital it is necessary to inhibit microbial growth ?why
They will not infect patent , staff membare or visitor

## Slide 2
Microbicidal
Microbicidal is the process or an agent that kills the microorganism.
The suffix -cidal or –cide means ??( See chapter 8 page 131)
Microbistatic
Microbistatic is the process or an agent that inhibits the growth and reproduction of the microorganism.
The suffix -static or –state means ? ( See chapter 8 page 131)
Notes: We will describe terms used to destroy or inhibit the growth of microbes
The suffix -cidal or –cide means ''killing''.
The suffix -static or –state means ''inhibiting or stopping

## Slide 3: Sterilization & Disinfection
Sterilization :
*( See page 131 , chapter 8 )
*all forms of microbial life including bacteria, viruses, fungi, parasites, and spores.
Can be accomplished by physical or chemical method
Disinfection ( elimination or reducing ) :
*( See page 131 , chapter 8 )
*Can be accomplished by pasteurization or liquid chemical
Notes: Sterilization
Sterilization is the complete destruction or elemination of all forms of microbial life including bacteria, viruses, fungi, parasites, and spores.
Disinfection
Disinfection is reducing or eliminating the number of pathogenic microorganisms to the point where they no longer cause disease. But this method does not affect spores.

## Slide 4: Disinfection
Pasteurization
( See page 131 , chapter 8 )
Is a disinfecting method
For liquids e.g. milk, juice,..
Sanitization
Sanitization is the use of chemical agents on food-handling equipment to meet public health standards and minimize chances of disease transmission e.g. use of hot water & soap in cleaning restaurants.
Antiseptic :
( See page 131 , chapter 8 )
Notes: Pasteurization
Is a disinfecting method used to eliminate pathogens from liquids e.g. milk, juice,..
Sanitization
is the hygienic means of promoting health t
Antiseptic : solutions used to disinfect skin and living tissue

## Slide 5: STERILIZATION AND DISINFECTION METHODS
Methods used to destroy or inhibit microorganisms are either physical or chemical, and sometimes both types are used.
Notes: Importance of sterilization and disinfection:
Safety in the laboratory.
The patient safety depends on using proper methods of sterilization to prepare instruments, needles, IV fluids.

## Slide 7: Physical Methods

## Slide 8: Physical Methods
They are commonly used in hospitals, clinics, and laboratories. Physical methods include:
Heat.
Cold.
Desiccation.
Radiation.
Ultrasonic waves.
Filtration.
Gaseous atmosphere.

## Slide 9: I- HEAT
Heat is considered the most common method for sterilization because it is practical, efficient, and inexpensive.
Heat kills microorganisms by denaturing their enzymes and other proteins.
There are two methods of sterilization or disinfection by heat:
dry heat
moist heat
Notes: Two factors effect this method : temperature and time .

## Slide 10: I- HEAT 1. Dry Heat
An effective way to sterilize metals, glassware, some powders, oils, and waxes
Hot Air Oven:
It is done in a 160-165°C oven for 2hours or in 170-180°C oven for 1hour.
Burning (incineration):
Is used to destroy contaminated disposable materials.
Direct Flame:
Bunsen burner or electrical heating device is used to sterile wire loops and forceps used in the laboratory.

## Slide 11
Dry heat Oven
Bunsen Burner
Electric Bunsen
I- HEAT

## Slide 12: I- HEAT 2. Moist Heat
Use in sterilization or disinfection method
There are three methods of sterilization or disinfection by moist heat:
Boiling water >>>>disinfection
Pasteurization >>>>>disinfection
Autoclave >>>>>>>>> sterilization
Faster and more effective than dry heat

## Slide 13: I- HEAT 2. Moist Heat
boiling (100°C) for 30 minutes. used to disinfect syringes, needles, and simple instruments.
Boiling is not always effective as spores, like Mycobacteria, and some viruses are not affected.
Notes: Heat applied in the presence of moisture as in boiling or steaming
It is faster and more effictive than dry heat

## Slide 14: I- HEAT 3. Autoclave
Autoclave is :
Definition : See page 133 , chapter 8
For sterilization
Autoclaving is done at : See page 133 , chapter 8
Notes: An autoclave is a large metal chamber that uses steam under pressure for sterilization (like the pressure cooker).
Autoclaving is done at 121.5°C and 15psi pressure for 20 minutes.

## Slide 15
Notes: The autoclave is a tough double walled chamber in which air is replaced by pure saturated steam under pressure.

## Slide 16: 3. Autoclave
An autoclave tape or strip (commercially available) is used to ensure proper functioning.

## Slide 17: II- cold
Freezing (below zero)
Freezing will greatly slow the metabolic activities of microorganisms leading to inhibition of their growth.
2. Refrigeration (4°C)
Refrigeration will slightly affect the metabolic activities of most microorganisms but it would not completely inhibit growth.

## Slide 18: II- cold
CAUSION:
Thawing and refreezing of
food ???? See page 134 , chapter 8
Notes: Thawing and refreezing of
food will allow the bacteria
and its spores to resume
growing.

## Slide 19: III- Desiccation (Drying)
Many microorganisms stay viable even after drying but they cannot reproduce i.e. desiccation will inhibit the growth of microorganisms.
When suitable moist and nutrient rich environment is available, the microorganism will grow rapidly.
It is a method mainly used for food preservation,antisera, antitoxin, antibiotics, and pure culture of microorganisms.
Notes: dried viable pathogens may be found in blood, pus, fecal material and dust that are found on floors , in bedding, on clothing. Thus wet mopping of floors, damp dusting of furniture rolling bed linens an towels carefully, is very important to avoid transmission of these microbes through air

## Slide 20: IV- Radiation
There are two types of radiation that can be used to control microorganisms:
Ionizing radiation.
( non- Ionizing radiation ) :
Ultraviolet radiation ( non- Ionizing radiation )
Microwave radiation ( non- Ionizing radiation )

## Slide 21: IV- Radiation 1. Ionizing Radiation
Gamma rays, X-rays, and Beta rays from radioactive materials have short wavelengths (less than 1 nanometer).
Cause death or mutations in microorganisms as they damage the DNA and proteins.
Used to sterilize heat-sensitive materials including medical equipment, disposable surgical supplies and drugs. Radiation can be carried out after packaging.
Food industry is interested in using ionizing radiation e.g. chicken.
Disadvantages: Penetrates human tissues and may cause genetic mutations in humans and cancer.
Notes: Irradiation has been used for many years to control microorganism on herbs, vegetables, meat.

## Slide 22: 2. Ultraviolet light (Non-ionizing Radiation)
Wavelength is longer than 1 nanometer.  low penetration.
Damages DNA which cause mutations or death.
Effective in air and surfaces
Most commonly used as UV-lamps that sterilize operating rooms, nurseries, cafeterias,..
Disadvantages: Damages skin, eyes and does not penetrate paper, glass, and cloth.
Notes:   U.V. light- Has limited sterilizing power because of poor penetration into most materials.
  Generally used in irradiation of air in certain areas eg. Operating Rooms and T.B. laboratories.
UV forms thymine dimers that damage the DNA

## Slide 23: IV- Radiation 3. Microwave Radiation
Wavelength ranges from 1mm to 1m.
Very little effect on microbes
May kill microbial cells in moist foods but not spores.
Notes: Electromagnatic radiation

## Slide 24: V- Ultrasonic Waves
Used for cleaning and sterilizing delicate equipments.
Ultrasonic cleaners consist of water tanks, were short sound waves pass
through, removing organic
debris from equipments.

## Slide 25: VI- Filtration
Filtration is : ( see page 135 , chapter 8 )
Filters of various pore sizes can be used.
Used to sterilize heat sensitive materials like vaccines, enzymes, antibiotics, and some culture media.
High Efficiency Particulate Air Filters (HEPA):
( see page 136 , chapter 8 )
Notes: Filtration is :the removal of microbes by passage of a liquid or gas through a screen like material with small pores.
HEPA: Used in operating rooms and burn units to remove bacteria from air.

## Slide 27: VI- Filtration HEPA

## Slide 28: VII- Gaseous Atmosphere
In rare cases, changing the atmosphere can be used as a way to inhibit the growth of microorganisms.
Aerobes and microaerophiles can be killed by placing them in oxygen-free atmosphere. Whereas, anaerobes can be killed by placing them in oxygen atmosphere.

## Slide 29: Chemical Methods

## Slide 30: Chemical Methods
Disinfectants
A disinfectant is a chemical agent that
is used to inhibit microbial growth
on inanimate objects, surfaces, and floors.
Antiseptics
An antiseptic is a chemical agent that
is used to inhibit microbial growth
on human skin and mucous membranes.
Notes: Disinfectants may be:
High level disinfectants.
Intermediate level disinfectants.
Low level disinfectants.

## Slide 31: Medical devices, equipment, and surgical materials are divided into three general categories based on the potential risk of infection involved in their use:
critical items
semicritical items
noncritical items

## Slide 32
High risk (critical items):
Contacting tissue or blood, includes
(surgical instruments and arthroscopes)
must be sterilized
Intermediate risk (semicritical items):
Contact mucous membrane or non intact skin, includes ( G-I endoscopes and respiratory tubes) need high level disinfection.
Low risk (noncritical items):
Contact only contact skin, includes
(ward equipment and stethoscopes)
low level disinfection is sufficient

## Slide 33: Most commonly used Disinfectants
Soaps and detergents, alcohols, and
phenolic compounds: destroy
microbial cell membranes e.g. Dettol.
Formaldehydes, hydrogen peroxide, halogens, and salts of heavy metals:
destroy enzymes and structural
proteins e.g. Bleach, Clorox.
Chlorine, ozone, iodine:
attach nucleic acids.

## Slide 34: Most commonly used Antiseptics
Iodophor: used as skin antiseptic in surgery.
Alcohol: used on skin before needle pricking.
Mercurochrome: used to disinfect skin wounds.