## Slide 1: Manual Process Planning
Manufacturing Processes (2), IE-352
Ahmed M El-Sherbeeny, PhD
Spring 2014
Notes: <number>

## Slide 2: Chapter Outline
Introduction
Manual Process Planning
Process Plan
Part Features Identification and Processes Selection
Processes Sequencing
<number>

## Slide 3: Introduction
Process Planning
Known as:
  manufacturing planning
  material processing
  process engineering
  machine routing
Definition:
  act of preparing detailed work instructions to produce a part
  it’s a function within the manufacturing facility (see figure)
  establishes processes and parameters used to convert part from initial form to final form
  predetermined in an engineering drawing
  person who develops process plan: often called process planner
<number>

## Slide 4: Introduction
Functions included in process planning:
  Raw material preparation
  Processes selection
  Process sequencing
  Machining parameter selection
  Tool path planning
  Machine selection
  Fixture selection
<number>

## Slide 5: Introduction
Factors Affecting Process Plan Selection:
  Shape
  Tolerance
  Surface finish
  Size
  Material type
  Quantity
  Value of the product
  Urgency
  Manufacturing system itself
Two approaches to carry out task of process planning:
  Manual Process Planning
  Computer Aided Process Planning (CAPP)
<number>

## Slide 6: Manual Process Planning
Process planner must have following knowledge:
  Ability to interpret an engineering drawing
  Familiarity with manufacturing processes and practice
  Familiarity with tooling and fixtures
  Know what resources are available in the shop
  Know how to use reference books (e.g. machinability data handbooks)
  Ability to do computations on machining time and cost
  Familiarity with raw materials
<number>

## Slide 7: Manual Process Planning
Some necessary steps to prepare a process plan
  Study overall shape of part  identify features, all critical dimensions
  Thoroughly study the drawing; try to identify all manufacturing features and notes
  Determine best raw material shape to use if raw stock not given
  Identify datum surfaces; Use information on datum surfaces to determine the setups
  Select machines for each setup.
  Determine rough sequence of operations necessary to create all the features for each setup
<number>
Notes:   Add these remaining steps in the future
  Sequence the operations determined in the previous step. Check whether there is any interference or dependency between operations. Use this information to modify the sequence of operations.
  Select tools for each operation. Try to use the same tool for several operations if possible. Keep in mind the trade-off on tool-change time and estimated machining time.
  Select or design fixtures for each setup.
  Evaluate the plan generated and make necessary modifications.
  Select cutting parameters for each operation.

## Slide 8: Process Plan
Process Plan AKA (among others):
  operation sheet
  route sheet
  operation planning summary
  Detailed plan contains:
  route
  processes
  process parameters
  machine and tool selections
  fixtures
<number>

## Slide 9: Process Plan
The level of details in the plan depends on the application:
  Operation: a process
  Operation Plan (Op-plan): description of an operation
    includes tools, machines to be used, process parameters, machining time, etc.
  Op-plan sequence: Summary of a process plan
<number>

## Slide 10: Process Plan: Examples of Process Plans
<number>

## Slide 11: Part Features Identification and Processes Selection
A wide variety of manufacturing processes are used to produce a workpiece
These processes can be classified as:
  Casting processes
  Forming and shaping processes
  Machining processes
  Joining processes
  Finishing processes
<number>

## Slide 12: Part Features Identification and Processes Selection
Machining processes
  Drilling
    drilling, countering, countersinking, deep-hole drilling, etc.
  Boring
  Tapping
  Milling
    face milling, end milling
  Turning
    facing, straight turning, taper turning, parting, etc.
  Threading
<number>
Notes: Boring: process of enlarging a hole that has already been drilled; Tapping: process of cutting internal threads in a round hole with a multi-point tool

## Slide 13: Part Features Identification and Processes Selection
Features that must be considered in selecting machining processes include:
  part features
  required dimensional and geometric accuracy and tolerance
  required surface finish
  available resources, including NC machines and cutting tools
  cost
<number>

## Slide 14: Part Features Identification and Processes Selection
Part features:
  distinctive geometric form or shape to be produced from raw material
  it determines process type, tool types (shapes and size), machine requirements (3-, 4-, or 5-axis), and tool path
Two types of part features
  Basic features
    simple forms/shapes that require only one machining operation
    include holes, slots, pockets, shoulders, profiles, and angles
  Compound features
    consist of two or more basic part features
    e.g. the combined result of two holes with different diameters
<number>

## Slide 15: Part Features Identification and Processes Selection
Example: Machining Processes Selection
Select the machining processes for the part shown in the figure given in the next slide.
Assume required dimensional accuracy and surface roughness are within process capability of drilling and milling operations.
The four sides of the raw material have been pre-machined to required dimensions.
<number>

## Slide 16: Part Features Identification and Processes Selection
Example: Machining Processes Selection (cont.)
<number>

## Slide 17: Part Features Identification and Processes Selection
Example: Machining Processes Selection (cont.)
Solution:
  Top flat surface
  Outer profile
  Three holes
Recommended machining processes for features are
  Face-milling: the top surface
  Rough-milling: the outer profile
  Finish-milling: the outer profile
  Center-drilling: the three holes
  Drilling: the three holes
<number>

## Slide 18: Processes Sequencing
Sequence of operations determined by three considerations:
Datum surfaces should be machined first if multiple work-holding setups required
  If possible, datum surfaces should be pre-machined in manually operated machine to facilitate workpiece locating and clamping
  In cases where  2 holding setups are required:
    rough datum surfaces are preprocessed in a manually operated machine
    then used as setup references to produce finished datum surfaces for the final work-holding
    this ensures the accuracy of the finished part
<number>

## Slide 19: Processes Sequencing
Sequence of operations determined by 3 considerations (cont.)
Surfaces with larger area have precedence
  Larger surfaces tend to be more adaptable to disturbances resulting from machining operations
Feature interference should be avoided.
  Feature interference occurs when machining of one feature destroys a requirement for the production of other features
  This happens when there is interaction or dependency between machining operations
<number>

## Slide 20: Processes Sequencing: Example
The figure shown in the next slide is a workpiece in which some features are interrelated.
The workpiece has five basic features
  a through slot in side C
  two angle strips (strip 1, strip 2)
  two through holes on strip 1 that are perpendicular to side A
  compound features are two tapped holes perpendicular to strip 1
Develop the process sequence for producing the part.
<number>

## Slide 21: Processes Sequencing: Example (cont.)
<number>

## Slide 22: Processes Sequencing: Example (cont.)
Solution:
The raw material is cut from a block stock with dimensions: 6.25 x 4.25 x 2.25 in
Studying the part features reveals:
  2 through holes on strip 1 interact with the formation of angle 
  slot in side C interacts with the cutting of angle β
Machining angle strip 1 first  difficulty in drilling 2 holes
   2 holes must be produced before angle strip 1
Likewise, making angle strip 2 first  difficulty in setting up workpiece to produce the through slot
   the slot has to be machined before angle strip 2 is made
<number>

## Slide 23: Processes Sequencing: Example (cont.)
Recommended processes sequence is:
Setup A for machining side B
Setup B for:
  machining sides A and E
  also drilling two holes on Side A
Setup C for:
  machining sides C and F
  also cutting the slot in side C
Setup D for:
  cutting angle strip 1
  drilling two tap holes and tapping the two holes.
Setup E for cutting angle strip 2
<number>

## Slide 24
<number>