## Slide 1
7. CLASSIFICATION OF SOILS

## Slide 2
INTRODUCTION
Soil classification is the arrangement of different soils with similar properties into groups and subgroups based on their application.
Soils may be classified in a general way as:
Cohesive vs. cohesionless
Fine- grained vs. coarse grained
Residual vs. Transported
However these terms are too general and cover too wide range of physical and engineering properties.
A more refined classification is necessary to determine the suitability of a soil for specific engineering purposes.
Therefore, these terms are collected into SOIL CLASSIFICATION SYSTEMS, usually with some specific engineering purpose in mind.
A number of classification systems have been proposed since the 1st quarter of the 20th century.

## Slide 3
NEED FOR SOIL CLASSIFICATION SYSTEMS
A soil classification system represents, in effect, a language of communication between engineers.
It enables one to use the engineering experience of others.
The engineering properties have been found to correlate quite well with the index and classification properties of a given soil deposit.
Therefore, by knowing the soil classification, the engineer already has a fairly good general idea of the way the soil will behave.
Most of the soil classification systems that have been developed for engineering purposes are based on simple index properties such as particle-size distribution and plasticity.

## Slide 4
Classification System
“Language”
Engineering Properties
Permeability, shear strength, compressibility,
swell-shrinkage etc.
Engineering Purpose
(Foundation, Dams, Highways, Airfields, etc.)
Role of Soil Classification in Geotechnical Engineering
Classification and index properties
(w, e,  , s, GSD, LL, PI, etc.)

## Slide 5
Why more than one Classification System are in use?
Classification systems are used to group soils in accordance with their general behavior under given physical conditions.
Soils that are grouped in order of performance for ONE SET of Physical CONDITIONS will not necessarily have the same order for performance under other set of physical conditions.
This led to classifying soil by use, and each agency (Like FAA, AASHTO, USBR) has in mind specific use for the soils.

## Slide 6
SOIL CLASSIFICATION SYSTEMS
1. Grain-size classification
Limitations:
Gives only border between groups (i.e. gravel, sand, silt, clay) but does not give us a name for a given bulk of soil.
In most cases, natural soils are mixtures of particles from several size groups.

## Slide 7
2. TEXTURALCLASSIFICATION
The texture of a soil is its appearance or ”feel” and it depends on:
Generally the term texture is refereed wholly to the size characteristics of the soil particles.
Large soil particles with some small particles will give COARSE-APPEARNCE or COARSE-TEXTURED soil.
Smaller particles give a MEDIUM TEXTURED soil.
Fine-grained particles give FINE-TEXTURED soil.
In the textural classification system, the soils are named after their principal components, such as sandy clay, silty clay, and so forth.
The relative sizes of the particles
Range or distribution of these sizes
Shapes of the particles

## Slide 8
A number of textural classification systems were developed in the past by different organizations.
The following figure shows the textural classification system developed by the USDA. It is based on the particle size limit as shown in Table 2.3 in the textbook.
Loam is soil composed of sand, silt, and clay in relatively even concentration (about 40-40-20% concentration, respectively).

## Slide 10
If there were no gravel in the soil, the line representing the three sizes included in the chart would intersect at a common point.
The chart is based on only the fraction of soils that passes through No. 10 sieve (opening = 2 mm).
In concrete technology called Feret Triangle.
Percentage of each class can be determined from GSD (without GSD, percentage can be determined based on sieve size opening).
If a certain percentage of the soil particles are > 2 mm in diameter, then a correction will be necessary.
REMARKS

## Slide 11
Example 1
Let it be desired to determine the textural classification of a soil whose grading is as follows:
Gravel | 4%
Sand | 31%
Silt-size | 44%
Clay-size | 21%
The two lines intersect within the area labeled LOAM, which is the textural class of this soil.
Notes
We could have used the point of intersection of:
Silt-size+ Clay-size
Sand-size + Clay-size

## Slide 12
Example 2
The textural classification is CLAY.
Gravel | 10%
Sand | 18%
Silt-size | 27%
Clay-size | 45%
Find the modified textural composition:
Let it be desired to determine the textural classification of a soil whose grading is as follows:
Because of the large percentage of gravel, it may be called GRAVELLY CLAY.

## Slide 13
They are based entirely on particle-size distribution and does not consider PLASTICITY which to great extent influences the physical properties of soils.
Limitations of Textural Classification Systems
The two elaborate systems used at present are AASHTO and USCS. Both systems take into account the particle-size distribution and plasticity.
Because textural classification systems do not take plasticity into account and are not totally indicative of many important soil properties, they are inadequate for most engineering purposes.
The AASHTO classification system is used mostly by highway departments. Geotechnical engineers generally prefer the Unified system.

## Slide 14
3. CLASSIFICATION BY USE
A. AASHTO CLASSIFICATION SYSTEM
The AASHTO soil classification system was originally developed in the late 1920’s (1929) by the U.S. Bureau of Public Roads (BPR) for the classification of soils for highway subgrade use.
It was developed as a result of the work of Hogentogler in the 1920’s.
Originally, the system classified soil as being either a group A or a Group B.
AASHTO : Acronym of American Association of State Highway and Transportation Officials.
Adopted by Bureau of Public Roads in 1931.

## Slide 15
It went through various revisions since 1929, and the classification system received its last revision in 1974.
ASTM D-3282; AASHTO method M145.
A Group A soil was able to maintain uniform pavement support at all location whereas the Group B soils were not.
The B designation was subsequently deleted, leaving only A soils in the classification system.
Consequently, the “A” still remains in an AASHTO classification of a soil type, but it no longer has any real significance.
The A soils were subdivided into eight subgrade soil groups. A-1 through A-8.

## Slide 16
Tests Required:
Grain-size analysis
Liquid Limit
Plastic Limit
Criteria:

## Slide 17
Remarks
In addition to Sieve no. 10 & 200 also sieve no. 40 is involved in AASHTO classification which separates between medium and fine sands.
In the classification, differentiation between silt and clay soils is based on plasticity.
Sieve No. 10
Sieve No. 200
Notes: CE 382 Geotechnical Engineering I
<number>

## Slide 18
<number>
4.75 mm
2.0 mm
0.425 mm
0.075 mm
(AASHTO)
Gravel
(USCS)
Sand

## Slide 19
Sieve No. involved in AASHTO Soil Classification System

## Slide 20
3 Groups
6 Subgroups

## Slide 21
4 Groups
2 Subgroups

## Slide 22
For classification starts apply the test data from left to right, top to bottom. By process of elimination, the first group from the left into which the test data fit is the correct classification.
No. 10
No. 40
No. 200

## Slide 23
If the soil is A-1 or A-3 we cannot use this chart (mainly non plastic soils).
The plot below is for the range of the liquid limit and the plasticity index for soils that fall into groups A-2, A-4, A-5, A-6, and A-7.
Note:
Differentiation between A-2’s and other group is based on %passing Sieve No. 200

## Slide 24
According to this system, soil is classified into eight major groups, A-1 through A-8.
Soil group A-8 is peat (very organic) or muck (thin very watery, and with considerable organic material).
A soil is classified according to the table by proceeding from left to right, top to bottom, column by column on the table to find the first group in which the soil test data will fit.
The first group from the left into which the test data will fit is the correct classification.
REMARKS
The classification process stops at this point regardless if another column farther to the right can also qualify.

## Slide 25
GROUP INDEX
Soils containing fine-grained material are further identified by a number called GROUP INDEX (GI). This was to establish the relative RANKING of a soil within a subgroup or a group. This help in evaluating the quality of a soil as a highway subgrade material.
It is dependent on:
1. Percentage of the soil passing the No. 200 (0.075 mm) sieve.
2. Liquid limit, LL
3. Plasticity Index, PI
The index is given by the following empirical formula:
F200= % passing No. 200 sieve.

## Slide 26
Rules for Determining Group Index
If GI is negative value take it as zero.
GI is rounded off to the nearest whole number.
There is no upper limit for GI.
The group index belonging to groups A-1-a, A-1-b, A-2-4, A-2-5 and A-3 will always be zero. Why?
When calculating the group index for soils belonging to groups A-2-6 and A-2-7, the partial group index for PI should be used, or
The group index value is written in parenthesis next to the AASHTO symbol. Ex. A-2-6(3), A- 4(5) etc.
In general the higher the GI, the less desirable is the soil for use as a subgrade. A GI of 0 indicates a “good’ subgrade , and a GI> or equal 20 indicates a “very poor” subgrade material.

## Slide 27
No. 10
No. 40
No. 200
GI = 0
Partial
Group
Index
Full Group Index

## Slide 28
Example 1
The sieve analysis and plasticity data for two soils are given in the table below. Classify soils according to the AASHTO soil classification system.
Sieve Size | Soil 1 %finer | Soil 2 %finer
NO. 4 | 100 | 35
NO. 10 | 100 | 20
NO. 40 | 99 | 10
NO. 100 | 90 | 5
NO. 200 | 75 | 2
LL | 110 | -
PL | 50 | -

## Slide 29
No. 10
No. 40
No. 200
Sieve Size | Soil 1 %finer | Soil 2 %finer
NO. 4 | 100 | 35
NO. 10 | 100 | 20
NO. 40 | 99 | 10
NO. 100 | 90 | 5
NO. 200 | 75 | 2
LL | 110 | -
PL | 50 | -
Soil 1:
A-7-5
GI =(75-35)[0.2+.005(110-40)]
+0.01(75-15)[60-10] = 52
The soil is A-7-5(52)
Soil 2:
A-1-a(0)

## Slide 30
110
Soil 1:
A-7-5
Because %Passing #200 > 35%
The soil is classified as A-7-5 and not A-2-7.

## Slide 31
Example 2

## Slide 32
#200 86%
LL 70%
PI 32%
Because %Passing #200 > 35%
The soil is classified as A-7-5 and not A-2-7.

## Slide 33
Example 3
The grain size distribution curve, natural water content, liquid limit, and liquidity index are give below. Classify the soil according to the AASHTO Classification System.
PL =21.25%
PI = 18.75%
Sieve No. | %finer
NO. 4 | 98
NO. 10 | 86
NO. 40 | 28
NO. 200 | 10
LL | 40
PI | 19
40
Given
Solution

## Slide 34
No. 10
No. 40
No. 200
Sieve No. | %finer
NO. 4 | 98
NO. 10 | 86
NO. 40 | 28
NO. 200 | 10
LL | 40
PI | 19
From the AASHTO Table the soil is classified as: A-2-6 (0)

## Slide 35
Because %Passing #200 < 35%
The soil is classified as A-2-6 and not A-6.
Sieve No. | %finer
NO. 4 | 98
NO. 10 | 86
NO. 40 | 28
NO. 200 | 10
LL | 40
PI | 19
Note: If the location comes along the border line, we need to consult the table and the grain size will tell the classification of the given soil.

## Slide 36
Remarks About AASHTO System
Boulders (retained on 75 mm (3 inch) sieve] should be excluded from the portion of the sample to which the classification is applied, but the percentage of such material, if any, in the sample should be recorded.
Differentiation between A-7-5, A-7-6 is according to the following criterion:
PI <= LL- 30 ------A-7-5
PI > LL- 30-------- A-7-6
Group A-3 is placed before group A-2 in the table since:
It is better as a subgrade
It is based only on grain size
So it was easer to put A-3 before A-2 in order to facilitate left to right and top to bottom procedures applied in this system.
For A-1, A-3, A-2-4, A-2-5…>> F<= 35% , PI < 15, therefore GI –ve (i.e. GI always zero).
Or instead we use the chart

## Slide 37
B. UNIFIED SOIL CLASSIFICATION SYSTEM (USCS)
This system was developed by Arthur Casagrande in 1942 for use in the air field construction works undertaken by the Army Corps of Engineers during WW II.
To make it applicable to DAMS and other constructions besides airfields, it was revised in 1952 in cooperation with the USBR.
The system was last revised in 1984 by the ASTM by the addition of a GROUP NAME to the group symbol. This modification has not been adopted by some agencies which use USCS to classify soils.
ASTM Test Designation D-2487.

## Slide 38
Coarse-grained soils < =50% passes sieve No. 200
Fine-grained soils > 50% passes sieve No. 200
Organic
This system classifies soils under three broad categories:
Criteria for USCS:
Grain size
Cu, Cc
Plasticity (Plasticity chart)
Tests required
Grain-size analysis
Liquid Limit
Plastic Limit
This system is the most popular soil classification system among geotechnical engineers.

## Slide 39
Prefix | Definition | Suffix | Definition
G | Gravel | W | Well graded
S | Sand | P | Poorly Graded
M | Silt | M | Silty
C | Clay | C | Clayey
O | Organic | H | High Plasticity
Pt | Peat | L | Low Plasticity
All soils are classified into 15 groups each group is designated by two letters called a GROUP SYMBOL.
The first letter of the group symbol is termed the PREFIX and the second letter is termed the SUFFIX. These letters are abbreviations of certain soil characteristics as follows:

## Slide 40
Use Plasticity Chart
Gravels
Sands
High
Plasticity
Low
Plasticity

## Slide 41
Sands
Gravels
AASHTO
USCS

## Slide 42
To determine if well graded (W) or poorly graded (P), calculate Cu and Cc
Coefficient of uniformity
Coefficient of gradation

## Slide 43
B-Line
MH
CH
ML
CL-ML
CL
A-Line
U-Line
OH
or
OH
or
OH
or
OH
or
OL or OH based on the value of a

## Slide 44: Organic Soils
  Organic clay or silt (group symbol OL or OH):
  The second symbol is obtained by locating the values of PI and LL (not oven dried) in the plasticity chart.
Highly organic soils- Peat (Group symbol Pt)
  A sample composed primarily of vegetable tissue in various stages of decomposition and has a fibrous to amorphous texture, a dark-brown to black color, and an organic odor should be designated as a highly organic soil and shall be classified as peat, PT.

## Slide 45
Coarse-grained soils (Gravel (G) or Sand (S))
Fine-grained soils (Silt (M) or Clay (C))
% Passing sieve No. 200 (0.075 mm)
> 50%
< = 50%
% Coarse soil (Co) = 100 - % Passing # 200
% Gravel (G) = 100 - % Passing # 4
G > 1/2 Co
G < 1/2 Co
Gravel (G)
Sand (S)
% Passing sieve No. 200
< 5%
5% -12 %
> 12%
GW, GP, SW or SP
Use  Cu, Cc
W : well graded P: poorly graded
GW-GM, GW-GC, GP-GM, GP-GC, SW-SM, SW-SC, SP-SM, SP-SC
GM, GC, SM, SC
Use  plasticity charts
B-Line
MH
CH
ML
CL-ML
CL
A-Line
OH
or
OH
or
OL
or
OL
or
OL or OH based on the value of 

## Slide 46
Example 1
The sieve analysis and plasticity data for two soils are given in the table below. Classify the soils according to the USCS soil classification system.
Sieve Size | Soil 1 %finer | Soil 2 %finer
NO. 4 | 100 | 100
NO. 10 | 93 | 100
NO. 40 | 52 | 100
NO.100 | 25 | 92
NO. 200 | 16 | 85
LL | 38 | 89
PL | 23 | 49
Soil 1:
Soil 2:
SC
MH

## Slide 47: Example 2
<number>
Classify the following soils Using USCS
SC
CH
SM

## Slide 48
SC
CH
SM
Example 2 (Cont.)

## Slide 49: Example 2 (Cont.)
<number>

## Slide 50
<number>
Example 3

## Slide 51
<number>
Soil A is then classified as SP-SM
(Poorly graded sand with silt and gravel)

## Slide 52: Example 4
#4 = 95%
#200 = 11%
Coarse fraction =100-11 = 89%,
Gravel = 100 -95 = 5% (5/89 = 5.6% < 50%) - Sand
From Atterberg Tests
LL = 32, PL = 26
Notes: Example

## Slide 53: Example 4 (cont.)
D10 = 0.06 mm, D30 = 0.25 mm, D60 = 0.75 mm
Cu = 0.75/0.06 = 12.5 Cc = 0.25X0.25/(0.75X 0.06) = 1.39
 Well graded
Notes: Example

## Slide 54
From Atterberg Tests
LL = 32, PL = 26
PI = 32-26 = 6
The soil is classified as SW-SM (Well-graded sand with silt)
The fine part is silt

## Slide 56
Remarks
If for coarse-grained soils, the percent passing through the No. 200 sieve is between 5 and 12% dual symbols are needed (i.e. GW-GC, GP-GC, GW-GM, GP-GM, SW-SC, SP-SC, SW-SM, SP-SM).
A soil that plots in the area to the left of the A-line in the plasticity chart bounded by 4<= PI <=7, the A-line, and the left of the boundary chart has a dual-classification of CL-ML. This is the only fine-grained soil that has such a dual classification.
Peat is visually identified
Whether the fine-grained soil is organic or not, that is determined as follows:

## Slide 57
Comparison of the USCS and AASHTO Classification Systems
In AASHTO if 35% passes No. 200  fine-grained
In USCS if 50% passes No. 200  fined-grained
In AASHTO Sieve No. 10 is used to separate gravel from sand, in USCS it is Sieve No.4.
In USCS, the gravely and sandy soils are clearly separated, in the AASHTO system they are not.
The symbols GW, SM, CH and others that are used in the USCS are more descriptive of the soil properties than the A symbols used in the AASHTO system.
The classification of organic soils such as OL, OH, and Pt has been provided in the USCS. In AASHTO system, there is no place for organic soils. (A-8 has been taken out).

## Slide 58
In AASHTO PI is used to distinguish between silt and clay (LL appears only in distinguishing A-7-5 and A-7-6). In USCS both PI and LL (plasticity chart) are used.
USCS distinguishes high and low plastic fine-grained soils.
Both AASHTO and USCS are better than most other available systems when applied to engineering or construction applications.
Both AASHTO and USCS systems have the advantage of having been used for many years and having gained acceptance in the engineering and construction fields.