## Slide 1: Lesson 10: Configuring IPv4 and IPv6 Addressing
MOAC 70-410: Installing and Configuring Windows Server 2012

## Slide 2: Overview
Exam Objective 4.1: Configure IPv4 and IPv6 Addressing
IPv4 Addressing
IPv6 Addressing
Planning an IP Transition
Notes: Lecture notes go here

## Slide 3: IPv4 Addressing
Lesson 10: Configuring IPv4 and IPv6 Addressing
Notes: Lecture notes go here

## Slide 4: IPv4 Addressing
IP Address
  32-bit address
  Four 8-bit decimal values between 0 and 255 separated by periods (octets)
Subnet Mask
  32-bit value of 0’s and 1’s
  1’s designate network bits, 0’s are host bits
Network Host
Examples: IP Address 192.168.43.100
Subnet Mask 255.255.255.0
Notes: Explain how each host on a network requires a unique address for communication.

## Slide 5: IPv4 Classful Addressing
The three IPv4 address classes
Notes: Explain that this is what USED to be done, but it is very wasteful. Use the next slide to help explain.

## Slide 6: IPv4 Address Classes
IP Address Class | Class A | Class B | Class C
First bit values (binary) | 0 | 10 | 110
First byte value (decimal) | 0–127 | 128–191 | 192–223
Number of network identifier bits | 8 | 16 | 24
Number of host identifier bits | 24 | 16 | 8
Number of possible networks | 126 | 16,384 | 2,097,152
Number of possible hosts | 16,777,214 | 65,534 | 254

## Slide 7: Classless Inter-Domain Routing
Classful addressing was gradually phased out by a series of subnetting methods, including variable length subnet masking (VLSM) and, eventually, Classless Inter-Domain Routing (CIDR).
CIDR is a subnetting method that enables administrators to place the division between the network bits and the host bits anywhere in the address, not just between octets.
Notes: Because Classful address is wasteful and the Internet has grown beyond the available addresses, mechanisms were created to extend the life of IPv4 by creating less waste and repeatedly using the same addresses.

## Slide 8: CIDR
CIDR notation: 192.168.43.0/26
Where the /26 means 26 bits of the address are used as the network identifier
In binary, the subnet mask translates to: 11111111.11111111.1111111.11000000 or 255.255.255.192 in decimal
This would allow us to divide this address into 4 networks, each with up to 62 hosts
Notes: Compare this to the default setting of 192.168.43.0/24, and use the example in the book.

## Slide 9: CIDR 192.168.43.0/26 Networks
Network Address | Starting IP Address | Ending IP Address | Subnet Mask
192.168.43.0 | 192.168.43.1 | 192.168.43.62 | 255.255.255.192
192.168.43.64 | 192.168.43.65 | 192.168.43.126 | 255.255.255.192
192.168.43.128 | 192.168.43.129 | 192.168.43.190 | 255.255.255.192
192.168.43.192 | 192.168.43.193 | 192.168.43.254 | 255.255.255.192
Notes: Use this table to illustrate the example on the previous slide.

## Slide 10: Public and Private IPv4 Addressing
Registered IP addresses are not necessary for workstations that merely access resources on the Internet
The three blocks of addresses allocated for private use are as follows:
  10.0.0.0/8
  172.16.0.0/12
  192.168.0.0/16
Notes: Explain how there are not enough registered addresses left and that this is a way for the same addresses to be used repeatedly.

## Slide 11: IPv4 Subnetting
Allows you to split one IP address range into multiple networks (e.g., you can take the 10.0.0.0/8 private IP address range and use the entire second octet as a subnet ID).
This creates up to 256 subnets with up to 65,536 hosts.
The subnet masks will be 255.255.0.0 and the network addresses will proceed as follows:
  10.0.0.0/16
  10.1.0.0/16
  10.2.0.0/16
  …
  10.255.0.0/16
When you are working on an existing network, the subnetting process is more difficult.
Notes: Use the example in the book to expand on this.

## Slide 12: Calculate IPv4 Subnets
Determine how many subnet identifier bits you need to create the required number of subnets.
Subtract the subnet bits you need from the host bits and add them to the network bits.
Calculate the subnet mask by adding the network and subnet bits in binary form and converting the binary value to decimal.
Take the least significant subnet bit and the host bits, in binary form, and convert them to a decimal value.
Increment the network identifier (including the subnet bits) by the decimal value you calculated to determine the network addresses of your new subnets.
Notes: Use these steps to work through an example.

## Slide 13: Supernetting
Allows contiguous networks to be added to a routing table with one entry to reduce the size of Internet routing tables.
For example:
  172.16.43.0/24
  172.16.44.0/24
  172.16.45.0/24
  172.16.46.0/24
  172.16.47.0/24
Can all be expressed in one supernet address: 172.16.40.0/21
Notes: Use the calculations in the book to work through this example

## Slide 14: Assigning IPv4 Addresses
To assign IPv4 addresses, there are three basic methods:
Manual configuration
Dynamic Host Configuration Protocol (DHCP)
Automatic Private IP Addressing (APIPA)

## Slide 15: Manual IPv4 Address Configuration
Manually enter IP address, subnet mask, default gateway and DNS servers.
Use a GUI or command line.
Not difficult, but it can be time consuming on a large network.
Difficult to troubleshoot if information is entered incorrectly.

## Slide 16: Dynamic Host Configuration Protocol (DHCP)
Client computers are configured to Obtain an IP address automatically.
DHCP Servers on the network contain a pool of addresses and other IPv4 configuration.
Clients request configuration at boot up.
DHCP Servers respond to the requests.
IPv4 configurations are leased for a period of time and renewed as necessary.
No addresses are duplicated.

## Slide 17: Assigning IPv4 Addresses
The Internet Protocol Version 4 (TCP/IPv4)
Properties sheet
Notes: Note the settings in the dialog box for manual or Automatic configuration.

## Slide 18: Automatic Private IP Addressing (APIPA)
A DHCP failover mechanism used by all current Microsoft Windows operating systems.
If a system fails to locate a DHCP server on the network, APIPA takes over and automatically assigns an address on the 169.254.0.0/16 network to the computer.
For a small network that consists of only a single LAN, APIPA is a simple and effective alternative to installing a DHCP server.

## Slide 19: IPv6 Addressing
Lesson 10: Configuring IPv4 and IPv6 Addressing
Notes: Lecture notes go here

## Slide 20: IPv6 Addressing
Designed to increase the size of the IP address space (128 bit), thus providing addresses for many more devices than IPv4
Reduces the size of the routing tables because the size of the addresses provides for more than the two levels of subnetting currently possible with IPv4

## Slide 21: Introducing IPv6
IPv6 addresses use a notation called colon-hexadecimal format
Eight 16-bit hexadecimal numbers, separated by colons: XX:XX:XX:XX:XX:XX:XX:XX
Each X represents eight bits (or 1 byte), which in hexadecimal notation is represented by two characters, as in: 21cd:0053:0000:0000:e8bb:04f2:003c:c394

## Slide 22: Contracting IPv6 Addresses
When an IPv6 address has two or more consecutive eight-bit blocks of zeroes, you can replace them with a double colon (but you can only use one double colon in any IPv6 address): 21cd:0053::e8bb:04f2:003c:c394
You can also remove the leading zeros in any block where they appear: 21cd:53::e8bb:4f2:3c:c394
Notes: Contracting, as in contractions…..shortening the address.

## Slide 23: Expressing IPv6 Network Addresses
No subnet masks in IPv6
Network addresses use the same slash notation as CIDR:
21cd:53::/64
This is the contracted form for the following network address:
21cd:0053:0000:0000/64

## Slide 24: IPv6 Address Types
IPv6 supports three address types:
Unicast: Provides one-to-one transmission service to individual interfaces, including server farms sharing a single address. IPv6 supports several types of unicast addresses, including global, link-local, and unique local.
Multicast: Provides one-to-many transmission service to groups of interfaces identified by a single multicast address.
Anycast: Provides one-to-one-of-many transmission service to groups of interfaces, only the nearest of which (measured by the number of intermediate routers) receives the transmission.

## Slide 25: Global Unicast Addresses
The current official format for global unicast addresses consists of the following elements:
Global routing prefix: A 48-bit field beginning with the 001 FP value, the hierarchical structure of which is left up to the RIR
Subnet ID: Formerly known as the SLA, a 16-bit field that organizations can use to create an internal hierarchy of sites or subnets
Interface ID: A 64-bit field identifying a specific interface on the network

## Slide 26: Global Unicast Addresses
The current IPv6 global unicast address format

## Slide 27: Subnet IDs
Organizations have a16-bit subnet ID with which to create an internal subnet hierarchy, if desired. Here are some of the possible subnetting options:
  One-level subnet: By setting all subnet ID bits to 0, all computers in the organization are part of a single subnet. This option is only suitable for smaller organizations.
  Two-level subnet: By creating a series of 16-bit values, you can split the network into as many as 65,536 subnets. This is the functional equivalent of IPv4 subnetting, but with a much larger subnet address space.
  Multi-level subnet: By allocating specific numbers of subnet ID bits, you can create multiple levels of subnets, sub-subnets, and sub-sub-subnets; suitable for an enterprise of almost any size.
Notes: Use example on the next slide to illustrate.

## Slide 28: Subnet ID Example
To support a large international enterprise, you could split the subnet ID as follows:
Country (4 bits): Creates up to 16 subnets representing countries in which the organization has offices
State (6 bits): Creates up to 64 sub-subnets within each country, representing states, provinces, or other geographical divisions
Office (2 bits): Creates up to 4 sub-sub-subnets within each state or province, representing offices located in various cities
Department (4 bits): Creates up to 16 sub-sub-sub-subnets within each office, representing the various departments or divisions.
To create a subnet ID for a particular office, it is up to the enterprise administrators to assign values for each field.
Notes: Expand on this example using the information in the book.

## Slide 29: Interface IDs
The interface ID contains a unique identifier for a specific interface on the network.
The Institute for Electrical and Electronic Engineers (IEEE) defines the format for the 48-bit MAC address assigned to each network adapter by the manufacturer, as well as the EUI-64 identifier format derived from it.
A privacy problem with this method of deriving interface IDs from the computer’s hardware—the location of a mobile computer might be tracked based on its IPv6 address.
Instead of using MAC addresses, Windows operating systems generate random interface IDs by default.

## Slide 30: Link-Local Unicast Addresses
In IPv6, systems that assign themselves an address automatically create a link-local unicast address, which is the equivalent of an APIPA address in IPv4.
All link local addresses have the same network identifier: a 10-bit FP of 11111110 010 followed by 54 zeroes, resulting in:
fe80:0000:0000:0000/64
In its more compact form, the link-local network address is:
fe80::/64

## Slide 31: Unique Local Unicast Addresses
These are the same as private addresses in IPv4, with the following format:
Global ID: A 48-bit field beginning with an 8-bit FP of 11111101 in binary, or fd00::/8 in hexadecimal. The remaining 40 bits of the global ID are randomly generated.
Subnet ID: A 16-bit field that organizations can use to create an internal hierarchy of sites or subnets.
Interface ID: A 64-bit field identifying a specific interface on the network.
Notes: Review the principles of private addressing as in IPv4.

## Slide 32: Unique Local Unicast Addresses
The IPv6 unique local unicast address format

## Slide 33: Special Addresses
Loopback address: Any messages sent to it are returned back to the sending system.
0:0:0:0:0:0:0:1 or ::1
Unspecified address: The address the system uses while requesting an address from a DHCP server.
0:0:0:0:0:0:0:0

## Slide 34: Multicast Addresses
Multicast addresses always begin with an FP value of 11111111, in binary, or ff in hexadecimal. The entire multicast address format is as follows:
FP: An 8-bit field that identifies the message as a multicast.
Flags: A 4-bit field that specifies whether the multicast address contains the address of a rendezvous point (0111), is based on a network prefix (0010), and is permanent (0000) or transient (0001).
Scope: A 4-bit field that specifies how widely routers can forward the address. Values include interface-local (0001), link-local (0010), site-local (0101), organization-local (1000), and global (1110).
Group ID: A 112-bit field uniquely identifying a multicast group.
Notes: Note that IPv6 has eliminated broadcast messages, but can use a Multicast to all hosts in a similar way.

## Slide 35: Anycast Addresses
Used to identify the routers within a given address scope and send traffic to the nearest router, as determined by the local routing protocols.
Can be used to identify a particular set of routers in the enterprise, such as those that provide access to the Internet.
To use anycasts, the routers must be configured to recognize the anycast addresses.
Notes: Review the example Anycast address that corresponds to the sample network used in previous examples from the book.

## Slide 36: Assigning IPv6 Addresses
As with IPv4, a Windows computer can obtain an IPv6 address by three possible methods:
Manual allocation: A user or administrator manually supplies an address and other information for each network interface.
Self-allocation: The computer creates its own address using a process called stateless address autoconfiguration.
Dynamic allocation: The computer solicits and receives an address from a Dynamic Host Configuration Protocol (DHCPv6) server on the network.
Notes: Explain each of these methods in more detail and refer to the IPv4 properties sheet on the next slide.

## Slide 37: Assigning IPv6 Addresses
The Internet Protocol Version 6 (TCP/IPv6)
Properties sheet

## Slide 38: Planning an IP Transition
Lesson 10: Configuring IPv4 and IPv6 Addressing
Notes: Lecture notes go here

## Slide 39: Planning an IP Transition
Administrators are reluctant to change from IPv4 to IPv6 because there is a lot to learn.
IPv4 hardware is still functioning.
The Internet is still mostly IPv4, but there is a gradual transition happening where there will be support for both IP versions.
Currently, we must have mechanisms in place to transmit IPv6 traffic over IPv4 connections, but the situation will be reversed in the future.

## Slide 40: Using a Dual IP Stack
The simplest way to transition is to run both IP versions.
Windows has been doing this since Windows Server 2008 and Windows Vista.
Use ipconfig /all to see IPv6 configuration.
This allows us to communicate with IPv4 and IPv6 devices at the same time.

## Slide 41: Tunneling
Tunneling is the process by which a system encapsulates an IPv6 datagram within an IPv4 packet.
Often used for router-to-router communication when communicating between two IPv6 networks over an IPv4 connection.

## Slide 42: Tunneling
Two IPv6 networks connected by an IPv4 tunnel

## Slide 43: Configuring Tunnels Manually
It is possible to manually create semi-permanent tunnels that carry IPv6 traffic through an IPv4-only network. When a computer running Windows Server 2012 R2 or Windows 8 is functioning as one end of the tunnel, you can use this command:
netsh interface ipv6 add v6v4tunnel “interface” localaddress remoteaddress
In this command, interface is a friendly name you want to assign to the tunnel you are creating and localaddress and remoteaddress are the IPv4 addresses forming the two ends of the tunnel. An example of an actual command would be this:
netsh interface ipv6 add v6v4tunnel “tunnel” 206.73.118.19 157.54.206.43

## Slide 44: Configuring Tunnels Automatically
A number of mechanisms automatically create tunnels over IPv4 connections. These technologies are designed to be temporary solutions during the IPv4-to-IPv6 transition:
6to4: Incorporates the IPv4 connections in a network into the IPv6 infrastructure by defining a method for expressing IPv4 addresses in IPv6 format and encapsulating IPv6 traffic into IPv4 packets.
ISATAP (Intra-Site Automatic Tunnel Addressing Protocol): An automatic tunneling protocol used by the Windows workstation operating systems that emulates an IPv6 link using an IPv4 network.
Teredo: A mechanism that addresses the issue of NAT routers not supporting 6to4 by enabling devices behind non-IPv6 NAT routers to function as tunnel endpoints.
Notes: Use the information in the book to expand on these mechanisms as necessary

## Slide 45: Lesson Summary
The IPv4 address space consists of 32-bit addresses, notated as four 8-bit decimal values from 0 to 255, separated by periods (e.g., 192.168.43.100). This is known as dotted decimal notation, and the individual 8-bit decimal values are called octets or bytes.
Because the subnet mask associated with IP addresses can vary, so can the number of bits used to identify the network and the host. The original Internet Protocol (IP) standard defines three address classes for assignment to networks, which support different numbers of networks and hosts.
Because of its wastefulness, classful addressing was gradually made obsolete by a series of subnetting methods, including variable-length subnet masking (VLSM) and eventually Classless Inter-Domain Routing (CIDR). CIDR is a subnetting method that enables administrators to place the division between the network bits and the host bits anywhere in the address, not just between octets.
Notes: Lecture notes go here

## Slide 46: Lesson Summary
When a Windows computer starts, it initiates the IPv6 stateless address autoconfiguration process, during which it assigns each interface a link-local unicast address.
The simplest and most obvious method for transitioning from IPv4 to IPv6 is to run both, and this is what all current versions of Windows do.
The primary method for transmitting IPv6 traffic over an IPv4 network is called tunneling—the process by which a system encapsulates an IPv6 datagram within an IPv4 packet.
Notes: Lecture notes go here

## Slide 47
Copyright 2013 John Wiley & Sons, Inc.
All rights reserved. Reproduction or translation of this work beyond that named in Section 117 of the 1976 United States Copyright Act without the express written consent of the copyright owner is unlawful. Requests for further information should be addressed to the Permissions Department, John Wiley & Sons, Inc. The purchaser may make back-up copies for his/her own use only and not for distribution or resale. The Publisher assumes no responsibility for errors, omissions, or damages, caused by the use of these programs or from the use of the information contained herein.