## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors” Fall – 2015 (1st Sem. 1436-7H)
Applied Anthropometry, Work-Space Design
Part I – Anthropometry
(Chapter 13)
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Lesson Overview
Introduction
Anthropometry
  Static Dimensions
  Dynamic (Functional) Dimensions
  Discussion: Static, Dynamic Dimensions
Use of Anthropometric Data
  Principles in the Application of Anthropometric Data
    Designing for Extreme Individuals
    Designing for Adjustable Range
    Designing for the Average
    Discussion of Anthropometric Design Principles

## Slide 3: Introduction
Poor design features of tools, facilities, e.g.:
  uncomfortable chairs
  high shelves
  too low or too high sinks
  clothes too tight/loose in certain parts
  equipment with no space to insert repair tool
Failure to design equipment, facilities to fit people’s physical dimensions ⇒
  not suitable to human use
  physiological disorders, diseases:
    e.g. poorly designed seats ⇒ back injury, muscle aches, pain: neck + shoulder, leg circulatory problems
Chapter: designing tools to fit physical dimensions of people, with emphasis on:
  seats, seated workstations

## Slide 4: Anthropometry
Defn: “measurement of humans for purposes of understanding human physical variation”
Involves measurement of:
  body dimensions
  other body physical characteristics, e.g.:
    volumes
    center of gravity
    masses of body segments
Body dimensions
  applies to wider range of design problems (here)
  types of body measurement:
    static
    dynamic (functional)
Engineering Anthropometry:
  applying these 2 types of data to designing objects

## Slide 5: Cont. Anthropometry
Static Dimensions
Defn: measurements taken when body is in fixed (static) position
Consist of:
  skeletal dimensions (bet. centers of joints e.g. bet. elbow & wrist)
  contour dimensions (skin-surf. dimensions e.g head circum.)
Many dimensions can be measured:
  NASA Anthropometric Source Book: 973 measurements from 91 worldwide surveys
Dimensions applications (many):
  specific applications (helmets, earphones, gloves)
  general utility of measuring certain body features:
    figure 13-1 + table 13-1 (next 2 slides)
“head-measurer”: tool used for research early 1910s (Wikipedia)

## Slide 6: Cont. Anthropometry
Cont. Static Dimensions
Figure below: structural (static) body features
Notice: reference can be:
  ground (1), or 2 body parts (11), or ends of the same body part (9,13)

## Slide 7: Cont. Anthropometry
Cont. Static Dimens.
Table: selected body dimensions and weights of US adult civilians
Dimensions 1-15 shown in last slide
Questions:
  How would this compare to Saudi body dimensions?
  What factors affect these dimensions?
  What is the meaning of “percentile”?

## Slide 8: Cont. Anthropometry
Cont. Static Dimensions
Percentile :
  Defn:“a value on a scale of 100 that indicates the percent of a distribution that is equal to or below it”
  Examples from last slide: male stature (which dim.?)
    5th percentile of standing males: 63.7 in (i.e. 162 cm) ⇒ only 5% of males heights (US: 20-60) are ≤ 63.7 in
    50th percentile of male height: 68.3 in (i.e. 173 cm) ⇒ 50% of males are shorter (or taller) than 68.3 in i.e. median of male heights (US: 20-60): 68.3 in (why?)
    Q: what is 95 percentile of US male sitting height?
    Q: what %ge of US females (20-60) weigh > 89.9 kg
  Interquartile range
    middle 50% of distribution: i.e. 25th – 75th percentiles
    this is measure of variability

## Slide 9: Cont. Anthropometry
Cont. Static Dimensions
Cont. Percentile :
  Figure below: percentiles in normal “bell” curve
  Percentiles = sum of area (∫) under normal curve

## Slide 10: Cont. Anthropometry
Cont. Static Dimensions
Body dimensions vary with:
  sex (males and females): next slide
  ethnicity (whites, blacks, Asians, etc.): next slide
  age:
    generally lengths, heights ↑ until late teens/early 20’s
    then remain relatively constant through adulthood
    then ↓: early-middle adulthood into old age
    Did you know: exception is ear (continues all life long!)
  occupation (i.e. job)
    caused by:
      imposed height and/or weight restrictions
      physical activity involved in work
      self-selection of applicants for practical reason (?)
    e.g. truck drivers: taller, heavier > general population
  times: US, Eur. ht. ↑ 1 cm/decade:1880-1960 (?)

## Slide 11: Cont. Anthropometry
Cont. Static Dimensions
Cont. Body dimensions variations:
  Sex (left figure): comparison showing overlap in male 5th %ile with female 95th %ile heights (huge!)
  Ethnicity: (right figure): comparison showing 5th-95th %ile among different male heights

## Slide 12: Cont. Anthropometry
Dynamic (Functional) Dimensions
Defn: measurements taken while body is engaged in some physical activity; e.g.
  operating a steering wheel
  assembling a toy
  reaching across the table for salt, etc.
Individual body members function mostly in concert
  i.e. all parts are affected together, at the same time
  e.g. limit of arm reach involves
    arm length, but also:
    shoulder movement
    trunk rotation (possible)
    back bending (possible)
    hand function

## Slide 13: Cont. Anthropometry
Cont. Dynamic (Functional) Dimensions
Somatography: diagram showing interaction of various body members
  e.g. below: 3 views (front, side, top) for forklift truck operator

## Slide 14: Cont. Anthropometry
Discussion: Static, Dynamic Dimensions
Anthropometric data
  Static data exists » dynamic data
  However, dynamic data: more representative of actual human activity
Converting static data to dynamic data
  No systematic procedure available
  However, following recommendations are helpful:
    Heights (stature, eye, shoulder, hip): reduce by 3%
    Elbow height: no change, or ↑ by 5% if elevated at work
    Knee or popliteal height, sitting: no change, except with high-heel shoes
    Forward and lateral reaches:
      ↓ by 30 percent for convenience
      ↑ by 20 percent for extensive shoulder and trunk motions
    Note, these estimates may change: e.g. work condition

## Slide 15: Use of Anthropometric Data
Which anthropometric data to use?
  Data should be representative of population that would use the designed item
  If designing for “everyone”⇒ the design features must accommodate as many people as possible
  If designing for specific groups ⇒ use data for your specific groups; examples:
    adult females
    children
    elderly (seniors)
    soccer players
    the handicapped (can you name more examples?)
    Note, many specific groups do not yet have available anthropometric data

## Slide 16: Use of Anthropometric Data
Principles in Application of Anthropometric Data
Three general principles
Each applies to different situation:
  Designing for Extreme Individuals
  Designing for Adjustable Range
  Designing for the Average

## Slide 17: Use of Anthropometric Data
Cont. Principles in Appl. of Anthropometric Data
Designing for Extreme Individuals:
  designs should try to accommodate everyone
  a single design dimension can be:
    limiting factor restricting use of facility for some
    a dictate for max./min. value of variable in question
  designing for max. population value:
    used if given max/high value of some design feature should accommodate –almost- all people
    examples: heights of doorways, strength of supporting devices (e.g. rope ladder, workbench, trapeze)
  designing for min. population value:
    used if given min/low value of some design feature should accommodate –almost- all people
    examples: distance of control button from operator; force required to operate the control

## Slide 18: Use of Anthropometric Data
Cont. Principles in Appl. of Anthropometric Data
Designing for Adjustable Range:
  equipment/facilities can have design features: adjustable to individuals who use them
    e.g.’s: automobile seats, office chairs, foot rests
  adjustments (e.g. arm reach) usu. cover range: 5th female - 95th male %tile of pop. characteristic
    ⇒ covers 95% (not 90%) of 50/50 male/female pop. (??)
    used when hard to cover extreme cases (100% of pop) due to resulting technical difficulties involved
  designing for adjustable range: preferred method of design, but is not always possible (why?)

## Slide 19: Use of Anthropometric Data
Cont. Principles in Appl. of Anthropometric Data
  Designing for the Average
  Designing for average generally not preferred:
    it should not just be “quick, easy way out” for design
    there is no “average” person
    person may be average on 1-2 dimensions but almost impossible on more than that:
      no perfect correlation exists between body dimensions
      e.g. people with short arms don’t have to have short legs
  When it is ok to design for average:
    in situations involving non-critical work (?)
    when not appropriate to design for extreme cases
    where adjustability is impractical
    e.g.: checkout counter at supermarket built for the average customer

## Slide 20: Use of Anthropometric Data
Cont. Principles in Appl. of Anthropometric Data
Discussion of Anthrop. Design Principle
  above principles apply to only single dimension
    e.g. arm reach (only), or stature height (only)
  considering > 1 dimension may cause “problems”
    taking 5th – 95th %ile on >1 dimension ⇒ eliminates high %ge of population
      on 13 dimen. ⇒ eliminates 52% (not just 10%) (Bittner, ’74)
      why? no perfect correlation exists bet. body dimensions
      ⇒imp. to consider body dimension combinations in design
    adding 5th or 95th %ile of body segments ≠ corresponding %ile value for combined dimension
      e.g. lengths: fingertip to elbow + elbow to shoulder ≠ fingertip to shoulder
      why? (again): no perfect correlation bet. body dimensions
      building 5th %ile female (ankle height, ankle to crotch, etc.) ⇒ female is 6 in (15.6 cm) < actual 5th %ile stature!

## Slide 21: Use of Anthropometric Data
Cont. Principles in Appl. of Anthropometric Data
Cont. Discussion of Anthrop. Design Principle
  articulated models
    AKA: articulated anthropometric scale models
    physical models (i.e. full-scale mockup)
    represent specific population %ile
    usu. used with work-space design (see right)
    note, computer software also exists to model work-space design

## Slide 22: Use of Anthropometric Data
Cont. Principles in Appl. of Anthropometric Data
Suggested Procedure for Using Anth. Data
  Determine body dimensions important in design
    e.g. application: sitting height or stature height?
  Define population to use facility/equipment
    establishes dimensional range to be considered
    e.g. children, women, Saudi men, world population)
  Determine principle to be applied
    i.e. extreme individuals, adjustable range, average?
  Select %ge of pop. to be accommodated (e.g. 90%)
  Find appropriate anthropometric data tables for chosen population used, extract relevant values
  Add appropriate allowances (e.g. clothing, shoes)
  Build full-scale mock-up of facility/equipment, have representative people of large and small users (of the population) test it (very important!)