## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors” Fall – 2015 (1st Sem. 1436-7H)
Applied Anthropometry, Work-Space Design
Part II - Design of Work Surfaces
(Chapter 13)
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Lesson Overview
Design of Work Surfaces
  Horizontal Work Surface Area
  Work-Surface Height
    Seated
    Standing

## Slide 3: Design of Work Surfaces
Important use of anthropometric data: work space
Work-space envelope (Defn): 3-D space within which individual works
  Involves mostly space where hands can move
  Within envelope, design decisions must be made about features of the workspace, e.g.
    location and design of benches, desks, tables, and control panels
  Discussed here samples of work surfaces: horizontal, vertical

## Slide 4: Horizontal Work Surface Area
This is area used by:
  Seated worker
  “Sit-stand” worker
Area should allow for manual activities within “convenient” arm reach (what is convenient?)
Research on horizontal work surface area:
  Barnes (1963) and Farley (1955):
    Shown in next slide (carefully examine dimensions)
    Normal Area: area conveniently reached by forearm (while upper arm hangs in natural position)
    Maximum Area: area reached by extending the arm from the shoulder
  Squires (1956): suggests “optimal area”: takes into account dynamic interaction of forearm movement as the elbow is also moving (also shown next slide)

## Slide 6: Cont. Horizontal Work Surface Area
Cont. Research on horiz. work surface area
  Squires (optimal) area vs. Farley area (normal-max.)
    Squires area more shallow but covers more area
    Squires area requires less forearm extension ⇒ minimal stress on elbow joint
  Ayoub (1973): suggests “optimal work” area:
    approx. 25 * 25 cm (see next slide; note similarities)
    located @ 10 cm from the table edge
    body mid-line crossing at the middle of the area
    Source [Pheasant textbook];

## Slide 8: Cont. Horizontal Work Surface Area
Cont. Research on horiz. work surface area
  Bridger (1988): slanted working surface is better:
    trunk: less motion –upright- (vs. horizontal)
    neck: less bending
    also less fatigue and discomfort
    slant (here) = 15º
    slant (other research): 12º and 24º
    applications:
      Visual tasks (e.g. reading)
      Can you name any dis- advantages of slanted surfaces?

## Slide 9: Work-Surface Height
Height of work surface:
  Can cause backaches, neck aches, shoulder pains
  Too low ⇒ back is bent over too much
  Too high ⇒ shoulders raised over relaxed posture ⇒ discomfort in shoulder and neck
Work-surface height vs. working height
  Work-surface height:
    height of upper surface of table, bench, desk, etc.
    measured from the floor
    for slanted surface: need height of front edge + angle
  Working height
    Depends on what operator is working on
    e.g. writing paper ⇒ working ht. = work-surface ht.
    e.g. writing on keyboard ⇒ working ht. = ht.: “asdfg…”
    how about when washing vegetable in a sink?

## Slide 10: Work-Surface Height: 1. Seated
Seated Work-Surface: Height & Arm Posture
  Work surface height is affected by:
    Arm posture
    Seat height
    Thickness of the work surface (which affects …?)
    Thickness of the thighs
  As work-surface height ↓ ⇒
    More relaxed posture of upper arms (@ working ht.)
    Elbows are at 90º (with respect to working ht.)
    Wrists are straight
    Overall comfortable working (shoulders, spine, etc.)
    Beneficial for repetitive tasks (e.g. typing, assembly)
  Common desk work-surface heights
    76 cm (30 in)
    Research: recommend reduction to 72 cm, 68.6 cm

## Slide 11: Cont. Work-Surface Height: 1. Seated
Seated Work-Surface: Height & Thigh Clearance
  Thigh clearance:
    Determined by dist. bet. seat & work surface bottom
      Design here for max, min, average, adjustable?
    Non-adjustable height work surface
      ANSI: 26.2 in (66.5 cm) as min. ht. of bottom
    Small users
      raise seat so elbows are at 90º to work surface
      ⇒ feet don’t touch floor
      ⇒ foot rest is needed to support feet
      or use adjustable-height work surface
    Adjustable-height work surface
      ANSI: 51.3 – 66.5 cm for bottom of work surface

## Slide 12: Cont. Work-Surface Height: 1. Seated
General Principles for Seated Work Surfaces:
  Best to find work surfaces with adjustable height (e.g. adjustable computer tables)
  Best if work surface is such that elbow height = working height
  Work surface should provide enough clearance for people with thick thighs
  Recomm. seated work surface ht. for different tasks:

## Slide 13: Work-Surface Height: 2. Standing
Factors governing standing work-surface ht
  Elbow height
  Type of work
Type of work vs. elbow height (next slide):
  Light and heavy work: work-surface height: below elbow height
  Precision work:
    work-surface height: slightly above elbow height
    Reason: to support elbow while performing work
    but recommended: sitting down for precision work
  Fixed vs. adjustable standing work surface height
    Fixed: designed for max. (i.e. tallest) users
    Shorter users:
      either use a platform to account for height difference
      or use adjustable ht. (e.g. electric, manual, hydraulic)

## Slide 15: Cont Work-Surface Height: 2. Standing
Other recommendations:
  Work height: too high ⇒ shoulders & upper limbs raised ⇒ fatigue, strain on shoulder muscles
  Work height: too low ⇒ trunk, neck, head: inclined forward ⇒ stress on spine
  Recommended hts. for different tasks: below for fixed vs. adjustable ht (and for male, female)