## Slide 1: Predetermined Motion Time Systems
Sections:
Overview of Predetermined Motion Time Systems – part 1
Methods-Time Measurement – part 2
Maynard Operation Sequence Technique

## Slide 2: Predetermined Motion Time Systems
Methods-Time Measurement

## Slide 3: Methods-Time Measurement
MTM is used to:
  analyze method for performing a given task
  set a time standard for the task
Definition:
“Procedure which analyzes any manual operation or method into the basic motions required to perform it and assigns to each motion a predetermined time standard which is determined by the nature of the motion and the conditions under which it is made”

## Slide 4: Methods-Time Measurement
“Methods-Time” hyphen shows connection bet.:
  basic motions used to perform a task
  time values associated with these motions
Note, should not be calculated until:
  task is divided into its component elements
  then determining if methods improvements can be made (step 3 in PMTS procedure)

## Slide 5: Methods-Time Measurement
MTM versions:
  MTM is family of PMT systems
  MTM-1
    original MTM
    first-level PMTS upon which all of the other MTM systems are based
  MTM is a family of products available through the MTM Association in Des Plaines, Illinois
Notes: Web site can be accessed at www.mtm.org

## Slide 6: MTM-1
MTM basic motions
  Operates at BME level in pyramidal structure of work
    Most MTM-1 BME’s involve hand and arm movements
    Also: BME’s for eye, leg, foot, and body actions
  Many BME’s correspond to original therbligs developed by Frank Gilbreth
  However, changes include:
    Adjustments to conform to needs of MTM
    Adding new elements not included in original therbligs

## Slide 7: Methods-Time Measurement

## Slide 8: MTM-1
TMU’s:
  time measurement units
  developed by studying motion pictures of work activity
  TMU is now defined as:
Notes:   * time per frame of motion picture film

## Slide 9: MTM-1
Table 3: defines the MTM-1 motion elements
Table 4: tabulation of time values*
Steps for MTM:
  Step 1: analyst describes task in terms of these BME’s
    taking note of:
      work variables that influence element time
      accounting for simultaneous right-hand and left-hand motions
      internal elements when task involves operation of machine, etc.
Notes:   * Table 3 and Table 4 are available on the course website

## Slide 10: MTM-1
Cont. Steps for MTM:
  Step 2:
    analyst retrieves time for each BME*
    normal time for task:
    analyst then adds according to company policy work being measured:
    note, analyst must first receive proper training in technique
Notes:   * Solve example: find TMU for M6B10 (see table 3, pg. 367)

## Slide 11: Other MTM Systems
Additional MTM systems added:
  serve specific work situations:
    clerical activity
    machine shop work
    electronic testing
  second- and third-level systems:
    reduce time required to develop
  several computerized systems have been developed based on MTM*
Notes: MTM Web site: www.mtm.org

## Slide 12: Other MTM Systems
MTM-2 – Second-level PMTS in which basic motion elements are combined into motion aggregates
  GET – combines Reach and Grasp
  PUT – combines Move and Position
MTM-3 – Third-level PMTS which has four motion categories
  Handle
  Transport
  Step and foot motions
  Bend and arise

## Slide 13: Other MTM Systems

## Slide 14: Other MTM Systems