## Slide 1: Low Level Laser Therapy (LLLT)
Mohammed TA Omar Ph.D. PT

## Slide 2: Objectives of lecture
Define laser and explain its physical principle of laser.
Explain the physical characteristics of laser.
Describe the classifications of laser.
Contrast the characteristics of helium neon and gallium arsenide low power laser.
Analysis the therapeutic application of laser in different conditions.
Demonstrate the application techniques of low power laser.
Describe the precautions and contraindications for low power laser.

## Slide 3: What Is Light Therapy?
*Light energy is a form of electromagnetic energy that has wavelength between 100-10.000nm, and contain tiny “Energy packets” called photons.
Each photons cantinas definite amount of energy depending on its wavelength and may be one of the following
  Laser
  Light emitting diodes (LED)
  Super-luminous diodes (SLD)
  Infrared
  Ultraviolet

## Slide 4: What Is Laser Therapy?
LASER is acronym of
Light : an electromagnetic
Amplification by
Stimulated
Emission of
Radiation
Notes: Light: Electromagnetic radiation that can produce a visual sensation•
Amplify: To increase in size, volume,
Stimulate: To excite or invigorate; to encourage or provoke something to grow, develop, or become more active•
Emission: release of electrons from parent atoms•
Radiation: The transfer of energy in the form of rays, waves, or particles, often from a central source; also called radiant energy

## Slide 5: Characteristics of Laser Radiation
Monochromaticity: refers to one color or one wavelength , and one frequency of laser light.
Coherence: The wavelengths are in phase (synchronizing)
Collimation (parallelity): All laser lights have minimal degree of divergence over distance. (non divergence)
Notes: All photons in:
White light is made up of a different colors
LED one color (monochromatic) but waves not in phase (non-coherent )
Laser light is one color, one wavelength, one frequency
Coherence:
Temporal coherence:: All photons of light travel in the same phase (time)
Spatial coherence: All photons of light travel in the same direction ( distance).
The advantage of collimation and coherence of light for therapy is the ability to make the beam focus on a very precise small target

## Slide 6: Production and components of Laser
There are 4 main components to a laser
Notes: Stimulated Emission principle
The concept of stimulated emission was postulated by Einstein and is the essential to the working principle of laser .It stats that a photon released from an excited atom would simulate another similarly excited atom to de –excite itself by releasing an identical photon .
The triggering photon would continue on its way unchanged, and the subsequent photon released would be identical in frequency, directions, and phase.
These two photons would promote the release of additional photons as long as other excited atoms were present.
Absorption : Incident photon(p) is absorbed by resting electron(e), which moves to higher level(E3).
Spontaneous emission: Excited electron drops to lower resting level (E1) emitting single photon (p)
Stimulated emission: Incident photon interacts with already excited electron to produce two identical photons (p1& p2)

## Slide 7: Production and components of Laser
Optical resonant cavity:
  Contains lasing medium which is surrounded by two parallel mirrors at either end. One mirror has 100% reflectance while the other has slightly less reflectance.(stimulation and amplification)
Lasing medium:
Material that excited to generates laser light
(gas, solid, semiconductors & liquid)
Power supply: 10,000 volts & 100’s amps.
Pumping system
  Applicator (laser probe):
  Single applicator
    Multiple applicator (SLDs and LID)
Notes: High voltage, photoflash lamps, radio-frequency oscillators.
Pumping is used to describe the process of elevating an orbiting electron to a higher, excited energy level.
The laser applicator, also sometimes referred to as a probe, is used to direct the photons (light energy) into the patient

## Slide 8: LASER Classification (Safety)
Class | Power level | Power (mW) | Example | Dangerous and safety
Class 1 | Very low | <0.05mw | Laser printer, CD players Supermarket reader | No effect on eye & skin.
Class II | Low | <1mw | Laser pointer | Safe to skin
Class III-a | Low | <5mW | Laser pointer, low LLLT | Safe to skin Not to eyes
Class III-b | Medium | <5-500mW | LLLT | 
Lass IV | Hot | >500mW | Hot Laser (surgical) | Unsafe to skin & eye
Notes: Safety is determined by the amount of energy applied to the lasing medium and the subsequent amount of energy released in the form of light—in other words, the power of the laser. The greater the power of the laser, the greater the potential danger
Laser equipment is grouped into four FDA classes with simplified and well-differentiated safety procedures for each
Low power lasers used in PT are categorized as Class II and III laser devices

## Slide 9: LASER Classification (lasing media)
Laser type | Lasing Media | Wavelength (nm) | Safety
Gas | He-Ne | 633 | 3a-3b
Gas | CO2 | 10.600 | 3b-IV
Gas | Argon | 488-514 | IV
Diode/ semiconductors | AlGaAs GaAs GaAl | 600-1000 | 3b
Excimer | Dimer | 351 | IV
Solid –state | Ruby Nd :YAG | 694 1060 | IV IV
Notes: Gas lasers: Use gas as a lasing medium. Helium and helium-neon (He-Ne) are the most common gas lasers.•
Diode or semiconductor lasers: Use semiconductors as the lasing medium. They can be either small and low-powered or large and high-powered.
Low-powered semiconductor lasers are those used in laser pointers, laser printers, and compact disc players. In fact, the 780-nm aluminum gallium arsenide (AlGaAs) laser diode, used in CD players, is the most common type of laser in the world. Large industrial diode lasers are capable of generating great amounts of heat and are used for cutting and welding.
Excimer lasers: Use a dimer as the lasing medium. (A dimer is a pseudo-molecule created by electrically stimulating a mixture of reactive gases, such as chlorine

## Slide 10: Characteristics of LASER, LED, & SLDs
 | LLLT | SLD | LED
Power | High | Medium | Low
Focus of light beam | Very focus | Moderately focus | Scattered
Penetration | Up to 5cm | Up to 1mm | Several mm
Notes: These devices have at least one true laser diode and, therefore have the capacity to emit a monochromatic, collimated, and coherent light beam.
The laser beam is highly focused and typically higher powered than the SLD or LED. The depth of penetration into tissue is greater (up to 5 cm), than the SLD and LED. Clinically, it is believed to be the light source of choice to treat deeper lying tissue. The laser property of collimation allows the laser beam to maintain a small spot size (less
Super luminous diodes are not true lasers. They emit a beam of light that is fairly monochromatic and moderately collimated. However, the SLD can not be referred to as a laser because it does not meet the third criteria of being coherent. The clinical significance of coherence is still being investigated and is a current area of debate in the literature. The super luminous diode emits light which is non-coherent. The SLD light beam is less focused than the laser diode, but more focused than the LED. Super luminous diodes typically have lower power levels (mW) than laser diodes. The SLD depth of penetration (up to 1 cm) is less than the laser diode, but greater than the LED. Hence, in clinical practice it is best suited for the treatment of superficial tissue.
Light emitting diodes, like SLDs are not true lasers. They emit a beam of light that is non-collimated (less focused) and non-coherent. Light emitting diodes have lower power levels (mW) than laser diodes. The LED depth of penetration (up to several mm) is the least of the three light sources. In clinical practice it is indicated for the treatment of very superficial tissue.

## Slide 11: High vs. Low Level Lasers
  High (500-10000mW)
  Surgical Lasers
  Hard Lasers
  Thermal
  Used for
  -Ophthalmology
-Dermatology
-Oncology
-Vascular specialties
Low (1-500mW)
  Medical Lasers
  Soft/ cold Lasers
  Sub-thermal
  Used for;
-Pain relieve
-Wound healing
-Anti/ or pro-inflammatory
  Maximum output of (90mW or less)
  Wavelength (600-1000nm )
  Penetration of (3-4mm).

## Slide 12: What’s in a Name?
Therapeutic Laser
Low Level Laser Therapy
Low Power Laser Therapy
Low-energy Laser
Soft Laser
Low-reactive-level Laser
Low-intensity-level Laser
Photo-bio-stimulation Laser
Photo-biomodulation Laser
Mid-Laser
Medical Laser
Bio-stimulating Laser
Bio-regulating Laser

## Slide 13: LLLT Treatment Parameters
Patients Parameters
Laser Parameters
Wavelength (nm)
Power (mw)
Mode (continuous/pulsed)
Energy density(J/cm2)
Treatment duration
Treatment frequency
Medical history and diagnosis
Vascularity of target tissues
Stage of injury (acute/chronic0
Skin type and pigmentation
Medications
Applications Techniques

## Slide 14: Laser Parameters: Wavelength
Longer wavelength deeper penetration
  Red visible laser Superficial conditions
  He-Ne (wavelength=632nm)
  Used for Superficial wound, ulcer
  Superficial trigger point
  Absorption of He-Ne occurs within first 2-5 mm of soft tissue with an indirect effect of up to 8-10 mm
  IR Laser “Deep conditions;
  Ga-As (wavelength=904nm) and
  (Ga-Al-As (wavelength=780-890nm)
  Use for Deep wound, edema (acute &chronic),
  Deep trigger point, & scar tissue
  IR laser has a longer wavelength directly absorbed at depths of 2-4 cm and has indirect effect up to 5 cm.

## Slide 15: Laser Parameters: Power
Power is defined as the rate of energy flow and measured in watts (mW) where (1watt=1J/second)
    Low-power lasers (1-5mW)
    Medium-power (5-500mW)
    High-power lasers (> 500mW)
Power Density (PD) is the amount of power per unit area of the beam (spot size), and measured by W/cm2 or mW/cm2.
= mW/cm2
Notes: Takes into consideration the actual beam diameter or spot size (cm2).
    If light spread over lager area = lower power density
    If light spread over smaller area = higher power density
    Beam diameter determines power density.
When laser or light applicators includes number of diodes, the power of application is equal to the sum of the power of all its diodes and the power density is equal to total power divided by total area

## Slide 16: Laser Parameters: Energy
Energy (joules): Energy is the power multiplied by the treatment time, and is measured by Joule (J or mJ)
  Energy (J) =Power output (W) X Treatment Time (s)
Energy Density (dosage) is the amount of energy per unit of area, and is measured in Joules/cm2 .
= J/cm2

## Slide 17: Laser Parameters: Energy
Recommended Dosage Range
  Therapeutic response = 0.01-10 J/cm2 (average 6J/cm2)
    Open wounds – 0.5-1.0 J/cm2
    Intact skin – 2.0-4.0 J/cm2
  Too much – suppressive effect >10 J/cm2
Notes: There are over 2000 published studies on LLLT. The methodology and quality of these studies varies dramatically, however it is important to note that a large percentage of these studies demonstrated positive therapeutic outcomes, including over 100 double blind studies

## Slide 18: Exercises

## Slide 19: Exercises

## Slide 20: Laser Parameters: Mode
The power on most LLLT devices can be periodically interrupted for a very brief period on time. This is called “pulsing”.
When pulsed mode is used the average power delivered will decrease proportional to the pulse frequency that is selected.
In continuous mode: Average power= Peak power
In pulsed mode the Average power calculated as:
Average power = Pulse rate X Peak power X Pulse width
=100Hz X 2WX (2x10-7 seconds)=0.04mW

## Slide 21: Laser Parameters Treatment frequency
Evidence Recommended the followings;
  Treatment should be individualized
  3-4 times/week with moderate dose are more effective than higher dose for fewer time per week
  Acute conditions should be treated more frequently than chronic
  Laser therapy has accumulative effect

## Slide 22
Parameters | Helium Neon Lasers | Gallium Arsenide
Laser type | Gas | Semiconductor
Emitting radiation | Red (visible) light | IR (invisible) laser
Wavelength | 632.8 nm | 904–910 nm
Pulse rate (frequency) | continuous | 1-1000Hz
Pulse width | continuous | 200nsec
Peak power | 1-2mW (25mW) | 1-5mW
Average power | 1.0mW | 0.04-0.4mW
Beam area | 0.01cm | 0.07cm
Depth of penetration | 0.5-1 cm | 2cm up to 5 cm
Used | Superficial wound | Deeper tissue

## Slide 23: Physiological effects of LASER
Therapeutic laser-tissue interaction is essentially ATHERMIC.
The main type of reaction with tissue during laser therapy would appear to be PHOTOCHEMICAL.
So, Laser light absorbed by irradiated tissue produce chemical rather than thermal energy.

## Slide 24: What LASER do?

## Slide 25: Main area of LASER Application

## Slide 26: Physiological effects of LLLT
These chromophores may be:
    Enzymes
    Membrane molecule
    Cellular or extracellular substances,
Activation of these chromophores by laser light is thought to be responsible for laser bio-stimulation effect.
The absorption of laser light take place in tissues photoreceptors known as chromophores .
Notes: Numerous examples of chromophores exist in nature, such as
Chlorophyll in plants,
Bacteriochlorophyll in bluegreen algae,
Flavoproteins, and hemoglobin found in red blood cells., and Cytochrome c in mitochondria

## Slide 27: Physiological effects of Laser
Bio-stimulation – improved metabolism, increase of cell metabolism
• Increases speed, quality & tensile strength of tissue repair
Improved blood circulation & vasodilation
• Increases blood supply
Increases ATP production
Analgesic effect
• Relieves acute/chronic pain
Anti-inflammatory & anti-edematous effects
• Reduces inflammation

## Slide 28: Physiological effects of Laser
Stimulation of wound healing
• Promotes faster wound healing/clot formation
• Helps generate new & healthy cells & tissue
Increase collagen production
• Develops collagen & muscle tissue
Increase macrophage activity
• Stimulates immune system
Alter nerve conduction velocity
• Stimulates nerve function
Notes: Stimulation of endogenous opiates, nitric oxide, and serotonin
Modulate prostaglandin levels which may lead to a decrease in the chemical inflammatory mediators that irritate free nerve endings
Alter nerve conduction velocities, leading closing gating mechanism (gate control theory) causing relieves of acute/chronic pain

## Slide 29: Tissue & Cellular Response
Notes: Diagram that illustrates the mechanism of low-level light therapy (LLLT) on the cellular and molecular level. Near infrared light, absorbed by the mitochondria, causes upregulation of the cellular respiratory chain. A host of downstream cellular responses involving nitric oxide, reactive oxygen species, and cyclic adenosine monophosphate ensues, which ultimately dictates LLLT effects.
nuclear factor-κB [NF-κB] and

## Slide 30: Tissue & Cellular Response
Magnitude of tissue’s reaction are based on physical
characteristics of:
Output wavelength/frequency
Density of power
Duration of treatment
Vascularity of target tissues
• Direct effect - occurs from absorption of photons
• Indirect effect – produced by chemical events caused by
interaction of photons emitted from laser & the tissues

## Slide 31: Indications
Pain control ; (acute & chronic)
  Pain secondary to soft tissue injuries ( sprain. Strain, bursitis)
  Osteoarthritis, Rheumatoid Arthritis, & low back pain
  Neurogenic Pain (trigeminal , post-herpetic, neuralgia)
  Acupuncture & trigger point pain application.
Soft tissue healing in following conditions;
  Pressure Ulcers, Diabetic foot
  Burn wound
  Postoperative wound care.
  Fracture healing ?
Inflammatory conditions
  Post traumatic peripheral nerve injury.
  Edema reduction
  Scar tissue remodeling .

## Slide 32: Contraindications & Precautions
  Application over eyes
  Over or around Cancer
  Over pregnant uterus
  Over & around thyroid gland & endocrine glands
  Patients who pre-treated with photosensitizers drugs
  Over area or radiotherapy
  Over cardiac region
  Vogues nerve
  Growth plates in children
  Fever
  Infected tissue
  Epilepsy
  Confused/disoriented patients

## Slide 33: Application Techniques: Indirect contact
This technique is used in treatment of open wounds.
The distance between the laser probe and wound bed should be 0.5-1 cm.
The probe also should be held perpendicular to the site of radiation

## Slide 34: Application Techniques: Direct contact
Clean area prior to treatment
The tip of the probe is held perpendicular in contact with skin.
Allow deeper penetration and maximize the power density on the target tissues as reflection is minimized
Notes: Laser tissue penetration is enhanced by maintaining pressure on the skin surface with the emitter or probe. This helps displace capillary blood ow in the superficial tissues and decrease blood ow to the treatment area. This is desirable because photon penetration into the tissue is inversely proportionate to the amount of water content in the tissues. Blood has high water content so it will tend to absorb more of the photon energy. This will result in less penetration into the deeper tissues.
Phototherapy devices that utilize a combination of laser and LED/ IRED combinations should be used in direct contact with the skin for the additional reason that these non laser light sources are non-coherent and lose their focus as they are distanced from direct contact with the skin. Phototherapy devices that utilize a combination of laser and LED/ IRED combinations should be used in direct contact with the skin for the additional reason that these non laser light sources are non-coherent and lose their focus as they are distanced from direct contact with the skin.

## Slide 35: Application Techniques: Gridding
  Divide treatment areas into grids of square centimeters
  Hand held applicator in light contact with treatment area.
  Each square is stimulated for specific period of time
  (60-90seconds)

## Slide 36: Application Techniques: Scanning
  Scanning or back and forth movement for the duration of the treatment time
  No contact between laser tip and skin.
  Tip is held at variable distance 10-50 cm from treatment area
  As distance from target increases amount of energy decreases

## Slide 37: Application Techniques: Acupoint
It is used to irradiate localized painful spot.
Using hand held probe, one can use contact and non-contact technique.
It is commonly used in treatment of localized painful site, trigger points, and acupuncture points.
Notes: Treatment of occipital trigger point. Treatment of occipital trigger point.; The approach is to treat trigger points. This is accomplished by using a stationary contact on the trigger point as described above. The use of an algometer is benefcial to obtain a comparison of pain level prior to treatment and post treatment.
Acupoint stimulation of LI4 with special acupoint probe: The third treatment approach is acupuncture point stimulation or laserpuncture. There have been considerable numbers of studies performed on laser stimulation of acupoints. The emitter or probe can be placed over the acupoint or a special acupoint probe may be used, if available (see Figure 5).

## Slide 38
Better to underexpose than to overexpose
Begin treatment with minimal and gradually increase
Avoid direct exposure into eyes (If lasing for extended periods of time, safety glasses are recommended)
If icing – use BEFORE phototherapy • Enhances light penetration
If heating – use AFTER phototherapy • Decreases light penetration
Not recommended to combined US and LASER in the same sessions
Medication should be considered e.g. photosensitizers
Treatment consideration

## Slide 39: Patients Parameters of laser therapy
  Need medical history & proper diagnosis
      Diabetes – may alter clinical efficacy
  Medications
    Photosensitivity (antibiotics)
  Pigmentation
    Dark skin absorbs light energy better
  Clean skin surface
  Wearing goggles