## Slide 1: Bacterial Count

## Slide 2: Bacterial Count
Total bacterial count:
It determines the No. of both living and dead bacteria.
The common methods:
1- Nephelometric method.
2- Counting chamber method.
Viable bacterial count:
It determines the No. of living bacteria only.
The common methods:
1- Pour plate method.
2- Spread plate method.
3- Miles and Misra method

## Slide 3: Total bacterial count

## Slide 4: 1. Nephelometric Method
Nephelometry is method used for determining the amount of cloudiness or turbidity in a solution (Nephlometery used to determine the amount of light scattered by a suspension of cells).
HOW??
(Note: turbidity is particulate objects in a solution)
Particulate objects such as bacteria will scatter light, the amount of scattering is proportional to bacterial cells number.

## Slide 6: 2. Counting Chamber Method

## Slide 8
Notes: large central square with a 1 mm2 which can be seen with the 10X objective
This large central square is divided into 16 medium squares with the 40X objective can seen
When we put the sample under the coverslip, the cell suspension reaches a height of 0.1 mm. the volume will be: 1 x 1 x 0,1 = 0,1 mm3 = 10-4 ml
( 1 cubic mm = 0.001 ml)
If we have counted N cells in one of the large squares (that is, in 16 medium squares), the concentration of our sample will be: N x 10 4 cel/ml
When prior to counting we concentrated or diluted the initial sample, we must take into account the concentration-dilution factor (f):
N x 104 x f cel/ml

## Slide 10: Viable bacterial count

## Slide 11
Dilution= sample volume/ total volume
Serial dilution= (s.v/ t.v) x previous dilution

## Slide 12
Serial Dilutions of the Sample
If we take one ml of the original sample and add it to 9 ml of sterile normal saline, it will give 1:10 or 10-1 dilution of original sample, i.e. the original sample has been diluted to 1/10th.
Similarly we may prepare 1:100 (10-2), 1:1,000 (10-3), 1:10,000 (10-4) and so on dilutions of the original sample.

## Slide 13: 1. Pour Plate Method
This is the most commonly used method for counting of living bacteria in a wide variety of samples including milk, food, meat, soil etc.
There are two steps to the process:
Dilution and Plating

## Slide 14
Dilution:
Because of the huge number of bacterial colonies and their small size, counting the number of bacteria in a sample can be difficult.
So, bacterial samples must be diluted to obtain reasonable counts (make counting colonies on petri-dish easier).
The best range for colonies on a plate is about 25-300
For nearly all environmental samples, a dilution step is needed

## Slide 15
Plating
Plating of the dilutions so that each cell in the diluted sample may then grow and form colonies, that will in turn become visible to the naked eye and can be counted.
Plating is important because only living cells will be able to multiply and form colonies, then counted.

## Slide 17: Principle of Pour Plate Method
The sample should be diluted successively with sterile saline. The agar medium is maintained in molten state at 45° c.
One ml of each dilution is added to each sterile an empty labeled Petri dish, Then pour 9 ml molten agar (45°c) into above Petri dish.
The contents are thoroughly mixed, and allowed to solidify. The dishes are incubated at suitable temperature 37c.
After 24-48hrs , different kinds of microbes grow as separate colonies. Colonies are counted .

## Slide 18
Advantages :
Does not require previously poured plates
Less work, less risk of contamination
Anaerobes and facultative anaerobes grow within the agar
Disadvantages :
Heating could kill some organisms
Oxygen diffusion is not sufficient for obligate aerobes

## Slide 19: 2. Spread Plate (Surface) Method
Procedure:
1. Place (0.1ml) of each dilution onto solid agar.
2. Spread with sterile glass or metal spreader.
3. Incubate (minimum 24 hrs, usually 48 hrs).
4. Colonies are counted

## Slide 22: 3. Miles and Misra
Procedure:
1. Divide plate into 3 or 4 or 5 sections.
2. To each section ,deliver 1 drop of the corresponding dilution using Pasteur pipette (do not throw the pipette after finishing, calculate using 1ml of water, how many drops are delivered of 1 ml water).
3. Incubate the plate at 37c for 24 hrs.
4. Colonies are counted.

## Slide 24: Calculation of Bacterial Count
The aim is to calculate how many colony forming units (C.F.U.) of organism which present in the original sample.
Colony forming units (CFU) = number of bacteria that were able to replicate many times and give one single, visible colony.
(Colony: is a group of bacteria that grew from one original bacterium).
B = N/ V x D
B = number of bacteria N = number of colonies counted on a plate V= volume
D = dilution factor

## Slide 25: Calculation of Pour Plate Method
The number of colonies counted:100
B (no of bacteria in original sample)
B = 100 / 1 x 10-6
= 100 x 106 C.F.U/ ml
= 1 x 108 C.F.U/ml

## Slide 26: Calculation of Spread Plate Method
The number of colonies counted:50
B (no of bacteria in original sample)
B = 50 / 0.1x 10-6
= 50 x 10x 106 C.F.U/ ml
= 5 x 108 C.F.U/ml

## Slide 27: Calculation of Miles and Misra Plate Method
The number of colonies counted: 5
Note:1 ml of Pasteur pipette= 40 drops
B (no of bacteria in original sample)
B= 5 / 4x10-1 x 10-6
= 5x40x106 = 2X108C.F.U/ ml