## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors Engineering” Fall – 2016 (1st Sem. 1437-8H)
Manual Materials Handling
(Chapter 8)
part 2 – Case Studies
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Lesson Overview
Part 1:
What is MMH?
MMH Activities
MMH Effect on Health
NIOSH Lifting Equation
Part 2:
Case Studies
  Case 1: Effect of Frequency Factor on RWL
  Case 2: Effect of Horizontal Distance on RWL
  Case 3: Effect of Vertical Distance on RWL

## Slide 3: Case 1: Effect of Frequency Factor on RWL
Problem Statement: Analyze the following work task. A worker lifts 10 kg boxes from the conveyor to the cart, ten times every minute for two-hours.
6 sec

## Slide 4: Case 1: Effect of Frequency Factor on RWL
Solution: First, calculate the recommended weight limit (RWL) for the task
Determine the weight of the load. Weight = 10 kg
Assess the six components of lifting task.
H (Horizontal Distance) | 20 cm
V (Vertical Distance) | 75 cm
D (Lifting/ carrying Distance) | 0 cm
A (Angle) | 90°
F (Frequency) | 6 sec
C (Coupling/quality of grip) | fair

## Slide 5: Case 1: Effect of Frequency Factor on RWL
Select appropriate multiplier factors for each lifting component from the appropriate tables
H (Horizontal Distance) | 20 cm | HM | 1
V (Vertical Distance) | 75 cm | VM | 0.99
D (Lifting/ carrying Distance) | 0 cm | DM | 1
A (Angle) | 90° | AM | 0.71
F (Frequency) | 6 sec | FM | 0.26
C (Coupling/quality of grip) | fair | CM | 1

## Slide 6: Case 1: Effect of Frequency Factor on RWL
Determine the Recommended Weight Limit for the task:
RWL = 23 kg * 1 * .99 * 1 * 0.71 * 0.26 * 1
= 4 .2 kg
Compare weight of the load against determined weight limit for the task:
weight of load (10 kg) > RWL (4.2 kg)
Conclusion: Task is Dangerous

## Slide 7: Case 1: Effect of Frequency Factor on RWL
Recommendations:
Assess which component(s) contribute(s) most to the risk
  the critical factor is FM ⇒ it is required to reconsider the frequency of lifting and/or duration of task
Shorten the frequency of lifting by:
  reducing the frequency of incoming boxes (i.e. increasing F) and/or
  assigning additional workers to task, and/or
  shortening the time of the task to 1 hour

## Slide 8: Case 1: Effect of Frequency Factor on RWL
Recommendations (Cont.):
Notes: * Note how we just moved only one step in the FM table: i.e. from 2 hours to 1 hour, and up from 6 sec to the nearest reading @ 10 sec

## Slide 9: Case 1: Effect of Frequency Factor on RWL
Redesign the Task
Assess the six components in the redesigned task
Determine new RWL:
RWL =23 kg * 1 * .99 * 1 * 0.71 * 0.75 * 1
= 12.1 kg
Compare weight of the box against determined weight limit for redesigned task:
weight of load (10 kg): now < RWL (12.1 kg)
Conclusion: most workers can perform the task safely (why most?)
Notes: * Note assuming only redesigning F (i.e. no change in AM), the min. FM such that W ≤ RWL  FM ≥ W / (LC * AM) ≥ 10 / (23 * 0.71) ≥ 0.612; and 0.75 is both close and greater than 0.612
* Also note assuming redesigning A (i.e. no change in FM), the min AM such that W ≤ RWL  AM ≥ W / (LC * FM) ≥ 10 / (23 * 0.26) ≥ 1.67, which is not possible since all multipliers must be ≤ 1

## Slide 10: Case 2: Effect of Horizontal Dist. on RWL
Problem Statement:
Analyze the following work task.
A worker lifts 15 kg boxes from the table to the shelf, five times an hour.
Notice that there is a barrier between the worker and the box.
Notes: Class exercise or Solve for extra credit

## Slide 11: Case 3: Effect of Vertical Distance on RWL
Problem Statement:
Analyze the following work task.
A worker lifts a 15 kg load of loosely-piled pieces of metal from the floor to the table, five times an hour.
Notes: Class exercise or Solve for extra credit

## Slide 12: References
  Slides by: Dr. Khaled Al-Saleh; online at: http://faculty.ksu.edu.sa/alsaleh/default.aspx
  Slides by: Dr. Mohammed Z. Ramadan; online at: http://faculty.ksu.edu.sa/mramadan/default.aspx
  Revised NIOSH Equation for the Design and Evaluation of Manual Lifting Tasks. Thomas R. Walters et al. Ergonomics 36(7): 749-776,1993.
  Applications Manual for the Revised NIOSH Lifting Equation. Thomas R. Walters, Vern Putz-Anderson, Arun Garg. US Department of Health and Human Services: Public Health Services. Cincinnati, OH, 1994.
  OSHA Technical Manual. Section VII: Chapter 1: Back Disorders and Injuries. Online at:
        www.osha.gov/dts/osta/otm/otm_vii/otm_vii_1.html