## Slide 1: MARIE: An Introduction to a Simple Computer

## Slide 2: Lecture Overview
A simple program
A discussion on assemblers
Extending our ISA

## Slide 3: A simple program
A Simple program
The figure below shows a program written in assembly language for MARIE
What does this program do?

## Slide 4: A simple program
A Simple program
This program simply adds to numbers and stores the result in the main memory.
  It loads the value stored at the location address 10416 into AC (the value is 002316 = 3510), ), (2*161+3*160) or 0000 0000 0010 0011 =35)
  It adds this value to the value stored at the location address 10516 (the value is FFE916 = (-23)10), (1111 1111 1110 1001)=0000 0000 0001 0110+1 =-23)
  Stores the sum into the location address 10616.
    So what will be stored in the location address 10616?
Now let us discover what happens during each “Fetch, decode, execute” cycle.

## Slide 5: Lecture Overview
A simple program
A discussion on assemblers
Extending our ISA

## Slide 6: What do Assemblers do
A discussion on Assemblers
Assembly language can be understood by the programmer but not the computer!
Assembly language must be converted into Machine Codes (binary codes) before being executed or even stored in the main memory.
An Assembler is used to translate assembly language into machine code
  It reads a source file (assembly program) and convert it to an object file (Machine code)
Assembler VS Compiler
  An assembler translates each mnemonic instruction (written in assembly) to exactly one machine code.
  With compilers, this is not usually the case

## Slide 7: Remember - Registers and Buses
MARIE
The Data path in MARIE is shown in this figure
  Note that a data word (that is an instruction) in the main memory travels a relatively long path before achieving the IR!

## Slide 8: Remember - The Fetch-Decode-Execute cycle
Instruction processing
MARIE, like any other computer architecture, follow the basic machine cycle:
  the fetch, decode, and execute cycle
Fetch
Decode
Execute

## Slide 9: Remember - The Von Neumann model
Chapter 1: Introduction
Instruction 1
Instruction 2
Instruction 3
Instruction 4
…
…
…
Instruction N
Instruction 3
Fetch
  PC indicates the iteration number
  CU fill the instruction register
2. Decode
  what ALU should do (add, multiply, …)?
  Fill registers with needed data
Data 1
Data 2

## Slide 10: Remember - The Von Neumann model
Instruction 1
Instruction 2
Instruction 3
Instruction 4
…
…
…
Instruction N
Instruction 3
3. Execute
  Execute the instruction
  Place the results in registers or memory
Data 1
Data 2
Result

## Slide 11: The Instruction Set Architecture
MARIE
The fundamental MARIE instructions are:

## Slide 12: What do Assemblers do
A discussion on Assemblers
Going back to our simple program, what really happens inside the CPU during each fetch, decode, execute cycle?
  Load 104:

## Slide 13: What do Assemblers do
A discussion on Assemblers
  Add 105:
  Store 106:

## Slide 14: What do Assemblers do
A discussion on Assemblers
An assembler directive is an instruction that is not supposed to be translated into machine code
In assembly language we can also use labels in order to clarify the program
  Example: base 16 is the default base when writing assembly program for MARIE, to specify the used base we can use “constant directives” such as DEC (decimal) or HEX (Hexadecimal)