## Slide 1: Agglutination
Direct Agglutination Test
Brucella Agglutination Test

## Slide 2
Agglutination
Definition : Ag Ab interaction where Ag is a particulate material ( cell, bacteria, carrier)
Y
Y
Y
+
↔
Agglutination test: Qualitative/ Quantitative(Ab titer) agglutination test
  It is used to determine either Ag or Ab in patient sample
Direct Agg
Self Ag
Y
Y
Cross linking

## Slide 3: Agglutination (cross linking)

## Slide 4: Ab Titer
Def: No of Ab units per unit volume of serum
Calculation :
Make serial doubling dilution
The highest dilution(last tube or well) that gives agglutination is end point.
Ab titer is the reciprocal of end point.

## Slide 5: Brucella Agglutination
Disease called Brucellosis ,Malta fever.
Causative agents: Brucella abortus, Br. melitensis ,and other species.
In this test need to determine the amount of Ab to Brucella Ag in patient sample.
Ag : Brucella abortus Ag
Diluent : 0.5% phenol saline

## Slide 6: Principle of test
Ab content of patient’s serum is measured by adding a constant amount of Brucella abortus colored Ag to serially diluted serum.
High Ab titers above 80 units are considered clinically significant.
Could be Quantitative or Qualitative test

## Slide 7: Test procedure(Quantitative)
Deliver 100 ul of diluent in wells 1-10
Deliver 60ul of diluent in well 1.
Deliver 40 ul of serum in well 1.
Change the tip , mix and transfer 100ul from well 1 to well 2.
Repeat the previous step till well 9.
Discard 100ulfrom well 9.
Deliver 25ul of Br. Abortus Ag to all wells.
Cover and incubate the plate at 37 c O.N.

## Slide 8: Procedure outline
160ul diluent | 100ul diluent |  |  |  |  |  |  |  |  |  | 
Serum 40ul | 100ul |  |  |  |  |  |  |  |  |  | 
Brucella Ag | 25ul |  |  |  |  |  |  |  |  |  | 
1:5 | 1:10 | 1:20 |  |  |  |  |  | 1: 1280 | -ve C |  | 
1 2 3 4 5 6 7 8 9 10 11 12

## Slide 9: Reading results
+ve result= Agglutination( membrane or film or Sheath appearance).
-ve result=no Agglutination( button formation)
+ve Agg
-ve Agg

## Slide 11: Control
Well no 10 is –ve control ( -ve Agg)
It contains diluent ( 0,5% phenol saline) + Brucella Ag
Prozone phenomenon
Due to Excess Abs or blocking Abs(non specific)
Test appears –ve Agg even Abs are present ( false –ve result)
Solve this problem by diluting the sample.

## Slide 12: Prozone phenomenon

## Slide 13: Factors Affecting Measurement of Ag/Ab Reactions
Affinity
Avidity
Ag : Ab ratio
Physical form of Ag
Ab excess
Equivalence – Lattice formation
Ag excess

## Slide 14: Important notes in serology
Serum must not be hemolyzed or contaminated.
Kits must be left 30min at room temperature before using them.
Controls (+ve,-ve) must be used regularly.
Check expiration date of kits, diluents and reagents.
Kits even though are tested against HIV ,HBV must be considered biological hazards.
Before using any kit, read the instructions provided carefully.