## Slide 1: Yes, No, Maybe...
07/29/26
<number>
BooleanAlgebra
Notes: <number>

## Slide 2: Boolean Algebra
07/29/26
<number>
Boolean algebra provides the operations and the rules for working with the set {0, 1}.
These are the rules that underlie electronic circuits, and the methods we will discuss are fundamental to VLSI design.
We are going to focus on three operations:
Boolean complementation,
Boolean sum, and
Boolean product

## Slide 3: Boolean Operations
07/29/26
<number>
The complement is denoted by a bar (on the slides, we will use a minus sign). It is defined by
-0 = 1 and -1 = 0.
The Boolean sum, denoted by + or by OR, has the following values:
1 + 1 = 1, 1 + 0 = 1, 0 + 1 = 1, 0 + 0 = 0
The Boolean product, denoted by  or by AND, has the following values:
1  1 = 1, 1  0 = 0, 0  1 = 0, 0  0 = 0

## Slide 4: Boolean Functions and Expressions
07/29/26
<number>
Definition: Let B = {0, 1}. The variable x is called a Boolean variable if it assumes values only from B.
A function from Bn, the set {(x1, x2, …, xn) |xiB, 1  i  n}, to B is called a Boolean function of degree n.
Boolean functions can be represented using expressions made up from the variables and Boolean operations.

## Slide 5: Boolean Functions and Expressions
07/29/26
<number>
The Boolean expressions in the variables x1, x2, …, xn are defined recursively as follows:
0, 1, x1, x2, …, xn are Boolean expressions.
If E1 and E2 are Boolean expressions, then (-E1), (E1E2), and (E1 + E2) are Boolean expressions.
Each Boolean expression represents a Boolean function. The values of this function are obtained by substituting 0 and 1 for the variables in the expression.

## Slide 6: Boolean Functions and Expressions
07/29/26
<number>
For example, we can create Boolean expression in the variables x, y, and z using the “building blocks” 0, 1, x, y, and z, and the construction rules:
Since x and y are Boolean expressions, so is xy.
Since z is a Boolean expression, so is (-z).
Since xy and (-z) are expressions, so is xy + (-z).
… and so on…

## Slide 7: Boolean Functions and Expressions
07/29/26
<number>
Example: Give a Boolean expression for the Boolean function F(x, y) as defined by the following table:
x | y | F(x, y)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
Possible solution: F(x, y) = (-x)y

## Slide 8: Boolean Functions and Expressions
07/29/26
<number>
Another Example:
Possible solution I:
F(x, y, z) = -(xz + y)
0
0
1
1
F(x, y, z)
1
0
1
0
z
0
0
1
0
1
0
0
0
y
x
0
0
0
1
1
0
1
0
1
1
1
1
0
1
0
1
Possible solution II:
F(x, y, z) = (-(xz))(-y)

## Slide 9: Boolean Functions and Expressions
07/29/26
<number>
There is a simple method for deriving a Boolean expression for a function that is defined by a table. This method is based on minterms.
Definition: A literal is a Boolean variable or its complement. A minterm of the Boolean variables x1, x2, …, xn is a Boolean product y1y2…yn, where yi = xi or yi = -xi.
Hence, a minterm is a product of n literals, with one literal for each variable.

## Slide 10: Boolean Functions and Expressions
07/29/26
<number>
Consider F(x,y,z) again:
F(x, y, z) = 1 if and only if:
x = y = z = 0 or
x = y = 0, z = 1 or
x = 1, y = z = 0
Therefore,
F(x, y, z) = (-x)(-y)(-z) + (-x)(-y)z + x(-y)(-z)
0
0
1
1
F(x, y, z)
1
0
1
0
z
0
0
1
0
1
0
0
0
y
x
0
0
0
1
1
0
1
0
1
1
1
1
0
1
0
1

## Slide 11: Boolean Functions and Expressions
07/29/26
<number>
Definition: The Boolean functions F and G of n variables are equal if and only if F(b1, b2, …, bn) = G(b1, b2, …, bn) whenever b1, b2, …, bn belong to B.
Two different Boolean expressions that represent the same function are called equivalent.
For example, the Boolean expressions xy, xy + 0, and xy1 are equivalent.

## Slide 12: Boolean Functions and Expressions
07/29/26
<number>
The complement of the Boolean function F is the function –F, where –F(b1, b2, …, bn) = -(F(b1, b2, …, bn)).
Let F and G be Boolean functions of degree n. The Boolean sum F+G and Boolean product FG are then defined by
(F + G)(b1, b2, …, bn) = F(b1, b2, …, bn) + G(b1, b2, …, bn)
(FG)(b1, b2, …, bn) = F(b1, b2, …, bn) G(b1, b2, …, bn)

## Slide 13: Boolean Functions and Expressions
07/29/26
<number>
Question: How many different Boolean functions of degree 1 are there?
Solution: There are four of them, F1, F2, F3, and F4:
x | F1 | F2 | F3 | F4
0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1

## Slide 14: Boolean Functions and Expressions
07/29/26
<number>
Question: How many different Boolean functions of degree 2 are there?
Solution: There are 16 of them, F1, F2, …, F16:
1
0
0
0
F2
0
0
0
0
F1
0
1
0
1
0
1
0
1
1
0
0
0
F3
y
x
1
1
1
0
F8
0
1
1
0
F7
0
0
0
1
F9
0
0
1
0
F5
1
1
0
0
F4
1
0
1
0
F6
0
1
0
1
F11
1
0
0
1
F10
0
1
1
1
F12
1
0
1
1
F14
0
0
1
1
F13
1
1
0
1
F15
1
1
1
1
F16

## Slide 15: Boolean Functions and Expressions
07/29/26
<number>
Question: How many different Boolean functions of degree n are there?
Solution:
There are 2n different n-tuples of 0s and 1s.
A Boolean function is an assignment of 0 or 1 to each of these 2n different n-tuples.
Therefore, there are 22n different Boolean functions.

## Slide 16: Duality
07/29/26
<number>
There are useful identities of Boolean expressions that can help us to transform an expression A into an equivalent expression B (see Table 5 on page 597 in the textbook).
We can derive additional identities with the help of the dual of a Boolean expression.
The dual of a Boolean expression is obtained by interchanging Boolean sums and Boolean products and interchanging 0s and 1s.

## Slide 17: Duality
07/29/26
<number>
Examples:
The dual of x(y + z) is
x + yz.
The dual of -x1 + (-y + z) is
(-x + 0)((-y)z).
The dual of a Boolean function F represented by a Boolean expression is the function represented by the dual of this expression.
This dual function, denoted by Fd, does not depend on the particular Boolean expression used to represent F.

## Slide 18: Duality
07/29/26
<number>
Therefore, an identity between functions represented by Boolean expressions remains valid when the duals of both sides of the identity are taken.
We can use this fact, called the duality principle, to derive new identities.
For example, consider the absorption law x(x + y) = x.
By taking the duals of both sides of this identity, we obtain the equation x + xy = x, which is also an identity (and also called an absorption law).

## Slide 19: Definition of a Boolean Algebra
07/29/26
<number>
All the properties of Boolean functions and expressions that we have discovered also apply to other mathematical structures such as propositions and sets and the operations defined on them.
If we can show that a particular structure is a Boolean algebra, then we know that all results established about Boolean algebras apply to this structure.
For this purpose, we need an abstract definition of a Boolean algebra.

## Slide 20: Definition of a Boolean Algebra
07/29/26
<number>
Definition: A Boolean algebra is a set B with two binary operations  and , elements 0 and 1, and a unary operation – such that the following properties hold for all x, y, and z in B:
x  0 = x and x  1 = x (identity laws)
x  (-x) = 1 and x  (-x) = 0 (domination laws)
(x  y)  z = x  (y  z) and (x  y)  z = x  (y  z) and (associative laws)
x  y = y  x and x  y = y  x (commutative laws)
x  (y  z) = (x  y)  (x  z) and x  (y  z) = (x  y)  (x  z) (distributive laws)

## Slide 21: Logic Gates
07/29/26
<number>
Electronic circuits consist of so-called gates. There are three basic types of gates:
x
y
x+y
OR gate
AND gate
x
y
xy
x
-x
inverter

## Slide 22: Logic Gates
07/29/26
<number>
Example: How can we build a circuit that computes the function xy + (-x)y ?
xy + (-x)y
x
y
xy
x
-x
y
(-x)y

## Slide 23: The End
07/29/26
<number>