## Slide 1
Chapter 12
Notes: <number>

## Slide 2
Summary
The Capacitor
Capacitors are one of the fundamental passive components. In its most basic form, it is composed of two plates separated by a dielectric.
The ability to store charge is the definition of capacitance.
Dielectric
Conductors
Notes: <number>

## Slide 3
Summary
The Capacitor
Initially uncharged
Charging
Fully charged
Source removed
The charging process…
A capacitor with stored charge can act as a temporary battery.
Notes: <number>

## Slide 4
Capacitance is the ratio of charge to voltage
Rearranging, the amount of charge on a capacitor is determined by the size of the capacitor (C) and the voltage (V).
Example
If a 22 F capacitor is connected to a 10 V source, the charge is
220 C
Capacitance
Notes: <number>

## Slide 5
Capacitance
An analogy:
Imagine you store rubber bands in a bottle that is nearly full.
You could store more rubber bands (like charge or Q) in a bigger bottle (capacitance or C) or if you push them in with more force (voltage or V). Thus,
Notes: <number>

## Slide 6
A capacitor stores energy in the form of an electric field that is established by the opposite charges on the two plates. The energy of a charged capacitor is given by the equation
Capacitance
where
W = the energy in joules
C = the capacitance in farads
V = the voltage in volts
Notes: <number>

## Slide 7
The capacitance of a capacitor depends on three physical characteristics.
Summary
C is directly proportional to
and the plate area.
the relative dielectric constant
C is inversely proportional to
the distance between the plates
Capacitance
Notes: <number>

## Slide 8
Summary
Find the capacitance of a 4.0 cm diameter sensor immersed in oil if the plates are separated by 0.25 mm.
The plate area is
The distance between the plates is
Example
178 pF
Capacitance
Notes: <number>

## Slide 9
Summary
Capacitor types
Mica
Mica capacitors are small with high working voltage. The working voltage is the voltage limit that cannot be exceeded.
Notes: <number>

## Slide 10
Summary
Capacitor types
Ceramic disk
Ceramic disks are small nonpolarized capacitors They have relatively high capacitance due to high r.
Notes: <number>

## Slide 11
Summary
Capacitor types
Plastic Film
Plastic film capacitors are small and nonpolarized. They have relatively high capacitance due to larger plate area.
Notes: <number>

## Slide 12
Summary
Capacitor types
Electrolytic (two types)
Symbol for any electrolytic capacitor
Al electrolytic
Ta electrolytic
Electrolytic capacitors have very high capacitance but they are not as precise as other types and tend to have more leakage current. Electrolytic types are polarized.
Notes: <number>

## Slide 13
Summary
Capacitor types
Variable
Variable capacitors typically have small capacitance values and are usually adjusted manually.
A solid-state device that is used as a variable capacitor is the varactor diode; it is adjusted with an electrical signal.
Symbols for the capacitor: (a) fixed; (b) variable.
Notes: <number>

## Slide 14
Capacitor labeling
Capacitors use several labeling methods. Small capacitors values are frequently stamped on them such as .001 or .01, which have units of microfarads.
Electrolytic capacitors have larger values, so are read as F. The unit is usually stamped as F, but some older ones may be shown as MF or MMF).
Notes: <number>

## Slide 15
  A label such as 103 or 104 is read as 10x103 (10,000 pF) or 10x104 (100,000 pF) respectively. (Third digit is the multiplier.)
Capacitor labeling
  When values are marked as 330 or 6800, the units are picofarads.
Example
What is the value of each capacitor?
Both are 2200 pF.
Notes: <number>

## Slide 16
Three ways to increase the area of a capacitor: (a) rolling; (b) stacking; (c) insertion.

## Slide 17
Summary
Series capacitors
When capacitors are connected in series, the total capacitance is smaller than the smallest one. The general equation for capacitors in series is
The total capacitance of two series capacitors is
…or you can use the product-over-sum rule
Notes: <number>

## Slide 18
Summary
Series capacitors
Example
If a 0.001 F capacitor is connected in series with an 800 pF capacitor, the total capacitance is
444 pF
Notes: <number>

## Slide 19
Summary
Parallel capacitors
When capacitors are connected in parallel, the total capacitance is the sum of the individual capacitors. The general equation for capacitors in parallel is
Example
1800 pF
If a 0.001 F capacitor is connected in parallel with an 800 pF capacitor, the total capacitance is
Notes: <number>

## Slide 20
Summary
Capacitors in dc circuits
When a capacitor is charged through a series resistor and dc source, the charging curve is exponential.
Effect of increasing values of C (with R constant) on the charging curve for vC.
Notes: <number>

## Slide 21
Summary
Capacitors in dc circuits
When a capacitor is discharged through a resistor, the discharge curve is also an exponential. (Note that the current is negative.)
Notes: <number>

## Slide 22
Summary
Capacitors in dc circuits
The same shape curves are seen if a square wave is used for the source.
VS
VC
VR
Question
What is the shape of the current curve?
The current has the same shape as VR.
Notes: <number>

## Slide 23
Summary
Universal exponential curves
Specific values for current and voltage can be read from a universal curve. For an RC circuit, the time constant is
Rising exponential
Falling exponential
Notes: <number>

## Slide 25
Summary
The universal curves can be applied to general formulas for the voltage (or current) curves for RC circuits. The general voltage formula is
v =VF + (Vi VF)et/RC
  VF = final value of voltage
  Vi = initial value of voltage
  v = instantaneous value of voltage
The final capacitor voltage is greater than the initial voltage when the capacitor is charging, or less that the initial voltage when it is discharging.
Universal exponential curves
Notes: <number>

## Slide 26
Summary
Capacitive reactance
Capacitive reactance is the opposition to ac by a capacitor. The equation for capacitive reactance is
Example
The reactance of a 0.047 F capacitor when a frequency of 15 kHz is applied is
226 
ω=2πf
Notes: <number>

## Slide 27
Summary
Capacitive phase shift
When a sine wave is applied to a capacitor, there is a phase shift between voltage and current such that current always leads the voltage by 90o.
Notes: <number>

## Slide 28
Summary
Power in a capacitor
Voltage and current are always 90o out of phase. For this reason, no true power is dissipated by a capacitor, because stored energy is returned to the circuit.
The rate at which a capacitor stores or returns energy is called reactive power. The unit for reactive power is the VAR (volt-ampere reactive).
Energy is stored by the capacitor during a portion of the ac cycle and returned to the source during another portion of the cycle.
Notes: <number>

## Slide 29
Summary
Switched capacitors
Switched capacitors move charge in a specific time interval between two points that are different voltages.
The switched capacitors emulate a resistor with a value of R=1/fC. Switched capacitors are widely used in certain types of integrated circuits because they can be made very small, have virtually no drift, and do not dissipate heat.
Notes: <number>

## Slide 30: Measurement and Testing of Capacitors
Checking the dielectric of an electrolytic capacitor.

## Slide 31
Selected Key Terms
Capacitor
Dielectric
Farad
RC time constant
An electrical device consisting of two conductive plates separated by an insulating material and possessing the property of capacitance.
The insulating material between the conductive plates of a capacitor.
The unit of capacitance.
A fixed time interval set by the R and C values, that determine the time response of a series RC circuit. It equals the product of the resistance and the capacitance.
Notes: <number>

## Slide 32
Capacitive reactance
Instantaneous power (p)
True power (Ptrue)
Reactive power (Pr )
VAR
(volt-ampere reactive)
The value of power in a circuit at a given instant of time.
The power that is dissipated in a circuit usually in the form of heat.
The opposition of a capacitor to sinusoidal current. The unit is the ohm.
Selected Key Terms
The rate at which energy is alternately stored and returned to the source by a capacitor. The unit is the VAR.
The unit of reactive power.
Notes: <number>

## Slide 34
Quiz
1. The capacitance of a capacitor will be larger if
a. the spacing between the plates is increased
b. air replaces oil as the dielectric
c. the area of the plates is increased
d. all of the above
Notes: <number>

## Slide 35
Quiz
2. The major advantage of a mica capacitor over other types is
a. they have the largest available capacitances
b. their voltage rating is very high
c. they are polarized
d. all of the above
Notes: <number>

## Slide 36
Quiz
3. Electrolytic capacitors are useful in applications where
a. a precise value of capacitance is required
b. low leakage current is required
c. large capacitance is required
d. all of the above
Notes: <number>

## Slide 37
Quiz
4. If a 0.015 F capacitor is in series with a 6800 pF capacitor, the total capacitance is
a. 1568 pF
b. 4678 pF
c. 6815 pF
d. 0.022 F
Notes: <number>

## Slide 38
Quiz
5. Two capacitors that are initially uncharged are connected in series with a dc source. Compared to the larger capacitor, the smaller capacitor will have
a. the same charge
b. more charge
c. less voltage
d. the same voltage
Notes: <number>

## Slide 39
Quiz
6. When a capacitor is connected through a resistor to a dc voltage source, the charge on the capacitor will reach 50% of its final charge in
a. less than one time constant
b. exactly one time constant
c. greater than one time constant
d. answer depends on the amount of voltage
Notes: <number>

## Slide 40
Quiz
7. When a capacitor is connected through a series resistor and switch to a dc voltage source, the voltage across the resistor after the switch is closed has the shape of
a. a straight line
b. a rising exponential
c. a falling exponential
d. none of the above
Notes: <number>

## Slide 41
Quiz
8. The capacitive reactance of a 100 F capacitor to 60 Hz is
a. 6.14 k
b. 265 
c. 37.7 
d. 26.5 
Notes: <number>

## Slide 42
Quiz
9. If an sine wave from a function generator is applied to a capacitor, the current will
a. lag voltage by 90o
b. lag voltage by 45o
c. be in phase with the voltage
d. none of the above
Notes: <number>

## Slide 43
Quiz
10. A switched capacitor emulates a
a. smaller capacitor
b. larger capacitor
c. battery
d. resistor
Notes: <number>

## Slide 44
Quiz
Answers:
1. c
2. b
3. c
4. b
5. a
6. a
7. c
8. d
9. d
10. d
Notes: <number>