## Slide 1: CE 424 HYDROLOGY
1
Instructor:
Dr. Saleh A. AlHassoun

## Slide 2
2
- Hydrology is the science of water in all its types:
It is the science that deals with the occurrence, circulation, and distribution of water of the earth and earth’s atmosphere.
It is concerned with water in streams and lakes, rainfall and snowfall, snow and ice on the land, and groundwater.
It is of inter-disciplinary nature.
1.1 Introduction

## Slide 3
3
In general, hydrology deals with
Estimation of water resources(supply &demand).
The study of processes such as precipitation, runoff, evapotranspiration and their interaction.
The study of water problems such as floods and droughts and strategies to combat them.
Planning, design, and operation of Hydraulic Structures for control and use of Water.
… 1.1 Introduction

## Slide 4
4
1.2. Hydrologic Cycle

## Slide 5: - Hydrologic Cycle Processes
5
Surface Water
Soil water
Atmospheric water
Groundwater
Processes
Precipitation ; P
Evaporation ; E , ET
Infiltration ; I
Surface Runoff ; Q or Qs
Groundwater Recharge
(Percolation) ; qr
Baseflow ; Qg
System
Land Surface

## Slide 6: Catchment Area or Watershed?
6
Catchment area or drainage basin or river basin or watershed is defined as:
The area drained by a stream or a system of connecting streams such that the surface runoff originating in this area leaves the area in concentrated flow through a single outlet.
1.3. Water Budget
A B
Stream Outlet B
Or Station B
Catchment boundary or watershed or divide for
the site at B
Stream Outlet A
Catchment boundary for
the site at A
Tributary

## Slide 7: Water budget equation
7
Hydrologic analysis for various applications and models begins with the system concept.
System Concept
SYSTEM
OPERATORS
  INPUTS
OUTPUTS
System Boundary
I = inflow volume per unit time
Q = outflow per unit time

## Slide 8: Typical Water Budget System Components
8
R
P
E
G
T
P - R - G - E - T =  S
P/  t – Qs – Qg – ET/  t =  S/  t
P = precipitation
E = evaporation
T = transpiration
R = Surface runoff
G = net groundwater flow
S = change in storage
Qs = R/ t
Qg = G/ t

## Slide 9
Example :
A small catchment of area 150 ha received a rainfall of 105 mm in 90 minutes due to a storm. At the outlet of the catchment, the stream draining the catchment was dry before the storm and experienced a runoff lasting for 10 hours with an average discharge value of 2.0 m3/sec. the stream was again dry after the runoff event.
1. What is the amount of water which was not available to runoff due to combined effect of infiltration, evaporation and transpiration.
2. What is the ratio of runoff to precipitation?
9

## Slide 10
Solution :
Losses = 157,000 - 72,000 = 85,500 m3 = Water not available to runoff.
The water budget equation for the catchment in a time Δt is :
P -R -G -E -T = ΔS
Take Δt = Duration of Runoff = 10 hours
Rainfall occurred in 90 minutes and the rest (8.5 hours) the precipitation was zero.
ΔS = 0
1. G + E + T = water not available to runoff = Losses = L
Hence : P - R = L
P = Precipitation = 150x100x100x10.5/100 = 157,500 m3
R = Runoff volume = 2.0x10x60x60= 72,000 m3
2. Runoff/rainfall = 72,000/157,500 = 0.457 or 45.7%
10

## Slide 11: 1.4. World Water Distribution :
9
Oceans 96.5 % of total water
(can cover Earth to 2.6 km)
Saline water on land 1% of total water
Fresh: 2.5 % of total water
Polar Ice 68.6 % of fresh water(2/3 of total Fresh)
Groundwater 30.1 % of fresh water
Lakes & Rivers 0.266 % of fresh water

## Slide 12: Global Water Balance :
10
Global Average Precipitation (per year):
Ocean (70.8 %) and Land (29.2%)
1270 mm x 0.708 + 800 mm x 0.292 = 1132 mm/yr.
60 % of Land Precip. will be Evap. (i.e. 60%X800 = 480 mm)
Global Average Evaporation (per year):
1400 mm x 0.708 + 480 mm x 0.292 = 1132 mm/yr.
Total Runoff to ocean = 316 mm/yr.

## Slide 13: 1.6. Application in Engineering
13
► Hydrology is needed in the design and operation of water resources engineering projects such as those for irrigation, water supply, flood control, water power and navigation.
More specific examples :
  The capacity of storage structures such as reservoirs
  The magnitude of flood flows to enable safe disposal of excess flow
  Floodplain analysis and delineation
  The minimum flow and quantity of flow available at various seasons
  Erosion and sediment control
  The interaction of the flood wave and hydraulic structures, such as levees, reservoirs, and bridges
  ► The hydrologic study should of necessity precede structural and other detailed design studies.

## Slide 14: 1.7. Sources of Data
14
The data normally required:
Weather records ( temperature, humidity, wind speed),
Precipitation data,
Stream-flow records,
Evaporation and transpiration data,
Infiltration characteristics of the area,
Groundwater characteristics,
Physical and geological characteristics.