## Slide 1: Chapter 5 Stream Flow
CE 424
Dr. Saleh AlHassoun

## Slide 2: INTRODUCTION
Rainfall has an effect on stream flow and hydraulics tends to measure the relationship between rainfall and stream flow.
The aim of measuring stream flow is mainly in establishing a stage discharge relationship.

## Slide 3: Definitions : Rainfall results in : 1. Infiltration , I 2. Evaporation , E ; ET 3. Intercepted & depression storage 4. Surface flow ,Q
Q & Qg & interflow goes to Stream (Stream flow)
** Channel & basin(watershed)
Water Stage Measurements :
Stage : water surface elevation ……
* Stage measurements are mainly made with gages.

## Slide 4: Components of the Flow :
Overland Flow
Interflow
Groundwater
Channel Flow
(Streamflow)
Rainfall

## Slide 5: STAGE-DISCHARGE RELATIONS
Simultaneous measurements of stage and discharge provide a calibration graph known as stage-discharge relations or rating curve.
Stage: Height of stream level measured from an arbitrary datum.
Depth: Measured from the bottom of the channel.
The datum can also be the mean sea level. A plot of stage Vs discharge is made to obtain a rating curve.

## Slide 6: STAGE-DISCHARGE RELATIONSHIP
Methods :
1. Non recording stream gage : a. Staff b. Wire(String)
c. Crest staff
2. Recording stream gage : 1. Float type 2. Digital gage
1. Manual Gages(Non recording)
a) Sectioned Staff Gages: A series of posts each overlapping.
The height above a certain datum is measured.
The stage is usually related to height above mean sea level (msl).

## Slide 8: Stage Measurements (Contd.)
A certain datum level is on the bridge and a string having a weight electrically connected is lowered to the water surface to get the depth of water surface.
Stage measurement can be inaccurate if there is scouring.

## Slide 9: Rules Guiding Location of Gauges
a) Gauges should not be located in rivers with scouring characteristics.
b) The locations should stir clear of river bends because the water surface is inclined and there is turbulence making the stage measurement inconsistent.
c) The upstream of a natural control eg. a rapid should be used, not downstream.
Rapid
Calm area

## Slide 10: Rules Guiding Location of Gauges
d) A uniform channel helps good stage measurement. Irregular cross sections should be avoided.
O.K.
Avoid this irregular section

## Slide 11: 2. Recording Gauges
They have advantages over the manual ones.
a) Float Gauge: Float movement fluctuates with change in stage and this is recorded by a chart. In hydrologic measurements, both the big and low flows are measured within the chart.

## Slide 12: Float Gauge
Float
Chart

## Slide 13: b) Digital Recorders
They have clocks and used when for example hourly measurements are desired usually where stages do not increase and decrease steeply.
The recorder should be placed at a height more than the expected peak stage.
To know the maximum stage expected, an ordinary gauge can be used for some time.

## Slide 14: c) Crest Gauges
They only measure peak flows.
It is a cylindrical tube sealed below with only a few holes to allow the water to enter the tube.
A ground cork fixed in the tube floats up and is held by surface tension when stage increases.
It stays at maximum stage until the reading is taken and let loose.

## Slide 15: Crest Gauge

## Slide 16: DISCHARGE MEASUREMENTS
Current Meter: It has a propeller which is rotated when water hits it and is connected to magnets which actuates recorders when the propeller rotates.
The velocity of water increases the propeller rotation.

## Slide 17: Current Meter

## Slide 18: Current Meter (Contd.)
The number of rotations are measured and correlated to velocity using the formula:
v = a + bN where N is the rotation of the propeller (revolutions per sec {rps})
a and b are coefficients determined by calibration in an experimental flume.

## Slide 19: Current Meter (Contd.)
1
b
Propeller Rotation, N
Velocity
a
Surface Velocity
Average Vel
0.6 D
D

## Slide 20: Current Meter Measurements (Contd.)
Considering the velocity profile with depth, average value of velocity can be obtained at 0.6 of the depth. i.e. V = average velocity is at about 0.6 D.
An alternative of using the 0.6 D velocity is to take 0.2 and 0.8 velocities and obtain the averages.
The latter method is more accurate but in a shallow cross-section, the velocity at 0.2 D may be difficult to measure so use a single value at 0.6 D.

## Slide 21: Discharge Measurements : 1. Velocity-Area station Method : Q = Vav * A
Vav = V0.6 for shallow stream ; depth < 3 m
Vav = (V0.8 +V0.2)/2 for moderate stream
Vav = C V0.5 for deep stream –flood flow
Velocity Measurements :
1. Velocity of float : Vav = C Vf
2. Current meters : Vav = a + b N
Q = Σ qi = Σ vi ai

## Slide 22: Determination of Discharges
D
V0.8D
V 0.2D
Average Discharge = V x area of Segment

## Slide 23: 2. Moving Boat Method : for large rivers 3. Chemical gagging :concentration of Chemical tracer 4. Ultrasonic :
5. Indirect Methods :
Measure flow depth (y) to get Q by :
* Flow measured structures : such as weirs , orifices , …
* Slope-area methods : such as Chezy , Manning , Hayzen

## Slide 24: Measurement of Discharges Contd.
First divide the cross-section of the stream into vertical sections such that no section carries more than 10 % of the total flow.
Take soundings to determine various depths. The sections are of a known width and so the discharge can be calculated if the velocities are taken along the 0.2 D and 0.8 D OR 0.6 D alone.

## Slide 25: Discharge Measurements Contd.
Flow in one segment,
q = average velocity(vav)x area of segment(ai).
Area of each segment can be calculated using the trapezoidal formula.
Total discharge, Q is equal to:
(average velocity x area of segments)
Q = Σ qi = Σ vi ai

## Slide 26: Discharge Measurements Using Floats
Any floatable substance eg. a tennis ball is placed at a point and the time(t) it takes it to move a known distance is noted.
d/t gives the average surface velocity of the water.
The surface velocity(Vs) is equal to 1.2(average Velocity, V) ie. Vs = 1.2V and V = 0.8 Vs.
The cross-sectional area of flow is then multiplied by the average velocity to get the flow rate.

## Slide 27: Rating Curve (Contd.)
The essence of the rating curve is that when the curve is established for a particular stream, subsequent determinations of discharges are merely obtained by dipping a measuring stick to measure the stage.
Discharge is then read from the rating curve.
The rating curve should be checked from time to time for accurate measurements.

## Slide 28: Rating Curve Graph
depth
stage
Datum
Stage
Discharge
Rating Curve

## Slide 29: Rating Curve Types : 1. Simple Rating Curve : a . on arithmetic Paper : Parabolic curve as : Q = a ( y – y0 ) ** C b. On logarithmic paper : straight line as : log Q = log a + c log ( y – y0 ) 2. -- 5. see Text Extension of rating curve : used Logarithmic method to get Qp

## Slide 30: RAINFALL RUNOFF
INTRODUCTION: Runoff results from rainfall occurrence in a hydrologic catchment. Rainfall-runoff relations are very important in hydrology.
Most work on the prediction of runoff requires past records.
The problem is that some streams are not gauged.
Also, non-recording gauges only gives the volume of water and not intensities.

## Slide 31: Rainfall Runoff Contd.
There is the need to get records of stream flow and recording gauge information to predict runoff from rainfall.
Some empirical methods are available for predicting runoff in a catchment without the stream flow and recording gauge information.

## Slide 32: RUNOFF PREDICTION
Aims
a) To estimate the peak runoff flows(Qp)
b) To estimate runoff volume.
qp
Time
Volume of runoff

## Slide 33: Definition of Time of Concentration
This is the longest time it takes for a part of the catchment to contribute water to the outlet.
It is the time it takes for all the parts of the watershed to be contributing water to the outlet.
The divide or watershed divides the flow of water along different slopes.
All runoffs flow from the whole catchment to the stream or outlet.

## Slide 34: Catchment
Catchment Area
One
Catchment
The
Other

## Slide 35: Diagram Showing Two Catchments

## Slide 36: Time of Concentration Contd.
After rainfall, the time for water to move from different areas of the catchment to the outlet differs according to the different positions of places.
Time of concentration (Tc) refers to when all the catchment areas are contributing runoff to the outlet.
It is the time taken for the most remote area of the catchment to contribute water to the outlet.

## Slide 37: Time of Concentration Contd.
Another name for Tc is gathering time. Tc can be related to catchment area, slope etc. using the Kirpich equation:
Tc = 0.02 L 0.77 S – 0.385
Tc is the time of concentration (min);
L is the maximum length of flow (m);
S is the watershed gradient (m/m).

## Slide 38: Time of Concentration Contd.
L
Et
Eo
S = (Et - Eo)/L where Et is the elevation at top of the watershed and Eo is the elevation at the outlet. Tc can also be obtained from Table 3.1 of Hudson's Field Engineering.

## Slide 39: Time of Concentration Contd.
With Tc obtained for the catchment, decide on a return period.
For small conservation works, return period is assumed as 10 years.
With the Tc and assumed return period, get an intensity value from the Intensity-Duration curve derived for the area described in Chapter 4 of this course.

## Slide 40: Time of Concentration Contd.
From figure below, the highest runoff of a catchment is obtained when rainfall duration is equal to Tc.
T will give lower intensity of rainfall so lower runoff while T' will give higher intensity but not all parts of the watershed are contributing to runoff since Tc has not been reached.
The worst case of runoff is then when rainfall duration (D) is equal to Tc.

## Slide 41: Rainfall Intensity Duration Curve
Rainfall Duration (D)
2 5 10 Return periods
T’ Tc T
Rainfall
Intensity

## Slide 42: Runoff Prediction Methods
There are different methods for predicting peak flows of runoff and total volumes of runoff.
A. Methods of Estimating of Peak Flows
Many methods have been developed for estimating the probable maximum floods to be expected from small agricultural catchments. The major ones include:

## Slide 43: a) The Rational Formula:
It states that:
qp = (CIA)/360
where qp is the peak flow(m3 /s);
C is dimensionless runoff coefficient; I is the intensity of a storm of duration Tc (mm/hr) for a given return period. This is the worst case of runoff (see last section).
A is the area of catchment(ha).

## Slide 44: Using the Rational Method
i) Obtain area of catchment by surveying or from maps or aerial photographs.
ii) Estimate intensity using the curve in Hudson's Field Engineering, page 42.
iii) The runoff coefficient C is a measure of the rain which becomes runoff. On a corrugated iron roof, almost all the rain would runoff so C = 1, while in a well drained soil, nine-tenths of the rain may soak in and so C = 0.10. The table (see handout) from Hudson's Field Engineering can be used to obtain C value. Where the catchment has several different kinds of characteristics, the different values should be combined in proportion to the area of each.

## Slide 45: Runoff Coefficient, C

## Slide 46: b) Cook's Method:
Three factors are considered:
Vegetation,
Soil permeability and
Slope.
These are the catchment characteristics.
For each catchment, these are assessed and compared with Table 3.4 of Hudson's Field Engineering

## Slide 47: Table 3.4: Hudson’s Field Eng’g (CC)

## Slide 48: Example
A catchment may be heavy grass (10) on shallow soils with impeded drainage(30) and moderate slope(10).
Catchment characteristics (CC) is then the sum of the three ie. 50.
The area of the catchment is then measured, and using the Area, A and the CC, the maximum runoff can be read from Table 3.5 (Field Engineering, pp. 45).

## Slide 49: Table 3.5: Hudson’s Field Eng’g (Runoff Values)

## Slide 50: Cook’s Method Contd.
This gives the runoff for a 10 yr return period. For other return periods, other than 10 years, the conversion factor is:
Return Period (yrs): 2 5 10 25 50
Conversion factor: 0.90 0.95 1.00 1.25 1.50
Another factor to be considered is the shape of the catchment.
Table 3.5 gives the runoff for a catchment, which is roughly square or round. For other catchment shapes, the following conversion factors should be used:
Square or round catchment (1) Long & narrow (0.8) Broad & short (1.25)

## Slide 51: ANALYSIS OF RAINFALL RUNOFF

## Slide 52: Components of the Hydrologic Cycle
Overland Flow
Interflow
Groundwater
Channel Ppt.
Rainfall

## Slide 53: Components of Runoff Contd.
Hydrographs originate from rainfall. Some rainfall infiltrate, others run off (overland flow).
Some rain fall direct to the channel (channel precipitation).
The overland flow varies according to the roughness of soil and slope.
There is then a time lag for it to reach the outlet.
Water can also move below the soil but re-surface and join the channel (interflow).

## Slide 54: Components of Runoff Contd.
Some go direct to the groundwater and then to the channel (outlet). A hydrograph therefore has 4 components:
a) Overland flow b) Interflow
c) groundwater or base flow and
d) channel precipitation.
All these different routes contribute to runoff. The pathway runoffs take influences the shape of the hydrograph.

## Slide 55: Techniques for Separation of Components of Hydrographs
There is the need to separate different forms of flows especially separating base flow from direct runoff.
This is because direct runoff results from a definite rainfall event of known intensity and can be related to runoff directly.
Hydrographs consist of direct surface runoff (overland flow, channel precipitation and interflow) and base flow (groundwater). Some techniques exist for separation of the two components.

## Slide 56: Separation of Hydrographs

## Slide 57: UNIT HYDROGRAPH
A standard hydrograph that relates to different storms can be produced.
The basis is a linear system.
For rainfall of a given duration, t and intensity, i , a hydrograph (A) can be obtained.
The principle of a linear system is that another rainfall can be added to get a new hydrograph(C).
The single hydrograph (C) was obtained by adding the ordinates of A and B.

## Slide 58: Unit Hydrograph Contd.

## Slide 59: Construction or Derivation of Unit Hydrographs
Desirable factors for derivation: Uniform intensity and short duration storms are needed for the construction.
Ideally, the storms should be of equal duration.
b) Specific information for derivation:
i) Duration of storm
ii) Total hydrograph
iii) Drainage area
iv) Base flow or basis for obtaining it.

## Slide 60: Derivation Steps of Unit Hydrographs
i) Tabulate the total hydrograph with time distribution
ii) Tabulate the base flow if given or separate with method of our choice.
iii) Find the direct runoff hydrograph(DRH) by subtracting the base flow from the total hydrograph.
iv) Find the volume of water under the DRH

## Slide 61: Derivation Steps of Unit Hydrographs Contd.
v) Divide the volume of water(step iv) by the drainage area to get effective rainfall (runoff) per unit area.
vi) Divide the ordinates of the DRH by the cm of effective rainfall(step v).
The result is a unit hydrograph(UHG) for the duration of storm.

## Slide 64: Solution Contd.
Total volume of flow = 59850 m3 /s x 2 hrs = 59850 m3 /s x 2 x 3600 s = 430.9 x 106 m3
Area of catchment = 4300 km = 4300 x 100 ha = 4300 x 100 x 100002 m2
= 4300 x 106 m2
Effective rainfall per unit area = 0.1 m =10 cm
To obtain 1 cm i.e. 1 unit hydrograph, divide DRO column ordinates by 10. If 6 hr DRO for 30 cm is required, multiply UHG ordinates by 30

## Slide 65: Conversion of Unit Hydrograph from Shorter to Longer Duration (Multiple Situation)
It is possible to convert say a 2 hr. unit hydrograph to 6 hr unit hydrograph.
This is by lagging 2hrs, two times, adding up ordinate values to get 6hr 30 mm hydrograph.
Divide ordinates by 3 to obtain a 6 hr unit hydrograph.

## Slide 67: Non-Constant Storms