## Slide 1: CE 424 HYDROLOGY
Chapter 6
Hydrograph Analysis
Dr. Saleh AlHassoun
<number>

## Slide 2
Hydrograph
Record of River Discharge over a period of time ;
Q vs t
River Discharge : Q = AXv
= cross sectional area
rivers mean (average) velocity
X
(at a particular point in its course)
Storm Hydrographs
Show the change in discharge caused by a period of rainfall

## Slide 3
Why Construct & Analyse
Hydrographs ?
To find out discharge patterns of
  a particular drainage basin
Help predict flooding events,
  therefore influence implementation of flood prevention measures
©Microsoft Word clipart

## Slide 4
0 12 24 36 48 30 72 t(hrs)
Hours from start of rain storm
___ Components of Streamflow
___ Elements of Hydrograph
3
2
1
Discharge (m3/s)
Base flow
Inter flow
Overland flow
Rising limb
Recession limb
Basin lag time
mm
4
3
2
Peak flow (crest)
Flood Hydrograph

## Slide 5
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)

## Slide 6
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
mm
4
3
2
Rainfall shown in mm, as a bar graph
Notes: <number>

## Slide 7
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
mm
4
3
2
Discharge in m3/s, as a line graph
Notes: <number>

## Slide 8
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Rising limb
mm
4
3
2
Rising limb
The rising flood water in the river
Notes: <number>

## Slide 9
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Rising limb
mm
4
3
2
Peak flow
Peak flow
Maximum discharge in the river
Notes: <number>

## Slide 10
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Rising limb
Recession limb
mm
4
3
2
Peak flow
Recession limb
Falling flood water in the river
Notes: <number>

## Slide 11
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Rising limb
Recession limb
Basin lag time
mm
4
3
2
Peak flow
Basin lag time
Time difference between the peak of the rain storm and the peak flow of the river
Notes: <number>

## Slide 12
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Base flow
Rising limb
Recession limb
Basin lag time
mm
4
3
2
Peak flow
Base flow
Normal discharge of the river
Notes: <number>

## Slide 13
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Base flow
Inter flow
Overland flow
Rising limb
Recession limb
Basin lag time
mm
4
3
2
Peak flow
Overland flow
Inter flow
+
GW (BF)
+
=
Stream Flow
Or
Total Runoff
Notes: <number>

## Slide 14
Volume of water reaching the river from surface run off
GW
The Base flow
Overland flow
Inter flow
Volume of water reaching the river through the soil and underlying rock layers

## Slide 15
Factors influencing
Storm Hydrographs
Area
Shape
Slope
Rock Type
Soil
Land Use
Drainage Density
Precipitation / Temp
Tidal Conditions
©Microsoft Word clipart

## Slide 16
Interpretation of Storm Hydrographs
Rainfall Intensity
Rising Limb
Recession Limb
Lag time
Peak flow compared to Base flow
Recovery rate, back to Base flow
You need to refer to:
Basin lag time
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Base flow
Through flow
Overland flow
Rising limb
Recession limb
mm
4
3
2
Peak flow

## Slide 17
Area
Large basins receive more precipitation than small therefore have larger runoff
Larger size means longer lag time as water has a longer distance to travel to reach the trunk river
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 18
Shape
Elongated basin will produce a lower peak flow and longer lag time than a circular one of the same size
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 19
Slope
Channel flow can be faster down a steep slope therefore steeper rising limb and shorter lag time
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 20
Rock Type
Permeable rocks mean rapid infiltration and little overland flow therefore shallow rising limb
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 21
Soil
Infiltration is generally greater on thick soil, although less porous soils eg. clay act as impermeable layers
The more infiltration occurs the longer the lag time and shallower the rising limb
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 22
Land Use
Urbanisation - concrete and tarmac form impermeable surfaces, creating a steep rising limb and shortening the time lag
Afforestation - intercepts the precipitation, creating a shallow rising limb and lengthening the time lag
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 23
Drainage Density
A higher density will allow rapid overland flow
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 24
Precipitation & Temperature
Short intense rainstorms can produce rapid overland flow and steep rising limb
If there have been extreme temperatures, the ground can be hard (either baked or frozen) causing rapid surface run off
Snow on the ground can act as a store producing a long lag time and shallow rising limb. Once a thaw sets in the rising limb will become steep
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 25
Tidal Conditions
High spring tides can block the normal exit for the water, therefore extending the length of time the river basin takes to return to base flow
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 26
<number>
Hydrograph Analysis

## Slide 27: Hydrograph Analysis : Hydrograph : Q vs t
<number>
Duration , t
Lag Time , tL
Time of Concentration , tc
Rising Limb
Recession Limb (falling limb)
Peak Flow ,Qp
Time to Peak (rise time),tp
Recession Curve
Base flow , BF
Separation of BF from Runoff
Notes: <number>

## Slide 28: Hydrograph Components
Taken from Wanielista, M., R. Kersten, and R. Eaglin, Hydrology: Water Quantity and Quality Control, p. 184

## Slide 29: Graphical Representation
<number>
Lag time
Time of concentration
Duration of excess precipitation.
Base flow
Notes: <number>

## Slide 30: Separation of Baseflow
<number>
  ... generally accepted that the inflection point on the recession limb of a hydrograph is the result of a change in the controlling physical processes of the excess precipitation flowing to the basin outlet.
  In this example, base flow is considered to be a straight line connecting that point at which the hydrograph begins to rise rapidly and the inflection point on the recession side of the hydrograph.
  the inflection point may be found by plotting the hydrograph in semi-log fashion with flow being plotted on the log scale and noting the time at which the recession side fits a straight line.
Notes: <number>

## Slide 31: Separation of Baseflow
<number>
Notes: <number>

## Slide 32: Hydrograph & Baseflow
<number>
Notes: <number>

## Slide 33: Separate Baseflow
<number>
Notes: <number>

## Slide 34: Q = d * UH Runoff = rainfall depth * Unit Hydrograph
<number>

## Slide 35: Unit Hydrograph(UH) Theory:
<number>
Sherman - 1932
Horton - 1933
Wisler & Brater - 1949 –
“the hydrograph of surface runoff resulting from a relatively short, intense rain, called a unit storm.”
The runoff hydrograph may be “made up” of runoff that is generated as flow through the soil (Black, 1990).
Notes: <number>

## Slide 36: Unit Hydrograph
<number>
The hydrograph (direct runoff)resulting from 1-inch (or 1cm) of excess precipitation spread uniformly in space and time over a watershed for a given duration.
The key points :
    1-inch (1cm) of EXCESS precipitation
    Spread uniformly over space - evenly over the watershed
    Uniformly in time - the excess rate is constant over the time interval
    There is a given duration. t-UH (ex. 2hr-UH)
Notes: <number>

## Slide 37
<number>

## Slide 38: Methods of Developing UH’s
<number>
From Streamflow Data
Synthetically
  Snyder
  SCS
  Time-Area (Clark, 1945)
“Fitted” Distributions
Geomorphologic
Notes: <number>

## Slide 39: Unit Hydrograph Derivation
i) Tabulate the total hydrograph with time distribution.
ii) Tabulate the baseflow if given or separate with method of our choice.
iii) Find the Direct Runoff Hydrograph(DRH) by subtracting the baseflow from the total hydrograph.( DRH = Q – BF )
iv) Find the volume of water under the DRH
Vol. = Σ Q * Δt

## Slide 40: Unit Hydrograph Derivation
<number>
Notes: <number>

## Slide 41: Unit Hydrograph Derivation
v) Divide the volume of water(step iv) by the drainage area(A) to get effective rainfall(de) (runoff) per unit area.
de = vol. / A
vi) Divide the ordinates of the DRH by the de of effective rainfall(step v).
The result is a unit hydrograph(UH) for the duration of storm.

## Slide 42: Unit Hydrograph Derivation
<number>
Notes: <number>

## Slide 43
<number>

## Slide 45: Obtain UH Ordinates
<number>
The ordinates of the unit hydrograph are obtained by dividing each flow in the direct runoff hydrograph by the depth of excess precipitation.
In this example, the units of the unit hydrograph would be cfs/inch (of excess precipitation).
Notes: <number>

## Slide 46: Final UH
<number>
Notes: <number>

## Slide 47: Determine Duration of UH
<number>
The duration of the derived unit hydrograph is found by examining the precipitation for the event and determining that precipitation which is in excess.
This is generally accomplished by plotting the precipitation in hyetograph form and drawing a horizontal line such that the precipitation above this line is equal to the depth of excess precipitation as previously determined.
This horizontal line is generally referred to as the -index and is based on the assumption of a constant or uniform infiltration rate.
The uniform infiltration necessary to cause 1.65 inches of excess precipitation was determined to be approximately 0.2 inches per hour.
Notes: <number>

## Slide 48: Estimating Excess Precip.
<number>
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
Time (hrs.)
Precipitation (inches)
Uniform loss rate of
0.2 inches per hour.
Notes: <number>

## Slide 49: Excess Precipitation
<number>
Notes: <number>

## Slide 50: Changing the Duration
<number>
Very often, it will be necessary to change the duration of the unit hydrograph.
If unit hydrographs are to be averaged, then they must be of the same duration.
Also, convolution of the unit hydrograph with a precipitation event requires that the duration of the unit hydrograph be equal to the time step of the incremental precipitation.
The most common method of altering the duration of a unit hydrograph is by the S-curve method.
The S-curve method involves continually lagging a unit hydrograph by its duration and adding the ordinates.
For the present example, the 6-hour unit hydrograph is continually lagged by 6 hours and the ordinates are added.
Notes: <number>

## Slide 51
<number>

## Slide 52
<number>

## Slide 53
<number>

## Slide 54: Develop S-Curve
<number>
Notes: <number>

## Slide 55: Convert to 1-Hour Duration
<number>
To arrive at a 1-hour unit hydrograph, the S-curve is lagged by 1 hour and the difference between the two lagged S-curves is found to be a 1 hour unit hydrograph.
However, because the S-curve was formulated from unit hydrographs having a 6 hour duration of uniformly distributed precipitation, the hydrograph resulting from the subtracting the two S-curves will be the result of 1/6 of an inch of precipitation.
Thus the ordinates of the newly created 1-hour unit hydrograph must be multiplied by 6 in order to be a true unit hydrograph.
The 1-hour unit hydrograph should have a higher peak which occurs earlier than the 6-hour unit hydrograph.
Notes: <number>

## Slide 56: Final 1-hour UH
<number>
Notes: <number>

## Slide 57: Shortcut Method
<number>
There does exist a shortcut method for changing the duration of the unit hydrograph if the two durations are multiples of one another.
This is done by displacing the the unit hydrograph.
For example, if you had a two hour unit hydrograph and you wanted to change it to a four hour unit hydrograph.
Notes: <number>

## Slide 58: Shortcut Method Example
<number>
First, a two hour unit hydrograph is given and a four hour unit hydrograph is needed.
There are two possibilities, develop the S - curve or since they are multiples use the shortcut method.
Notes: <number>

## Slide 59: Shortcut Method Example
<number>
The 2 hr-UH is then displaced by 2 hours.
This is done because the 2 hr-UH will be used to represent
a 4 hr-UH.
Notes: <number>

## Slide 60: Shortcut Method Example
<number>
These two hydrographs are then summed.
Notes: <number>

## Slide 61: Shortcut Method Example
<number>
Finally the summed hydrograph is divided by two.
This is done because when two unit hydrographs are added, the area under the curve is two units. This has to be reduced back to one unit of runoff.
Notes: <number>

## Slide 62: Average Several UH’s
<number>
It is recommend that several unit hydrographs be derived and averaged.
The unit hydrographs must be of the same duration in order to be properly averaged.
It is often not sufficient to simply average the ordinates of the unit hydrographs in order to obtain the final unit hydrograph. A numerical average of several unit hydrographs which are different “shapes” may result in an “unrepresentative” unit hydrograph.
It is often recommended to plot the unit hydrographs that are to be averaged. Then an average or representative unit hydrograph should be sketched or fitted to the plotted unit hydrographs.
Finally, the average unit hydrograph must have a volume of 1 inch of runoff for the basin.
Notes: <number>

## Slide 63: Synthetic UHG’s
<number>
Snyder
SCS
Time-area
IHABBS Implementation Plan :
NOHRSC Homepage
http://www.nohrsc.nws.gov/
http://www.nohrsc.nws.gov/98/html/uhg/index.html
Notes: <number>

## Slide 64: Snyder
<number>
Since peak flow and time of peak flow are two of the most important parameters characterizing a unit hydrograph, the Snyder method employs factors defining these parameters, which are then used in the synthesis of the unit graph (Snyder, 1938).
The parameters are Cp, the peak flow factor, and Ct, the lag factor.
The basic assumption in this method is that basins which have similar physiographic characteristics are located in the same area will have similar values of Ct and Cp.
Therefore, for ungaged basins, it is preferred that the basin be near or similar to gaged basins for which these coefficients can be determined.
Notes: <number>

## Slide 65: Basic Relationships
<number>
Notes: <number>

## Slide 66: Final Shape
<number>
The final shape of the Snyder unit hydrograph is controlled by the equations for width at 50% and 75% of the peak of the UH:
Notes: <number>

## Slide 67: SCS
<number>
Notes: <number>

## Slide 68: Dimensionless Ratios
<number>
Notes: <number>

## Slide 69: Triangular Representation
<number>
Notes: <number>

## Slide 70: Triangular Representation
<number>
The 645.33 is the conversion used for delivering 1-inch of runoff (the area under the unit hydrograph) from 1-square mile in 1-hour (3600 seconds).
Notes: <number>

## Slide 71: 484 ?
<number>
Comes from the initial assumption that 3/8 of the volume under the UHG is under the rising limb and the remaining 5/8 is under the recession limb.
Notes: <number>

## Slide 72: Duration & Timing?
<number>
L = Lag time
For estimation purposes :
Again from the triangle
Notes: <number>

## Slide 73: Time of Concentration
<number>
Regression Eqs.
Segmental Approach
Notes: <number>

## Slide 74: A Regression Equation
<number>
where : Tlag = lag time in hours
L = Length of the longest drainage path in feet
S = (1000/CN) - 10 (CN=curve number)
%Slope = The average watershed slope in %
Notes: <number>

## Slide 75: Segmental Approach
<number>
More “hydraulic” in nature
The parameter being estimated is essentially the time of concentration or longest travel time within the basin.
In general, the longest travel time corresponds to the longest drainage path
The flow path is broken into segments with the flow in each segment being represented by some type of flow regime.
The most common flow representations are overland, sheet, rill and gully, and channel flow.
Notes: <number>

## Slide 76: A Basic Approach
<number>
McCuen (1989) and SCS (1972) provide values of k for several flow situations (slope in %)
Sorell & Hamilton, 1991
Notes: <number>

## Slide 77: Triangular Shape
<number>
In general, it can be said that the triangular version will not cause or introduce noticeable differences in the simulation of a storm event, particularly when one is concerned with the peak flow.
For long term simulations, the triangular unit hydrograph does have a potential impact, due to the shape of the recession limb.
The U.S. Army Corps of Engineers (HEC 1990) fits a Clark unit hydrograph to match the peak flows estimated by the Snyder unit hydrograph procedure.
It is also possible to fit a synthetic or mathematical function to the peak flow and timing parameters of the desired unit hydrograph.
Aron and White (1982) fitted a gamma probability distribution using peak flow and time to peak data.
Notes: <number>

## Slide 78: Fitting a Gamma Distribution
<number>
Notes: <number>

## Slide 79: Time-Area
<number>
Notes: <number>

## Slide 80: Time-Area
<number>
Notes: <number>

## Slide 81: Time-Area
<number>
Notes: <number>

## Slide 82: Hypothetical Example
<number>
A 190 mi2 watershed is divided into 8 isochrones of travel time.
The linear reservoir routing coefficient, R, estimated as 5.5 hours.
A time interval of 2.0 hours will be used for the computations.
Notes: <number>

## Slide 83: Rule of Thumb
<number>
R - The linear reservoir routing coefficient can be estimated as approximately 0.75 times the time of concentration.
Notes: <number>

## Slide 84: Basin Breakdown
<number>
Notes: <number>

## Slide 85: Incremental Area
<number>
Notes: <number>

## Slide 86: Cumulative Time-Area Curve
<number>
Notes: <number>

## Slide 87: Trouble Getting a Time-Area Curve?
<number>
Synthetic time-area curve - The U.S. Army Corps of Engineers (HEC 1990)
Notes: <number>

## Slide 88: Instantaneous UHG
<number>
t = the time step used n the calculation of the translation unit hydrograph
The final unit hydrograph may be found by averaging 2 instantaneous unit hydrographs that are a t time step apart.
Notes: <number>

## Slide 89: Computations
<number>
Notes: <number>

## Slide 90: Incremental Areas
<number>
Notes: <number>

## Slide 91: Incremental Flows
<number>
Notes: <number>

## Slide 92: Instantaneous UHG
<number>
Notes: <number>

## Slide 93: Lag & Average
<number>
Notes: <number>

## Slide 94: Geomorphologic
<number>
Uses stream network topology and probability concepts
Law of Stream Numbers
range: 3-5
Law of Stream Lengths
range: 1.5-3.5
Law of Stream Areas
range:3-6
Notes: <number>

## Slide 95: Strahler Stream Ordering
<number>
1
1
1
1
1
1
2
2
3
2

## Slide 96: Probability Concepts
<number>
Water travels through basin, making transitions from lower to higher stream order
Travel times and transition probabilities can be approximated using Strahler stream ordering scheme
Obtain a probability density function analogous to an instantaneous unit hydrograph
Can ignore surface/subsurface travel times to get a channel-based GIUH

## Slide 97: GIUH Equations
<number>
Channel-based, triangular instantaneous unit hydrograph:
L in km, V in m/s, qp in hr-1, tp in hrs