## Slide 1: Review
<number>
Definition:
Reliability is the probability that a component or system will perform a required function for a given period of time when used under stated operating conditions.
Notes:
Reliability is concerned with the life of a system from a success/failure point of view.
Reliability is a “time” oriented quality characteristic.
Reliability is a probability which is a function of time.
The random variable used to measure reliability is the “time”-to-failure random variable, T.
Next…
How to measure reliability?

## Slide 2: Failure Distributions -- Reliability Measures
<number>
Overview
1. Probability Functions Representing Reliability
  1.1 Reliability Function
  1.2 Cumulative Distribution Function (CDF)
  1.3 Probability Density Function (PDF)
  1.4 Hazard Function
  1.5 Relationships Among R(t), F(t), f(t), and h(t)
2. Bathtub Curve
-- How population of units age over time
3. Summary Statistics of Reliability
  3.1 Expected Life (Mean time to failure)
  3.2 Median Life and Bα Life
  3.3 Mode
  3.4 Variance

## Slide 3: Probability Functions Representing Reliability
<number>
Reliability Function
Cumulative Distribution Function (CDF)
Probability Density Function (PDF)
Hazard Function
Relationships Among R(t), F(t), f(t), and h(t)

## Slide 4: Reliability Function
<number>
Definition:
Reliability function is the probability that an item is functioning at any time t.
Let T = “time”-to-failure random variable, reliability at time t is
For example, reliability at time t=100s is
R(100) = P(T >= 100)
Properties:

## Slide 5: Reliability Function
<number>
Two interpretations:
R(t) is the probability that an individual item is functioning at time t
R(t) is the expected fraction of the population that is functioning at time t for a large population of items.
Other names:
Survivor Function -- Biostatistics
Complementary CDF

## Slide 6: CDF and PDF
<number>
Cumulative Distribution Function, F(t)
F(t)= P(T<t) =1-R(t)
Properties:
Interpretation:
F(t) is the probability that an item fails before time t.
Probability Density Function, f(t)
Properties:
Interpretation:
f(t) indicates the likelihood of failure for any t, and it describes the shape of the failure distribution.

## Slide 7: Relationships Among R(t), F(t), and f(t)
<number>
t
T
P(T>=t)
P(T<t)

## Slide 8: Relationships Among R(t), F(t), and f(t)
<number>

## Slide 9: Examples
<number>
Example 1
Consider the pdf for the uniform random variable given below:
where t is time-to-failure in hours. Draw the pdf, cdf and the reliability function.
Solution
T
f(t)
1/100
100
pdf
f(t)
1/100
100
Cdf & R(t)

## Slide 10: Examples
<number>
Example 2
Given the probability density function
where t is time-to-failure in hours and the pdf is shown below:
Graph the cdf and the reliability function.
Solution

## Slide 11: Examples
<number>
Example 3
For the reliability function
where t is time-to-failure in hours.
  What is the 200 hr reliability?
  What is the 500 hr reliability?
  If this item has been working for 200 hrs, What is the reliability of 500 hrs?
Solution

## Slide 12: Examples
<number>
Example 4
Given the following time to failure probability density function (pdf):
where t is time-to-failure in hours. What is the reliability function?
Solution

## Slide 13: Examples
<number>
Example 5
Given the cumulative distribution function (cdf):
where t is time-to-failure in hours.
What is the reliability function?
What is the probability that a device will survive for 70 hr?

## Slide 14: Hazard Function
<number>
Motivation for Hazard Function
It is often more meaningful to normalize with respect to the reliability at time t, since this indicates the failure rate for those surviving units. If we add R(t) to the denominator, we have the hazard function or “instantaneous” failure rate function as

## Slide 15: Hazard Function
<number>
Notes:
For small Δt values,
which is the conditional probability of failure in the time interval from t to t+ Δt given that the system has survived to time t.

## Slide 16: Hazard Function
<number>
Notes (cont.):
The shape of the hazard function indicates how population of units is aging over time
  Constant Failure Rate (CFR)
  Increasing Failure Rate (IFR)
  Decreasing Failure Rate (DFR)
Some reliability engineers think of modeling in terms of h(t)
Other Names for Hazard Function
Reliability: hazard function/hazard rate/failure rate
Actuarial science: force of mortality/force of decrement
Vital statistics: age-specific death rate

## Slide 17: Hazard Function
<number>
Various Shapes of Hazard Functions and Their Applications
Shapes of Hazard Functions | Applications
Constant Failure Rate (CFR) | Failures due to completely random or chance events It should dominate during the useful life period
Increasing Failure Rate (IFR) | The most likely situation Items wear out or degrade with time
Decreasing Failure Rate (DFR) | Less common situation Burn-in period of a new product
Bathtub-shape Failure Rate (BT) | Typical shape of many products

## Slide 18: Plots of R(t), F(t), f(t), h(t) for the normal distribution
<number>
R(t) f(t)
F(t) h(t)

## Slide 19: Relationships Among R(t), F(t), f(t), and h(t)
<number>

## Slide 20: Relationships Among R(t), F(t), f(t), and h(t)
<number>
One-to-One Relationships
Between Various Functions
Notes: The matrix shows that any of the three other probability functions (given by the columns) can by found if one of the functions (given by the rows) is known.
 | f(t) | R(t) | F(t) | h(t)
f(t) | . |  |  | 
R(t) |  | . |  | 
F(t) |  |  | . | 
h(t) |  |  |  | .

## Slide 21: Examples
<number>
Example 6
Consider the pdf used in Example 2 given by
Calculate the hazard function.
Solution

## Slide 22: Examples
<number>
Example 7
Given h(t)=18t, find R(t), F(t), and f(t).
Solution

## Slide 23: Bathtub Curve
<number>
The failure of a population of fielded products is due to
Problems due to inherent design weakness.
The manufacturing and quality control related problems.
The variability due to the customer usage.
The maintenance policies actually practiced by the customer and improper use or abuse of the product.

## Slide 24: Bathtub Curve
<number>
Over many years, and across a wide variety of mechanical and electronic components and systems, people have calculated empirical population failure rates as units age over time and repeatedly obtained a bathtub shape:
Infant mortality (burn-in) period: decreasing failure rate early in the life cycle
Constant failure rate (useful life) period: nearly constant failure rate
Wear-out period: the failure rate begins to increase as materials wear out and degradation failures occur at an ever increasing rate.

## Slide 25: Bathtub Curve
<number>

## Slide 26: Bathtub Curve
<number>
An Example: Accident Rates and Age
16-19 20-24 25-29 60-64 65-69 70-74 …
Age
Annual Rate of
Accidents
Young drivers
Seniors

## Slide 27: Bathtub Curve
<number>
Typical information for components of a PC
Component | Infant Mortality Rate | Typical useful life period (years) | Likelihood of Failure Before Wearout
Power Supply | Low | 3-6 | Moderate
Motherboard | Moderate | 4-7 | Low
Processor | Low | 7+ | Very Low
System Memory | Moderate to High | 7+ | Very Low
Video Card | Low to Moderate | 5-7 | Low
Monitor | Low to Moderate | 5-7+ | Moderate to High
Hard Disk Drive | Moderate to High | 3-5 | Moderate to High
Floppy Disk Drive | Low | 7+ | Low
CD-ROM Drive | Moderate | 3-5 | Moderate
Modem | Low | 5-7+ | Low
Keyboard | Very Low | 3-5 | Moderate
Mouse | Very Low | 1-4 | Moderate to High

## Slide 28: Summary Statistics of Reliability
<number>
Expected Life (Mean time to failure)
Median Life and Bα Life
Mode
Variance

## Slide 29: Expected Life
<number>
E[T] is also called:
Mean Time to Failure (MTTF) for nonrepairable items
Mean Time between Failure (MTBF) for repairable items that can be completely renewed by repair
E[T] is a measure of the central tendency or average value of the failure distribution, and it is known as the center of gravity in physics.

## Slide 30: Expected Life
<number>
Relationship between E[T] and R(t):
Show that E(T) can be re-expressed as
Sometimes, one expression is easier to integrate than the other  exponential example, how?

## Slide 31: Examples
<number>
Example 8
Given that
What is the MTTF?
Solution

## Slide 32: Examples
<number>
Example 9
Given that
what is the MTTF?

## Slide 33: Median Life and Bα Life
<number>
The median life, B50, divides the distribution into two equal halves, with 50% of the failure occurring before and after B50.
Bα Life is the time by which α percent of the items fail.
For example, B10 life can be calculated by

## Slide 34: Mode and Variance
<number>
Mode is the time value at which the probability density function achieves a maximum.
Mode is the most likely observed failure time.
Variance

## Slide 35: Examples
<number>
Example 9
Consider the pdf used in Example 2 (triangle distribution) given by
Calculate the MTTF, the B50 life (the median life), and the mode.

## Slide 36: Examples
<number>
Example 10
For the exponential distribution with mean=100, calculate the B50 life (the median life), and the mode.