## Slide 1: Time-Dependent Failure Models
<number>
Probability models used to describe
non-constant failure rate processes
Overview
Weibull Distribution
  Probability Functions
  Characteristics of Weibull Distribution
  MTTF, Variance, Median and Mode
  Conditional Reliability
Normal Distribution
  Probability Functions
  Mean, Variance and Moments
  Central Limit Theorem
Lognormal Distribution
  Probability Functions
  Mean, Variance

## Slide 2: Weibull Distribution
<number>
Weibull distribution can attain many shapes for various values of shape parameter β.
It can model a great variety of data and life characteristics, including constant, increasing, and decreasing failure rates (CFR, IFR, and DFR).
Therefore, it is one of the most widely used lifetime distributions in reliability engineering.
Two-Parameter Weibull Distribution:
β = shape parameter, or slope parameter
θ = scale parameter, or characteristic life parameter

## Slide 3: Probability Functions
<number>
CFR, IFR, DFR
↓
Hazard Function
↓
Reliability Function
↓
Cumulative Distribution Function
↓
Probability Density Function

## Slide 4: Characteristics of Weibull Distribution
<number>
Characteristic Effects of Shape (Slope) Parameter, β
  Effects of β on Weibull Hazard Function
  (CFR, IFR, DFR depending on the value of β )
  Effects of β on Weibull PDF
  Effects of β on Weibull Reliability Function
Characteristic Effects of Scale Parameter, θ

## Slide 5: Effects of β on Weibull Hazard Function
<number>

## Slide 6: Effects of β on Weibull Hazard Function
<number>
All three life stages of the bathtub curve can be modeled with the Weibull distribution and varying values of β:
β < 1: DFR
β = 1: CFR (Exponential distribution)
β > 1: IFR
  1< β < 2, the h(t) curve is concave
   the failure rate increases at a decreasing rate as t increases
  β = 2, a straight line relationship between h(t) and t
  β > 2, the h(t) curve is convex
   the failure rate increases at an increasing rate as t increases

## Slide 7: Effects of β on Weibull Hazard Function
<number>
Value |  | Property | Application
0<β<1 |  | DFR (pdf is similar to Exponential Dist.) | Model infant mortality
β =1 |  | CFR (pdf is Exponential Dist.) | Model useful life
β >1 | 1< β <2 | IFR (hazard function is concave) | Model wearout
 | β =2 | LFR (hazard function is linearly increasing) (pdf is Rayleigh distribution) | 
 | β >2 | IFR (hazard function is convex) | 
 | 3≤β≤4 | IFR (pdf approaches normal, symmetrical) | 

## Slide 8: Effects of β on Weibull PDF
<number>

## Slide 9: Effects of β on Weibull PDF
<number>
0 < β < 1:
As t 0, f(t) ∞.
As t ∞, f(t) 0.
f(t) decreases monotonically as t increases
f(t) is convex
The mode is non-existent.
β = 1:
exponential distribution
β > 1:
f(t) = 0 at t = 0
f(t) increases as t approaches to the mode and decreases thereafter
1<β < 2.6, f(t) is positively skewed  right tail
2.6 < β < 3.7, its coefficient of skewness approaches zero no tail, approximate the normal pdf,
β > 3.7, f(t) is negatively skewed  left tail

## Slide 10: Effects of β on Weibull Reliability Function
<number>

## Slide 11: Effects of β on Weibull Reliability Function
<number>
0 < β < 1, R(t) decreases sharply and monotonically, and is convex.
β = 1, R(t) decreases monotonically but less sharply than for 0 < β < 1, and is convex.
β > 1, R(t) decreases as t increases. As wear-out sets in, the curve goes through an inflection point and decreases sharply.

## Slide 12: Scale Parameter, θ
<number>
The scale parameter influences both the mean and the spread of the Weibull distribution.
All Weibull reliability functions pass through the point (θ, 0.368).
θ is also called characteristic life.
θ has the same units as T, such as hours, miles, cycles, actuations, etc.

## Slide 13: Effects of θ on Weibull PDF
<number>
Increasing the value of θ has the effect of stretching out the pdf
 influences both mean and spread
Since the area under a pdf curve is a constant value of one, the “peak'' of the pdf curve will also decrease with the increase of θ

## Slide 14: Examples (Weibull Dist.)
<number>
Example 1
A two-speed synchronized transfer case used in a large industrial dump truck experiences failures that seem to be well approximated by a two parameter Weibull distribution with
(1) Characterized the failure process based on the values of θ and β.
(2) What is the 10,000 km reliability?
(3) What is the 24,000 km reliability?

## Slide 15: Examples (Weibull Dist.)
<number>
Example 1 (Cont.)
A two-speed synchronized transfer case used in a large industrial dump truck experiences failures that seem to be well approximated by a two parameter Weibull distribution with
(4) What is the B10 life? (km at which 10% of the population will fail, or 90% reliability is desired.)
(5) If the Weibull slope can be changed to by changing the synchronizer gear tooth design, how will this affect the above answers?

## Slide 16: Examples (Weibull Dist.)
<number>
Example 2
The characteristic life for a highly turbocharged diesel engine in a military application is 1,800 miles with a Weibull slope of 1.97. What is the B10 life?

## Slide 17: Examples (Weibull Dist.)
<number>
Example 3
A device that shows running-in failure pattern, has threshold time to failure of 150 days and characteristic life of 100days. What is the probability that this device will fail before 200 days of running times? What is the probability that this device will survive for 180days? What is the age-specific failure rate at 180 days? (Hint: the shape factor in this case could be one of the following; 1.2 ,0.5, 4.5)

## Slide 18: MTTF and Variance
<number>
where is the gamma function:
To obtain the gamma function, use Standard Table in the textbook, and

## Slide 19: Median and Mode
<number>
Design Life and Bα Life
Median
Mode

## Slide 20: Conditional Reliability
<number>
Conditional reliability is useful in describing the reliability of an item following a burn-in period or after a warranty period, T0.
For Weibull distribution, the conditional reliability is
R(t | T0) = R(t) for all t if and only if R(t) is exponential.

## Slide 21: Burn-In
<number>
Early failures (infant mortality) – common “reliability” problem, esp. in electronic equipment  usually caused by manufacturing “defects”--- quality problems. Problems are typically common in “new” products and may disappear as technology matures.
Ideal  build-in Q&R upfront and reduce such problems – but hard to do with complex technology and pressure to reduce product development cycle time.
To achieve reliability goals and reduce field-failure, common practice to “burn-in” components and systems to screen out units that would fail early – esp. important in safety-critical applications  can be viewed as a type of 100% inspection.
Done at use condition or low-level stress environment to avoid undue aging of components and systems.
Burn-in is expensive  incorporate costs and benefits and decide on optimal trade-off

## Slide 22: Examples (Weibull Dist.)
<number>
Example 4
Given a Weibull distribution with a characteristic life of 127,000 hr and a slope of 3.74, find the mean and standard deviation. Also find the probability of surviving the mean life.
Solution

## Slide 23: Examples (Weibull Dist.)
<number>
Example 4
For the two-speed synchronized transfer case problem in Example 1, we have two designs. Find the mean and standard deviation of the life.
A:
Solution
B:

## Slide 24: Normal (Gaussian) Distribution
<number>
Normal distribution is not a true reliability distribution since the random variable ranges from minus infinity to plus infinity.
When the probability that the random variable takes on negative values is negligible, the normal distribution can be used successfully to model fatigue and wear out phenomena.
It will be used to analyze lognormal distribution.

## Slide 25: Probability Density Function
<number>
For T ~ N(μ, σ2), the PDF is:
μ is the location parameter
 shifts the graph left or right on the horizontal axis
σ2 is the scale parameter
 stretches or compresses the graph
where is the pdf for standard normal distribution (μ=0, σ2=1).

## Slide 26: CDF and Reliability Function
<number>
F(t) R(t)
Cumulative Distribution Function, F(t)
where is the cdf for standard normal distribution (μ=0, σ2=1).
Reliability Function, R(t)

## Slide 27: Hazard Function
<number>
h(t) is an increasing function
 the normal distribution can only be used to model wear-out (IFR) phenomena.

## Slide 28: Examples of Normal Distributions
<number>

## Slide 29: Mean, Variance and Moments
<number>
Mean and Variance
Moments of Normal Distribution

## Slide 30: Central Limit Theorem
<number>
If X1, X2, …, Xn is a random sample of size n taken from a population (either finite or infinite) with mean μ and finite variance σ2, and if is the sample mean, as the sample size n approaches to infinite,
The central limit theorem basically states:
  The sampling distribution of the mean becomes approximately normal regardless of the distribution of the original population.
  The sampling distribution of the mean is centered at the population mean, μ.
  The standard deviation of the sampling distribution of the mean approaches .
Due to the central limit theorem, the normal distribution plays a central role in classical statistics.

## Slide 31: Examples (Normal)
<number>
Example 1
A component has a normal distribution of failure times with μ =20,000 cycles and σ =2,000 cycles. Find the reliability of the component and the hazard function at 19,000 cycles.

## Slide 32: Lognormal Distribution
<number>
The lognormal distribution is used extensively in reliability applications to model failure times. (The lognormal and Weibull distributions are the most commonly used distributions in reliability applications.)
Like the Weibull distribution, the lognormal can take a variety of shapes.
The relationship between lognormal distribution and normal distribution is very useful in analyzing the lognormal distribution.

## Slide 33: Lognormal Distribution
<number>
If then
with Probability Density Function
μ is the mean of ln(T), and
σ2 is the variance of ln(T), and
 | Lognormal T | Normal Ln(T)
Mean |  | 
Variance |  | 
Median |  | 
Mode |  | 

## Slide 34: Lognormal Distribution
<number>
PDF and CDF
Reliability Function
Hazard Function
where and are the pdf and cdf for standard normal distribution (μ=0, σ2=1).

## Slide 35: Examples of Lognormal Distribution
<number>

## Slide 36
<number>
The lognormal distribution is a distribution skewed to the right.
The pdf starts at zero, increases to its mode, and decreases thereafter.
The degree of skewness increases as σT increases.
σT=0.5
σT=1.5

## Slide 37: Examples (Lognormal)
<number>
Example 1
The failure time of a certain component is log-normally distributed with .
Find the reliability of the component and the hazard rate for a life of 150 time units.
Find the mean and variance of the failure time of the component.