## Slide 1
Industrial Engineering
Maintainability & Availability

## Slide 2
Maintainability Definition
Maintainability implies a built in characteristics of the equipment design which imparts to the cell an inherent ability to be maintained so as to keep the equipment productively operating by employing a minimum number of maintenance man-hour, skill levels, and maintenance costs.
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 3
Maintainability
Various measures are used in maintainability analysis:
  Mean Time To Repair (MTTR)
  Mean Preventive Maintenance Time ( MPMT)
  Mean Maintenance Downtime (MMD)
In addition to these measures, maintainability functions are used to predict the probability that a repair, starting at time t =0, will be completed in a time t.
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 4
Maintainability
It measures the elapsed time required to perform a given maintenance activity.
MTTR is expressed by:
MTTR = ( ∑ λi CMTi ) / ∑ λi
Where:
k = number of units or parts
λi = failure rate of unit/part i , for i= 1, 2, 3, .....k
CMTi = Corrective Maintenance or repair Time required to repair unit or part i, for i= 1, 2, 3, ....., k
Usually, times to repair follow exponential, lognormal, and normal probability distributions
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 5
Maintainability
The mean preventive maintenance time is defined by:
MPMT = (∑ FPMi x ETPMTi) / ∑ FPMi
Where:
MPMT = Mean Preventive Maintenance Time
m = total number of preventive maintenance tasks
FPMi = Frequency of Preventive Maintenance task i, for i = 1, 2, 3, ....., m
ETPMTi = Elapsed Time for Mreventive Maintenance Task i, for i= 1, 2, 3, ....., m
Note that if the frequencies FPMi are given in maintenance task per hour, then ETPMTi should also be given in hours.
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 6
Maintainability
Mean maintenance downtime (MMD) is described as the total time required either to restore system to a given performance level or to keep it at that level of performance.
It is composed of corrective maintenance, preventive maintenance, administrative delay, and logistic delay times.
The administrative delay time is the system or item downtime due to administrative constraints.
Logistic delay time is the time spent waiting for a required resource such as spare part, a specific test, or a facility
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 7
Maintainability
MMD = MAMT + LDT + ADT
Where:
ADT = Administrative Delay Time
LDT = Logistic Delay Time
MAMT = Mean Active Maintenance Time or mean time needed to perform preventive and corrective maintenance associated tasks.
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 8
Maintainability Functions
Maintainability functions predict the probability that a repair, starting at time t = 0, will be completed in a time t.
The maintainability function for any distribution is defined by:
M(t) = ∫ ƒr (t) dt
Where:
t = time
M(t) = maintainability function (probability that a repair action will be finished at time t)
ƒr(t) = probability density function of the repair time
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 9
Maintainability Functions
Exponential p.d.f:
Exponential p.d.f is widely used in maintainability work to represent repair times. It is expressed by:
ƒr(t) = (1/MTTR) exp (-t/MTTR)
The maintainability function in this case is:
M(t) = ∫ (1/ MTTR) exp (- t/ MTTR) dt
= 1- exp (- t/ MTTR)
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 10
Maintainability Functions
Weibull p.d.f:
Weibull p.d.f can also be used to represent times to repair. It is defined by:
ƒr(t) = (β/θ) t exp (- (t / θ))
where:
β = shape parameter θ = scale parameter
The maintainability function in this case is:
M(t) = ∫ (β/ θ ) t exp (- (t / θ) ) d
= 1- exp (- (t / θ) )
When β= 1 and θ= MTTR , the M(t) reduces to the M(t) in the case of exponential distribution
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 11
Maintainability Functions
Normal p.d.f:
Normal p.d.f can also be used to represent times to repair. It is defined by:
ƒr(t) = 1/σ √ 2 π exp (- 1/2(t – θ/ σ)²)
where:
σ = standard deviation of the variable maintenance time t around the mean value θ
θ = mean of maintenance times
The maintainability function in this case is:
M(t) = 1/σ √ 2 π ∫ exp (- 1/2(t – θ/ σ)²) dt
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 12
Maintainability Functions
The mean of the maintenance times is:
θ = ∑ ti / k
where:
k = total number of maintenance tasks performed
ti = ith maintenance time, for i= 1, 2, 3, ...... K
The standard deviation is :
σ = [ ∑ (ti – θ)²/ (k – 1)]½
Maintainability
Maintainability Functions
Examples
Industrial Engineering

## Slide 13
Availability
Industrial Engineering
Maintainability
Maintainability Functions
Availability
Availability is the probability that a facility scheduled for service will be operating at any point in time.
System availability predicts the actual running or uptime in terms of ratio of actual operating time to the scheduled operating time:
Availability = Actual operating time / Standard Operating Time

## Slide 14
Availability
Industrial Engineering
Maintainability
Maintainability Functions
Availability
Availability = MTBF or MTTF / (MTBF or
MTTF + MFOT or MTTR)

## Slide 15
Availability
Industrial Engineering
Maintainability
Maintainability Functions
Availability
This means an increase in maintainability (results in small MTTR) or reliability (results in a high MTBF or MTTF) or both increases the availability of the system.
Therefore, sound design provides both high reliability and maintainability.

## Slide 16
Example
A mechanical machine has three important subsystems. The first subsystem has failure rate of 0.003 failures per hour and repair time of 1 hour. The second and the third subsystems have failure rates of 0.005 and 0.004 failures per hour and repair times of 4 hours and 3 hours respectively. The times to repair of this machine are exponentially distributed. Find:
The probability that a repair on this machine will be performed in 5 hours.
The MTTR of this machine
The MMD of this machine, if the authorization of the maintenance work order takes 12 min and the time to get the required materials and spare parts from the store is 20 min
Industrial Engineering
Maintainability
Maintainability Functions
Examples