## Slide 1
Maintenance Capacity Planning
Industrial Engineering

## Slide 2
Maintenance Capacity Planning
Maintenance capacity planning is performed to determine the optimal level of resources required to meet the forecasted maintenance load
Maintenance Capacity planning procedures:
  Determine the total maintenance load
  Estimate the required spare parts and material to meet the load
  Determine the equipment and tools necessary for all types of maintenance work
  Determine the skills and the number of workers for each skill
  Provide special plans for highly computerized equipment
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 3
Maintenance Capacity Planning
Four basic strategies are used to match the fixed capacity with fluctuating monthly maintenance demands:
  1. Chase strategy: performing the exact amount of maintenance workload required for each month, without advancing or delay
  2. Levelling strategy: the peaks of demand are distributed to periods of lower demand, aiming to have a constant level of monthly maintenance activity
  3. Demand management: the maintenance demand itself is levelled by distributing preventive maintenance equally among all periods
  4. Subcontracting: regular employees perform a constant level of monthly maintenance activity, leaving any excess workload to contractors
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 4
Maintenance Capacity Planning
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering
The Extremes
Level Strategy
Chase Strategy
Production equals demand
Production rate is constant

## Slide 5
Maintenance Capacity Planning
Sources of Craftsmen
  Regular workers
  Overtime in-house workers
  Contract maintenance workers
The best mix is determined by using cost and availability measures
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 6
Capacity Planning Techniques
Capacity Planning Techniques
  Deterministic models
  Stochastic models
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 7
Capacity Planning Techniques
Deterministic models:
Assumes the following are fixed constants:
  Forecasted maintenance load
  Standard times
  Other variables
Types of deterministic techniques:
  Heuristic tableau method
  Linear programming
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 8
Capacity Planning Techniques
Stochastic models :
Assumes the following are random variables with certain probability distributions:
  Forecasted maintenance load
  Standard times
  Other variables
Types of deterministic techniques:
  Queuing models.
  Stochastic discrete event simulation
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 9
Capacity Planning Techniques
Heuristic Tableau Method
For each maintenance craft, the required capacity is given by the forecasted workload for each period. The available capacity for each period is given by the quantity of available resources of different categories. Each of these categories, such as regular time, overtime, and subcontract, has its own cost.
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 10
Capacity Planning Techniques
Heuristic Tableau Method
Principles and guidelines:
  Maintenance work load is classified into grades according to the skill the work requires and the priority of the work.
  All priority work is performed by regular in-house workers as much as possible.
  If it is not possible to satisfy grade 1 work by regular in-house workers, use overtime.
  No backlog is allowed for grade 1 work.
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 11
Capacity Planning Techniques
Heuristic Tableau Method...
  The staffing level must be determined based on the average maintenance load with a healthy backlog from grade 2 work carried out into the system.
  The grade 2 work can be met with overtime or contract maintenance.
  The overtime capacity is at most 25% of the regular in-house capacity.
  The maximum for backlog is 100 man-hours. If the backlog exceeds this limit, subcontracting is utilized and it is assumed that subcontracting can provide as much capacity as needed.
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 12
Capacity Planning Techniques
Steps of Heuristic Tableau Method
  FMt = Total forecasted Maintenance load.
  Bt-1 = Maintenance workload backlog from period t-1
  TMt = Total Maintenance workload for period t;
  TMt = FMt + Bt-1
  TM i,t = Total Maintenance workload of grade i in period t, i=1,2 as needed.
  RM i,t = Regular in-house capacity for Maintenance workload of grade i in period t
  OM i,t = Overtime capacity for Maintenance workload of grade i in period t
  CM i,t = Contract capacity for Maintenance work of grade i in period t
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 13
Capacity Planning Techniques
Steps of Heuristic Tableau Method
  Cr = Hourly cost of trade on regular time
  Co = Hourly cost of trade on overtime
  Cs = Hourly cost of subcontracting
  Bt = Backlog in man-hours at the beginning of period t
  CRt = Capacity of in-house regular time in period t
  COt = Capacity of in-house overtime in period t
  CSt = Capacity of subcontracting in period t
  FMt = Forecasted maintenance load in period t
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 14
Capacity Planning Techniques
Steps of Heuristic Tableau Method
  The transportation tableau in shows the setup for a three-period planning horizon, with three resources for maintenance work in each period (m = R: regular time, m = O: overtime, m = S: subcontract). Assigning an infinite cost (∞) prohibits assigning any maintenance work to the given (i, j) cell.
  After the modified transportation tableau is constructed, it is solved by the least-cost assignment heuristic. This heuristic assigns as much as possible (the minimum of supply and demand) to the available (unassigned) cell with the least cost. After each assignment, the supply and demand for the given cell are updated, and the process continues until all demands have been assigned. Although this technique does not guarantee an optimum solution, it is an effective heuristic that frequently leads to optimum solutions.
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 15
Capacity Planning Techniques
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering
Periods | Period Sources | 1 | 2 | 3 | Capacity
1 | Regular Time | Cr |  |  | CR1
 | Overtime | Co |  |  | CO1
 | Subcontract | Cs |  |  | CS1
2 | Regular Time | Cr +  | Cr |  | CR2
 | Overtime | Co +  | Co |  | CO2
 | Subcontract | Cs +  | Cs |  | CS2
3 | Regular Time | Cr + 2 | Cr +  | Cr | CR3
 | Overtime | Co +2 | Co + | Co | CO3
 | Subcontract | CS + 2 | Cs + | Cs | CS3
 | Maintenance load | M1 | M2 | M3 | 

## Slide 16
Example
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering

## Slide 17
Example
Maintenance Capacity Planning
Capacity Planning Techniques
Example
Industrial Engineering