## Slide 1
Maintenance Performance Measures
Management needs information of maintenance performance for planning and controlling the maintenance process. The information needs to focus on the effectiveness and efficiency of the maintenance process, its activities, organization, cooperation and coordination with other units of the organization.
Maintenance Performance Measurement (MPM) is the multidisciplinary process of measuring and justifying the value created by maintenance investment, and taking care of the organization’s stockholder’s requirements viewed strategically from the overall business perspective.
Maintenance Performance
OEE
Example
Industrial Engineering

## Slide 2
Maintenance Performance Measures
Maintenance productivity aims at minimizing the maintenance cost dealing with the measurement of overall maintenance results/performance and maximizing the overall maintenance performance
Some of the important measures of maintenance productivity are:
Total cost of maintenance/total production cost;
A (availability)
Mean time to repair (MTTR)
Mean time between failure (MTBF)
Overall Equipment Effectiveness (OEE)
Maintenance Performance
OEE
Example
Industrial Engineering

## Slide 3
Maintenance Performance Measures
  (OEE) is a way to monitor and improve the efficiency of your manufacturing process.
  OEE has become an accepted management tool to measure and evaluate plant floor productivity.
  OEE is broken down into three measuring metrics of Availability, Performance, and Quality.
  OEE = Availability x Performance x Quality
Maintenance Performance
OEE
Example
Industrial Engineering

## Slide 4
Maintenance Performance Measures
  Availability = Run Time / Total Time
  = Operating Time / Planned Production Time
  Percentage of the actual amount of production time the machine is running to the production time the machine is available.
  The total run time of the machine subtracting all unplanned downtime
  Scheduled maintenance, planned downtime events, or equipment trials are not considered to be part of the time that machines are available for production
Maintenance Performance
OEE
Example
Industrial Engineering

## Slide 5
Maintenance Performance Measures
  Performance = Total Count / Target Count
  = Ideal Cycle Time / Operating Time
  = Ideal Cycle Time / (Operating Time / Total Pieces)
  =(Total Pieces / Operating Time)/Ideal Run time
  Percentage of total parts produced on the machine to the production rate of machine.
  How well a machine is running when it is running
Maintenance Performance
OEE
Example
Industrial Engineering

## Slide 6
Maintenance Performance Measures
  Quality = Good Count / Total Count
  Percentage of good parts out of the total parts produced on the machine.
  How many good parts versus bad parts a machine has produced
Maintenance Performance
OEE
Example
Industrial Engineering

## Slide 7
Maintenance Performance Measures
Maintenance Performance
OEE
Example
Industrial Engineering
OEE Loss Category | OEE Metric | Loss Category Examples
Down Time Losses | Availability | 1. Equipment Failures 2. Tooling Damage 3. Unplanned Maintenance 4. Process Warm Up 5. Machine Changeovers 6. Material Shortage
Speed Losses | Performance | 1. Product Misfeeds 2. Component Jams 3. Product Flow Stoppage 4. Level of Machine Operator Training 5. Equipment Age 6. Tooling Wear
Quality Losses | Quality | 1. Tolerance Adjustments 2. Warm Up Process 3. Damage 4. Assembled Incorrectly 5. Rejects 6. Rework

## Slide 8
Maintenance Performance Measures
Maintenance Performance
OEE
Example
Industrial Engineering
  Calculate OEE for the following machine information

## Slide 9
Maintenance Performance Measures
Maintenance Performance
OEE
Example
Industrial Engineering
  Planned Production Time = [Shift Length - Breaks]
  = [480 - 60]= 420 minutes
  Operating Time = [Planned Production Time - Down Time]
  = [420 - 47] = 373 minutes
  Good Pieces = [Total Pieces - Reject Pieces]
  = [19,271 - 423] = 18,848 pieces

## Slide 10
Maintenance Performance Measures
Maintenance Performance
OEE
Example
Industrial Engineering