## Slide 1: Experiment 8 Cooling and Dehumidification
Shereef Sadek
ME 322

## Slide 2: Experiment 8 Cooling and Dehumidification
Refrigeration
  Refrigeration is the achievement of a temperature below that of the immediate surroundings [1].
  To maintain this lower temperature removal of heat from the product at low temperature and the discharge of this heat to a higher temperature is required.
Methods of Refrigeration
  Rise in temperature of coolant
  Change of phase
  Expansion of a liquid
  Steady Flow expansion of a perfect gas
  Emptying process
  Electrical process

## Slide 3: Experiment 8 Cooling and Dehumidification
Psychrometry
  Psychrometry is the study of the properties of mixture of air and water vapor.
  Psychrometry is important since air is almost always mixed with water vapor
  All air-conditioning processes must factor in the presence of water vapor
  Psychrometric charts facilitates the calculation of processes involving a mixture of air and water-vapor
  The coordinates of a Psychrometric chart are the water vapor pressure as the ordinate (y-axe) and the mixture temperature as the abscissa (x-axe).
  The left boundary of the char t is the water saturation line, the region to the right is called superheated water vapor

## Slide 4: Experiment 8 Cooling and Dehumidification

## Slide 5: Experiment 8 Cooling and Dehumidification

## Slide 6: Experiment 8 Cooling and Dehumidification
Relative humidity
Humidity Ratio
Wet bulb temperature
  The temperature indicated by a thermometer which has a wetted bulb in contact with blowing air.

## Slide 7: Experiment 8 Cooling and Dehumidification
  Nomenclature
Orifice differential head (mm H2O)
Specific volume of air calculated by assuming air to be a perfect gas.
Air mass flow rate in kg/sec
Specific humidity, kg/kg
Specific enthalpy
Refrigerant mass flow rate ,
Refrigerant enthalpies after and before the evaporator coil.

## Slide 8: Experiment 8 Cooling and Dehumidification
References
  Stoecker, W. F. “Refrigeration and Air Conditioning”. McGraw-Hill, 1958.