## Slide 1: Procedures
Fixation Tissues must be immersed in fixative immediately after removal from the body .
10% Neutral Buffered Formalin is the routine fixative.
Tissue Processing
Tissue processing consists of 3 steps:
1- Dehydration
2-Clearing
3- Infiltration ( lasting between 8 to 12 hours).
Tissue Embedding Embedding is enclosing the tissue in the infiltration medium (paraffin) used for processing and then allowing the medium to solidify.
Sectioning with a microtome The microtome advances the tissue block, toward a sharp knife. The tissue is moved in an up and down motion to cut the tissue into a preset number of micrometers. The paraffin and tissue shavings are shaved off like a ribbon.
Tissue Staining
Cover slipping, mounting.

## Slide 2
This processor uses Vacuum function to accelerate the speed of tissue processing for plant ,animal and human tissues automatically. It is accurate and easy to use and maintain.
The processing tissue:

## Slide 3: Embedding
Prepared by: Reem Aldossari

## Slide 4: TISSUE PROCESSING
The aim of tissue processing is to embed the tissue in a solid medium firm enough to support the tissue and give it sufficient rigidity to enable thin sections to be cut , and yet soft enough not to damage the knife or tissue.
Stages of processing:
1- Dehydration.
2- Clearing.
3- Infilteration.

## Slide 5: Dehydration
In the paraffin wax method, dehydration from aqueous fixatives is usually initiated in 60%-70% ethanol, progressing through 90%-95% ethanol, then two or three changes of absolute ethanol before proceeding to the clearing stage.

## Slide 6: Clearing
Makes tissue appear “clear”
Some clearing agents:
- xylene.
- Chloroform.
- Benzene.

## Slide 7: Infiltration
A. Replace xylene with paraffin
B. Immerse in melted paraffin
1. ~55o C MP
C. Remove all bubbles

## Slide 8: Embedding
is the process by which tissues are surrounded by a medium such as wax which when solidified will provide sufficient external support during sectioning.
Procedure
1. Place tissue cassette in melted paraffin
2. Fill mold with paraffin
3. Place tissue in mold
4. Allow to cool

## Slide 9: Tissue Embedding

## Slide 10: Precaution of embedding in wax
The wax must be clear
No dust particles must be present.
The wax must be rapidly cooled after tissue embedding to reduce wax crystallization.

## Slide 11
Sectioning with
Microtome
Prepared by : Jawahir algamdi

## Slide 12
Cutting The Specimen
using the Rotary microtome
A microtome to sectioning biological specimens a tissue sample into very thin slices (sections)
thicknesses varying from 2 - 25 micrometers thick.

## Slide 13
1. hand
2.safety lock
4.cutt knife (blade)
5.the knife holder
6.a specimen holder
7. Knife regulating rod for inclining angle
8.Knife fixing knob
9.Paraffin block fixing screw
10. Sectioning thickness regulating knob
Amicrotome has the essential machinery of a slicer:

## Slide 14: Sectioning
This is done with a microtome.
The most important necessity for proper sectioning is a very sharp knife
-Cut tissue sections from blocks (3 – 10 ųm)
-Floating out onto water (45°C)
-Sections flatten out, picked up onto glass slides.

## Slide 15
Sectioning

## Slide 16
2- Picking up sections
Floating sections onto slides Carefully arrange the sections in the center of the slide (that helps remove wrinkles)

## Slide 17
3-Microscope slide preparation:
Taking the section onto slide
Flat, no air bubbles, no stretch or breaks.
Taken on hot plate at 37˚C to dry .

## Slide 18
HAZARDS
1. Extremely sharp blades – all operations with the blade must be done with the greatest of care.
2.Whenever handling knives, use cut resistant gloves.
3.When mounted in the microtome, the knife can only be cleaned using a brush, cotton bud or swab.
4.All knives must be stored or disposed of safely when not in use. Standard knives are stored in their box, disposable and razor blades disposed of in a dedicated sharps container.
5.Knives are NEVER transported in the bare hand, even for the shortest distance

## Slide 19
Thank you