## Slide 1: Experiment 6

## Slide 2: Determination of Chloride by Volhard Method
Objective of this experiment:
(a) Determination of chloride in an unknown solution.
(b) Determination of chloride in an unknown salt.

## Slide 3
Principle:
*The chloride present in the unknown are precipitated by adding an excess amount of standard Silver Nitrate solution.
*The un reacted silver nitrate is determined by back titration with a standard solution of Potassium Thiocyanate using Ferric Ammonium Sulphate as indicator.
Ag+ + Cl‾ AgCl (white ppt)
Ag+ + SCN ‾ AgSCN (back titration)
Fe+ ++ + SCN ‾ FeSCN ++ (brown color) end point

## Slide 4
*The silver thiocyanate (AgSCN) is precipitated before the production of FeCNS because of the very small solubility product of the silver thiocyanate.
*Concentrated Nitric Acid is added to prevent hydrolysis of the Ferric Ammonium Sulphate which used as indicator.
Reagent:
1- Standard 0.1 N Silver Nitrate (AgNO3).
2- 0.1 N Potassium Thiocyanate (KSCN).
3- Con. Nitric Acid (HNO3).
4- Ferric Ammonium Sulphate.
5- Unknown solution of Chloride.

## Slide 5
Procedure:
I) Standardization of Potassium Thiocyanate (KSCN)
1- 20 ml AgNO3
2- 80 ml distilled water, mix well 3- 2 ml con.HNO3, mix well 4- 2 ml Ferric ammonium sulphate, mix well
5- Titrate with Potassium tiocyanate solution until get light brown color (end point).

## Slide 6
II) Titration of unknown solution of chloride
1- 5 ml unknown solution of chloride
2- 20 ml D.W, mix well
3- 10 ml AgNO3, mix well (note the white ppt)
4- 1 ml HNO3, mix well
5- 1 ml Ferric ammonium sulphate indicator, mix well
6- Titrate with Potassium thiocyanate until get the light brown color.

## Slide 7
Calculation:
a) calculate the concentration of KSCN
Ex: If volume of KSCN react in standardization of KSCN = 23
*M1 x V1 = M2 x V2
MAg+ x VAg+ = MSCN‾ x VSCN ‾
0.1 x 20 = M SCN‾ x 23
M SCN‾ = 0.087 M

## Slide 8
b) calculate the concentration of chloride
Ex: If volume of KSCN react in standardization of Chloride = 5.3
*Total m moles of Ag+ = M x V
T = 0.1 x 10 = 1 m moles
*Un reacted m moles of Ag+ (m moles of KSCN used) = MKSCN x VKSCN
U = 0.087 x 5.3 = 0.46 m moles
*Reacted m moles of Ag (m moles of Chloride) = T – U
= 1 – 0.46
= 0.54 m moles / 5 ml
= 0.108 m moles / ml