## Slide 1
Question 1
What are the types of flow line analyses? And why breakdown analysis is important?
A two-week study is performed on a 10-stations transfer line. The line behaves according data given in table (1). Solve the following: -
  Find for cases below, (1) Failure and repair rates, (2) Line efficiency, (3) Production rate, (4) Acceptable number of parts, and (5) Defect parts.
    No parts are removed when the line jam,
    Parts are removed when the line jam,
    Parts are removed for 25% of the breakdown occurrence.
  When the line is to be divided to stages, find the optimum number of buffers
(1)TABLE |  |  |  |  |  |  |  |  |  | 
Station | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Average Uptime, cycles | 250 | 300 | 480 | 300 | 800 | 750 | 960 | 600 | 520 | 320
Average Downtime, cycles | 10 | 15 | 9 | 9 | 24 | 15 | 15 | 10 | 14 | 8
Cycle time, min | 1.25 |  |  |  |  |  |  |  |  | 

## Slide 2
1-B-i-
Machine | Failure Analysis |  | Repair Analysis |  | Machine efficiency E=1/(1+p/r)
 | MTBF, cycles | Failure Rate p=1/MTBM | MTTR, cycles | Repair Rate r=1/MTTR | 
1 | 250 | 0.004 | 20 | 0.02 | 0.9259
2 | 300 | 0.003333 | 30 | 0.0333 | 0.9091
3 | 480 | 0.002082 | 40 | 0.025 | 0.9231
4 | 300 | 0.003333 | 30 | 0.0333 | 0.9091
5 | 800 | 0.00125 | 60 | 0.0167 | 0.9302
6 | 750 | 0.001333 | 60 | 0.0167 | 0.9259
7 | 960 | 0.00142 | 72 | 0.0139 | 0.9302
8 | 600 | 0.001667 | 60 | 0.0167 | 0.9091
9 | 550 | 0.001818 | 50 | 0.02 | 0.9167
10 | 320 | 0.003125 | 24 | 0.0417 | 0.9302
1-B-ii-

## Slide 3
Question 2
An assembly line produces two models (A, B) in a ratio of (2:3) respectively. The line consists of seven stations. It is arranged such that an inspection station (I) is placed after two assembly stations (S1, S2) and hence it is branched to produce each model. Model (A) is produced by assembly station (SA) followed by inspection station (IA). Also, Model (B) is produced by assembly station (SB) followed by inspection station (IB). Find the expected number of model A and B, and the throughput given the following data:
  Number of products at the start of the line is 440 units per week.
  Inspection station (I) has scrap rate of 8%.
  Inspection station (IA) has failure rate of 5%, which return to assembly station (SA).
  Inspection station (IB) has failure rate of 7%, which return to assembly station (SB).
  Processing Time of stations (S1,S2,I,SA,IA,SB,IB) are (5,4,3,4,3,5, 3) min. respectively.
S1
S2
I
SA
IB
IA
SB

## Slide 4
 | S1 | S2 | I | SA | IA | SB | IB
Arrival Rate,  unit/hr | 11 | 11 | 11 | 11x(2/5)= 4.05 |  | 11x(3/5)= 6.07 | 
Arrival Rate, ’ unit/hr | 11 | 11 | 11 | 4.05/0.95=4.2632 |  | 6.07/0.93= 6.527 | 
Service Rate,  unit/hr | 12 | 15 | 20 | 15 | 20 | 12 | 20
Utilization Ratio, =’/  | 0.9167 | 0.733 | 0.55 | 0.2842 | 0.2132 | 0.544 | 0.3264
= ’/  | 1 | 1 | 1 | 1.053 |  | 1.0753 | 
Queue, L= /(1- ), unit | 11.005 | 2.7453 | 1.222 | 0.397 | 0.271 | 1.193 | 0.4846
throughput, w=1/(- ’) hr | 1 | 0.25 | 0.111 | 0.0931 | 0.6355 | 0.1827 | 0.7422
LA, units | (2/5){11.005+2.7453+1.222) + 0.397 + 0.2132 = 6.5991 |  |  |  |  |  | 
WA=w, hr | 1 + 0.25 + 0.111 + 1.053(0.0931+0.6355) = 2.0896 |  |  |  |  |  | 
LB, units | (3/5){11.005+2.7453+1.222) + 1.193 + 0.4846 = 10.661 |  |  |  |  |  | 
WB w, hr | 1 + 0.25 + 0.111 + 1.0753(0.1827+0.7422) = 2.2859 |  |  |  |  |  |