## Slide 1
Fluorometric determination of riboflavin

## Slide 2
Introduction

## Slide 3
Fluorescence is a kind of a luminescence, which is the emission of photons from electronically excited states. Fluorescence occurs when the electron is transferred from a lower energy state into an "excited" higher energy state. The electron will remain in this state for 10⁻⁸ sec. then the electron returns to the lower energy state and it releases the energy in form of fluorescence.
Fluorescence

## Slide 5
In ultraviolet absorption spectroscopy when molecule absorbs UV radiation at one wavelength and its immediately re-emission, usually in a longer wavelength
Fluorescence

## Slide 6
Some molecules fluoresce naturally and others can be modified to make fluorescent compounds.

## Slide 7
Increasing
energy
excitation
fluorescence
First excited state with four vibrational energy levels
Ground state with four Vibrational energy levels

## Slide 8
Fluorescent compounds have two characteristic spectra:
an excitation spectrum (the wavelength and amount of light absorbed) and an emission spectrum (the wavelength and amount of light emitted). These spectra are often referred as a compound's fluorescence signature or fingerprint.
No two compounds have the same fluorescence signature. This principle makes fluorometry a highly specific analytical technique.

## Slide 9
*What is fluorometery?
Fluorometry is the measurement of fluorescence.
It’s measured by a fluorometer or fluorimeter.
,

## Slide 10
Fluorometer
A fluorometer involves using a beam of light, usually ultraviolet light.
A fluorometer generates the wavelength of light required to excite the analyte of interest; it selectively transmits the wavelength of light emitted, then it measures the intensity of the emitted light. The emitted light is proportional to the concentration of the analyte being measured (up to a maximum concentration).

## Slide 11
Fluorescence is generally a property to a rich electron compounds for example:
1- aromatic and heterocyclic compounds.
2- compounds with multiple conjugated groups.
3- compounds containing electron donating groups as OH, NH2 ,OCH3...
4- poly cyclic compounds like vit K, purines, nucleosides, vit A .

## Slide 12
5- NADH fluorescence.
6- non fluorescence compounds when converts to fluorescent derivatives like:
Steroids
Metals by chelating.
Antibodies.

## Slide 13: Fluorescence spectra
Fluorescence is used primarily for quantitative
analysis in ppm (part per millions) .
F=Kфp₀ (2.3 abc)
Where F is fluorescence intensity
K instrument constant
Ф is the quantum efficiency
p₀ intensity of excitation
a molar absorptive, b cell path, c molar concentration
F=k.َc
k.َ= Kфp₀ (2.3 ab)
the intensity of fluorescence is directly proportional to the conc. of fluorescence compound.

## Slide 14
Advantages of fluorometer:
- Very specific
- Very sensitive.
- Wide Concentration Range
- Simplicity and Speed
- Low Cost

## Slide 15
Disadvantages:
The fluorescence is very sensitive to environmental changes which include:
PH,
temperature,
solvent contamination and
UV light used for excitation can photochemical change

## Slide 16
Clinical uses of instrument
Uses to measure fluorescence for qualitative and quantitative analysis
Used to measure any substance that exists in small conc. for example: vitamins from blood sample.

## Slide 18: Instrumentation
1-Light Source:
The lamp or light source provides the energy that excites the compound of interest by emitting light. Light sources include xenon lamps, high pressure mercury vapor lamps.

## Slide 19
2-Excitation Filter ( or monochromator) : The excitation filter is used to screen out the wavelengths of unabsorbed light by the compound being measured.

## Slide 20
3-Sample Cell/Cuvette:
Cuvettes are made from borosilicate or quartz glass…
Cuvette size affects the measurement. The greater the pathlength (or diameter) of the cell, the lower the concentration that can be read.
The cuvette material must allow the compound's absorption and emission light energy to pass through.

## Slide 21
sample holder.

## Slide 22
4-Emission Filter(or monochromator ):
Stray light scatter is also emitted from the sample.

## Slide 23
5-Light Detector.
The light detector is most often a photomultiplier tube, though photodiodes are increasingly being used. The light passing through the emission filter is detected by the photomultiplier or photodiode. The light intensity, which is directly proportional (linear) to the compound's concentration, is registered as a digital readout.

## Slide 24
Schemating drawing

## Slide 25: Precautions
maintain pH
Cleanliness of glassware.
High standards of experimental technologist are necessary to prevent quenching.
maintain Temperature.
Cuvette Size (Pathlength):

## Slide 26: Riboflavin (vitamin B2) measurment.
Principle:
Riboflavin (vitamin B2) is strongly fluorescent in 5% acetic acid solution.
The excitation and fluorescent spectra are obtained to determine the wavelengths of the excitation and emission to use, and unknown is determined by comparison to standards .

## Slide 27: Chemical and solutions required
We need to prepare :
1- 5 % Acetic acid.
The addition of a few drops of glacial acetic acid to the solution will insure an acid pH and help to stabilize it.
2- Riboflavin stock solution .
3- Riboflavin standards solution 10( ppm)
4- Unknown.

## Slide 28: Preparation of standards
 | Blank | Std .1 | Std.2 | Std.3 | Std.4 | Std.5
Riboflavin stoc.std(10 ppm) | ............. | 0.2 ml | 0.4 ml | 0.6 ml | 0.8 | 1 ml
5% acetic acid |  | 9.8 ml | 9.6 ml | 9.4 ml | 9.4 ml | 9 ml

## Slide 29: Procedure
1- switch on the mains.
2- install the excitation and emission filtered in their holders.
3- start lamp (UV) by pressing 3-4 sec. the start switch and release it.
4- leave to warm up ,15 mins.
5- open the door of the instrument which acts as sample holder.

## Slide 30
6- adjust the range select or at x1 (excitation filter) for less conc. sample (ppm) and the higher range for higher conc. sample.
7- Put reagent blank cuvette in the sample holder, close the door and with the help of blank knob set read out to zero.
8- Remove reagent blank and insert the std. highest conc. And with help of attenuator knob set the read out to 100 and record this reading.

## Slide 31
9- Check twice for zeroing and 100 by inserting appropriate samples . If this not ok select higher range .
10- Take the reading for other std. and given unknown .

## Slide 32
 | blank | Std. 1 | std 2 | std 3 | std 4 | std 5
Conc. In ppm volume | 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0
reading | 0 | 15.5 | 24. 7 | 52.9 | 92.4 | 100

## Slide 33
11- plot the graph and from the graph find out the conc. of unknown.
F
0
1
5
CONC.