## Slide 1: Chapter 5
Present Worth Analysis

## Slide 2
Systematic Economic Analysis Technique
1. Identify the investment alternatives
2. Define the planning horizon
3. Specify the discount rate
4. Estimate the cash flows
5. Compare the alternatives
6. Perform supplementary analyses
7. Select the preferred investment

## Slide 3: Measures of Economic Worth
Present Worth (> $0)
Future Worth (> $0)
Annual Worth (> $0)
Capitalized Worth (> $0)
Discounted Payback Period (< Value, e.g. 2 yrs)
Payback Period (< Value)
Internal Rate of Return (> MARR)
External Rate of Return (> MARR)
Modified Internal Rate of Return (> MARR)
Benefit/Cost Ratio (> 1.0)

## Slide 4: Measures of Economic Worth
Ranking Methods or Incremental Methods
  Present Worth
  Future Worth
  Annual Worth
  Capitalized Worth
  Discounted Payback Period
  Payback Period
Incremental Methods
  Internal Rate of Return
  External Rate of Return
  Modified Internal Rate of Return
  Benefit/Cost Ratio

## Slide 5: Measures of Economic Worth
The following are consistent measures of economic worth, i.e., yield the same recommendation (if performed correctly)
  Present Worth
  Future Worth
  Annual Worth
  Internal Rate of Return
  External Rate of Return
  Benefit/Cost Ratio
Capitalized worth yields the same recommendation if the planning horizon is infinitely long or equal to a least common multiple of lives of the investment alternatives

## Slide 6: Present Worth Analysis
Ranking versus incremental analysis
Before-tax versus after-tax analysis
Equal versus unequal lives
Single versus multiple alternatives
Finite versus infinite planning horizon
Discounted payback period and payback period analyses

## Slide 7: Present Worth Analysis
Single Alternative

## Slide 8: Present Worth Method
converts all cash flows to a single sum equivalent at time zero using i = MARR over the planning horizon
the most popular DCF method
(bring all cash flows back to “time zero” and add them up!)

## Slide 9: Example 5.2
A $500,000 investment in a surface mount placement machine is being considered. Over a 10-year planning horizon, it is estimated the SMP machine will produce net annual savings of $92,500. At the end of 10 years, it is estimated the SMP machine will have a $50,000 salvage value. Based on a 10% MARR and a present worth analysis, should the investment be made?
PW = -$500K + $92.5K(P|A 10%,10) + $50K(P|F 10%,10)
= $87,650.50
=PV(10%,10,-92500,-50000)-500000
= $87,649.62

## Slide 10
Solving with Excel®,

## Slide 11
Plotting Cumulative Present Worth,

## Slide 12: Present Worth Analysis Multiple Alternatives
Choose the alternative with the greatest present worth
 j

## Slide 13: Example 5.3
Two design alternatives (A & B) are being considered for a new ride (The Scream Machine) at a theme park in Florida. Alternative A requires a $300,000 investment and will produce net annual revenue of $55,000/yr. Alternative B requires a $450,000 investment and will produce net annual revenue of $80,000/yr. At the end of the 10-yr planning horizon, both designs will have negligible salvage values. Based on a 10% MARR, which should be chosen? (The “do nothing” alternative is feasible and assumed to have a PW of $0.)
PWA(10%) = -$300,000 + $55,000(P|A 10%,10) = $37,951.35
=PV(10%,10,-55000)-300000 = $37,951.19 > $0
(A is better than doing nothing)
PWB(10%) = -$450,000 + $80,000(P|A 10%,10) = $41,565.60
=PV(10%,10,-80000)-450000 = $41,565.37 > PWA
(B is better than A)

## Slide 14: Example 5.3
Two design alternatives (A & B) are being considered for a new ride (The Scream Machine) at a theme park in Florida. Alternative A requires a $300,000 investment and will produce net annual revenue of $55,000/yr. Alternative B requires a $450,000 investment and will produce net annual revenue of $80,000/yr. At the end of the 10-yr planning horizon, both designs will have negligible salvage values. Based on a 10% MARR, which should be chosen? (The “do nothing” alternative is feasible and assumed to have a PW of $0.)
PWA(10%) = -$300,000 + $55,000(P|A 10%,10) = $37,951.35
=PV(10%,10,-55000)-300000 = $37,951.19 > $0
(A is better than doing nothing)
PWB(10%) = -$450,000 + $80,000(P|A 10%,10) = $41,565.60
=PV(10%,10,-80000)-450000 = $41,565.37 > PWA
(B is better than A)
How does PW change with changing MARR?

## Slide 16
Flow Chart for the Incremental Comparison of Investment Alternatives

## Slide 17: Example 5.4
Let’s use an incremental approach to evaluate the two design alternatives for a new ride at a theme park. Recall, Alternative A required a $300,000 investment and produced annual revenue of $55,000; Alternative B required a $450,000 investment and produced annual revenue of $80,000. At the end of the 10-yr planning horizon, both had negligible salvage values. Based on a 10% MARR, which should be chosen?
PWA(10%) = -$300,000 + $55,000(P|A 10%,10) = $37,951.35
=PV(10%,10,-55000)-300000 = $37,951.19 > $0
(A is better than doing nothing)
PWB-A(10%) = -$150,000 + $25,000(P|A 10%,10) = $3,614.25
=PV(10%,10,-25000)-150000 = $3,614.18 > $0
(B is better than A)

## Slide 18: Present Worth Analysis
“One Shot” Investments

## Slide 19: Example 5.5
Two investment alternatives (1 & 2) are available, with the CFDs shown below. They are “one shot” investments. Using a 15% MARR, which should be chosen?
PW1(15%) = -$4,000 + $3,500(P|A 15%,4) + $1,000(P|F 15%,4)
PW1(15%) = $6,564.18
PW2(15%) = -$5,000 + $1,000(P|A 15%,6) + $1,000(P|G 15%,6)
PW2(15%) = $6,721.26

## Slide 20: Example 5.5
Two investment alternatives (1 & 2) are available, with the CFDs shown below. They are “one shot” investments. Using a 15% MARR, which should be chosen?
PW1(15%) = -$4,000 + $3,500(P|A 15%,4) + $1,000(P|F 15%,4)
PW1(15%) = $6,564.18
PW2(15%) = -$5,000 + $1,000(P|A 15%,6) + $1,000(P|G 15%,6)
PW2(15%) = $6,721.26

## Slide 21: Discounted Payback Period Analysis
Single Alternative

## Slide 22: Discounted Payback Period Method
determines how long it takes to fully recover an investment while considering the time value of money
increasing in popularity
determine the smallest value of m such that
(determine the point in time when cumulative discounted cash flow > $0)

## Slide 23: Discounted Payback Period
EASTMAN calls this the net present value payback year
Let’s use Excel’s® SOLVER and/or GOAL SEEK to determine the DPBP for the SMP investment with salvage value decreasing as geometric and gradient series.

## Slide 24: Example 5.6
Based on a 10% MARR, how long does it take for the $500,000 investment in a surface mount placement machine to be recovered, based on an annual savings of $92,500 and a negligible salvage value, regardless of how long the machine is used?
# years =NPER(10%,92500,-500000)
= 8.16 years

## Slide 25: Example 5.6 (Continued)
How is the PW of the investment in the SMP machine affected when salvage value decreases from $500,000 to $50,000 over the 10-year planning horizon? Consider both geometric and gradient decreases.

## Slide 26: Example 5.6 (Continued)
How is the PW of the investment in the SMP machine affected when salvage value decreases from $500,000 to $50,000 over the 10-year planning horizon? Consider both geometric and gradient decreases.
G = ($500,000 - $50,000)/10 = $45,000/yr
j =RATE(10,,-500000,50000) = -20.6%/yr

## Slide 28: Example 5.7
Based on a 10% MARR, how long does it take for the $500,000 investment in a surface mount placement machine to be recovered, based on an annual savings of $92,500 and a salvage value at the end of n years equal to
a) $500,000(1 – 0.206)n and
b) $500,000 - $45,000n?
The Excel® SOLVER tool is used to solve the example.

## Slide 30
Notes: Note: SOLVER parameter box can be grabbed, moved, and re-sized
<number>

## Slide 32: Payback Period Method
EASTMAN calls it the cash payback year
determines the length of time required to recover the initial investment without considering the time value of money
not equivalent to those already considered
a popular method of valuing investments
determine the smallest value of m such that
(ignores cash flows that occur after the payback period)

## Slide 33: Why Use the Payback Period Method?
does not require interest rate calculations
does not require a decision concerning the MARR
easily explained and understood
reflects a manager’s attitudes when capital is limited
hedge against uncertainty of future cash flows
provides a rough measure of the liquidity of an investment

## Slide 34: Example 5.8
What is the payback period for the $500,000 SMP investment, given an annual savings of $92,500?
PBP = $500,000/$92,500
= 5.4054 years
=NPER(0%,92500,-500000)
= 5.4054

## Slide 35: Discounted Payback Period Analysis
Multiple Alternatives

## Slide 36: Example 5.9
Now, suppose a third design (alternative C) is developed for The Scream Machine. As before, A requires a $300,000 investment and produces revenue of $55,000/yr; and B requires a $450,000 investment and produces revenue of $80,000/yr. The new design (C) requires a $150,000 investment and produces 1st year revenue of $45,000; thereafter, revenue decreases by $5000/yr. Based on a 10% MARR, which design has the smallest DPBP?
DPBPA(10%) =NPER(10%,-55000,300000) = 8.273 years
DPBPB(10%) =NPER(10%,-80000,450000) = 8.674 years
DPBPC(10%) = 6.273 years (using the Excel® SOLVER tool)

## Slide 39: Example 5.9
Now, suppose a third design (alternative C) is developed for The Scream Machine. As before, A requires a $300,000 investment and produces revenue of $55,000/yr; and B requires a $450,000 investment and produces revenue of $80,000/yr. The new design (C) requires a $150,000 investment and produces 1st year revenue of $45,000; thereafter, revenue decreases by $5000/yr. Based on a 10% MARR, which design has the smallest DPBP?
DPBPA(10%) =NPER(10%,-55000,300000) = 8.273 years
DPBPB(10%) =NPER(10%,-80000,450000) = 8.674 years
DPBPC(10%) = 6.273 years (using SOLVER)
Note: PWC(10%) = -$150,000 + $45,000(P|A 10%,10) - $5,000(P|G 10%,10)
PWC(10%) = $12,048.81 < PWA(10%) < PWB(10%) B is best, not C!!

## Slide 40
Present Worth as a Function of Investment Duration

## Slide 41
Close-Up of Critical Region

## Slide 42: Example 5.10
Three investments are available, but only one can be pursued: invest $10,000 and obtain $5,000/yr for 2 yrs, plus $1,000 after 5 yrs; invest $10,000 and receive $5,000, $4,000, $3,000, $2,000, and $1,000 over the next 5 yrs; invest $10,000 and receive $2,500/yr for 5 yrs, plus $10,000 after 5 yrs. Which is best using PBP? using PW and a MARR of 10%?
PBP ranking: 1, 2, 3
PW ranking: 3, 2, 1

## Slide 43: Capitalized Worth Analysis
Single Alternative

## Slide 44: Capitalized Worth Method
a perpetuity is an investment that has an infinite life
the capitalized worth is the present worth of a perpetuity
the capitalized worth indicates the amount of money needed “up front” such that the interest earned will cover the cash flow requirements forever for the investment
used mostly by government

## Slide 45: Example 5.11
Every 10 years the dome of the state capital building has to be cleaned, sand blasted, and re-touched. It costs $750,000 to complete the work. Using a 5% MARR, what is the capitalized cost for the refurbishment of the capital dome?
CC = $750,000 + $750,000(P|F 5%,10) + $750,000(P|F 5%,10) + …
or
CC = $750,000(A|P 5%,10)/0.05 = $750,000(0.1295)/0.05 = $1,942,500
CC =PMT(5%,10,-750000)/0.05 = $1,942,569
or
CC = $750,000 + $750,000(A|F 5%,10)/0.05
CC = $750,000 + $750,000(0.0795)/0.05 = $1,942,500
CC =750000+PMT(5%,10,,-750000)/0.05 = $1,942,569
Recall, (A|P i%,n) = (A|F i%,n) + i

## Slide 46: Example 5.12
A new highway is to be constructed. Asphalt paving will be used. The asphalt will cost $150/ft, including the material and paving operation. Due to heavy usage, the asphalt is expected to last 5 yrs before requiring resurfacing. The cost of resurfacing will be the same/ft. Paved ditches must be installed on each side of the highway and will cost $7.75/ft to install; ditches will have to be re-paved in 15 yrs at a cost equal to the initial cost. Four pipe culverts are required/mile; each costs $8,000 and will last 10 yrs; replacements will cost $10,000, each, forever. Annual maintenance of the highway will cost $9,000/mi. Cleaning each culvert will cost $1,250/yr. Cleaning and maintaining each ditch will cost $3.75/ft every year. Using a 5% MARR, what is the capitalized cost (CC) per mile for the highway?

## Slide 47: Example 5.12 (Solution)
Paving Highway and Ditches/mile
CC = 5,280 ft/mi[$150/ft(A|P 5%,5) + $7.75/ft(A|P 5%,15)]/0.05
= $3,737,409
=5280*(PMT(5%,5,-150)+PMT(5%,15,-7.75))/0.05 = $3,737,487
Highway Maintenance/mile
CC = $9,000/0.05 = $180,000
Ditch Maintenance/mile
CC = 2(5,280 ft/mi)($3.75/ft)/0.05 = $792,000
Culverts/mile
CC = 4[($8,000 + $1,250/0.05 + $10,000(A|F 5%,10)/0.05]
= $195,600
CC =4*(8000+1250/0.05+PMT(5%,10,,-10000)/0.05)
= $195,604
Highway/mile
CC = $3,737,487 + $180,000 + $792,000 + $195,604
= $4,905,091

## Slide 48: Example 5.13
How much will it cost to endow a $12,500 scholarship if the endowment earns 4.5% interest?
CW = $12,500/0.045 = $277,777.78

## Slide 49: Example 5.14
Suppose, instead of endowing a scholarship, you wish to establish a fund that will pay for the cost of a scholarship for 100 years. How much must you contribute to a fund that earns interest at an annual rate of 9%, if the size of the scholarship grows at an annual rate of 4.5%?

## Slide 53: Capitalized Worth Analysis
Multiple Alternatives

## Slide 54: Example 5.15
In a developing country, two alternatives are being considered for delivering water from a mountainous area to an arid area. A pipeline can be installed at a cost of $125 million; major replacements every 15 years will cost $10 million. Annual O&M costs are estimated to be $5 million. Alternately, a canal can be constructed at a cost of $200 million; annual O&M costs are estimated to be $1 million; upgrades of the canal will be required every 10 years at a cost of $5 million. Using a 5% MARR and a capitalized cost analysis, which alternative should be chosen?

## Slide 55: Example 5.15 (Solution)
Pipeline
CC = $125,000,000 + [$10,000,000(A|F 5%,15) + $5,000,000]/0.05 = $234,268,000.00
=125000000+(PMT(5%,15,,-10000000)+5000000)/0.05
= $234,268,457.52
Canal
CC = $200,000,000 + [$5,000,000(A|F 5%,10)
+ $1,000,000]/0.05 = $227,950,000.00
CC = 200000000+(PMT(5%,10,,-5000000)+1000000)/.05
CC = $227,950,457.50

## Slide 56
Pit Stop #5— Open Road Ahead!
True or False: Present worth analysis is the most popular DCF measure of economic worth.
True or False: Unless non-monetary considerations dictate otherwise, choose the mutually exclusive investment alternative that has the greatest present worth, regardless of the lives of the alternatives.
True or False: When using present worth analysis to evaluate the economic viability of mutually exclusive alternatives, use a common period of time in the comparison.
True or False: If PW > 0 and MARR = 20%, then DPBP < 5 years.
True or False: DPBP > PBP.
True or False: If CW > 0, then PW > 0.
True or False: If PW(A) > PW(B), then CW(A) > CW(B), DPBP(A) < DPBP(B), and PBP(A) < PBP(B).
True or False: PW, FW, AW, CW, and B/C are ranking methods; therefore, the alternative having the greatest PW, FW, AW, CW, or B/C should be recommended.
True or False: Either ranking or incremental analysis can be used with all four “worth” methods (PW, FW, AW, and CW).
True or False: The “do nothing” alternative always has negligible incremental costs and revenues.

## Slide 57
Pit Stop #5— Open Road Ahead!
True or False: Present worth analysis is the most popular DCF measure of economic worth. TRUE
True or False: Unless non-monetary considerations dictate otherwise, choose the mutually exclusive investment alternative that has the greatest present worth, regardless of the lives of the alternatives. FALSE
True or False: When using present worth analysis to evaluate the economic viability of mutually exclusive alternatives, use a common period of time in the comparison. TRUE
True or False: If PW > 0 and MARR = 20%, then DPBP < 5 years. FALSE
True or False: DPBP > PBP. TRUE
True or False: If CW > 0, then PW > 0. TRUE
True or False: If PW(A) > PW(B), then CW(A) > CW(B), DPBP(A) < DPBP(B), and PBP(A) < PBP(B). FALSE
True or False: PW, FW, AW, CW, and B/C are ranking methods; therefore, the alternative having the greatest PW, FW, AW, CW, or B/C should be recommended. FALSE
True or False: Either ranking or incremental analysis can be used with all four “worth” methods (PW, FW, AW, and CW). TRUE
True or False: The “do nothing” alternative always has negligible incremental costs and revenues. FALSE