## Slide 1: Chapter 16
Obtaining and Estimating
Cash Flows
Notes: <number>

## Slide 2: Think of Chapter 16 as Two Separate but Related Topics
Cost terminology and estimation - for obtaining and understanding cash flows (16.1-16.3)
Accounting principles – to help understand economic analysis from the business’ perspective (16.4-16.5)
Notes: <number>

## Slide 3: Cost Terminology and Estimation (16.1-16.3)
Introduction
  Why is this important?
Five Cost Viewpoints
  Different perspectives yield different insights
Cost Estimation
  Obtaining numeric values
Notes: <number>

## Slide 4: Why Is This Important? (16-1)
Economic decision making requires collecting data about the amount and timing of cash flows for the alternatives.
  A variety of sources is frequently required.
  Understanding viewpoints helps ensure that all relevant cash flows are collected.
  Understanding terminology for the various sources helps ensure that cash flows are properly interpreted.
  Read Example 16.1 for additional insight.
Notes: <number>

## Slide 5: Cost Viewpoints (16-2)
Five Cost Viewpoints
Life Cycle Viewpoint
Past/Future Viewpoint
Manufacturing Cost Structure Viewpoint
Fixed/Variable Viewpoint
Average/Marginal Viewpoint
Notes: <number>

## Slide 6: The Life Cycle Viewpoint
The Life Cycle viewpoint focuses on when cash flows occur within the life cycle of an asset’s (or project’s) service life.
  First Cost
  Operating and Maintenance (O&M) Costs and Revenues
  Salvage Value
Notes: <number>

## Slide 7: The Life Cycle Viewpoint First Costs
First Costs are the costs required to place the asset in service.
  Purchase Cost
  Training Cost
  Shipping and Installation Cost
  Initial Tooling Cost
  Supporting Equipment Cost
  Site Preparation
Notes: <number>

## Slide 8: The Life Cycle Viewpoint O&M Costs
Operating and Maintenance (O&M) Costs are the routine costs required to keep the asset in service.
A wide variety of costs may be considered here depending on the situation.
  Energy Costs
  Routine Maintenance (lubricants, filters, etc.)
  Indirect Labor
  etc.
Notes: <number>

## Slide 9: The Life Cycle Viewpoint Operating Revenues
Operating Revenues are the revenues that result from having and using the asset.
Revenues are typically estimated based on the volume and value of the parts that utilize the asset or result from the project.
These revenues are ones that would not be available if the asset or project was not in service.
Notes: <number>

## Slide 10: The Life Cycle Viewpoint Salvage Value
Salvage Value is the net cash flow resulting from disposing of the asset or terminating the project.
  Salvage Value may be positive or negative.
Salvage Value is determined by deducting the cost of disposal from the market value of the asset at the time of disposal.
Salvage value is typically one of the most difficult values to estimate.
Notes: <number>

## Slide 11: The Past/Future Viewpoint
The Past/Future viewpoint focuses on when costs and revenues occur relative to “time now”.
A past cost is any cost that occurred prior to “time now”.
A future cost is any cost that is expected to occur subsequent to “time now”.
Similar interpretations apply to past revenue and future revenue.
Notes: <number>

## Slide 12: The Past/Future Viewpoint Additional Terms
A Sunk Cost is any past cost that cannot be reasonably expected to be recovered.
    Read Examples 16.2 and 16.3 for additional insight.
Opportunity Cost is the cost of foregoing an opportunity to earn interest, or a return.
    Funds invested (or tied up in) one opportunity cannot be used for others.
    The difference in expected returns is an opportunity cost of the choice.
    The annual opportunity cost of holding $600 million dollars in inventory is $90 million/year if an interest rate of 15%/year is assumed.
    Example 16.4 provides an additional example.
Notes: <number>

## Slide 13: The Past/Future Viewpoint Additional Terms
Cost of Capital (CoC) refers to the cost of obtaining funds for investment.
Cost of Capital provides a lower bound for MARR.
  MARR >= CoC
Two majors sources of capital are frequently used:
  Debt sources consist primarily of loans and bonds
  Equity sources consist primarily of stocks and accumulated prior earnings
Notes: <number>

## Slide 14: Manufacturing Cost Structure Viewpoint
The Manufacturing Cost Structure breaks the selling price of a product into component pieces.
Labels are applied to the component pieces and to various combinations of the component pieces.
  The labels can vary by company and by industry but the component pieces are usually consistent.
A similar cost structure can be developed for non-manufacturing environments,
  however, some of the terminology for the component pieces and the combinations may differ.
Notes: <number>

## Slide 15: Manufacturing Cost Structure Component Pieces
Direct Materials Cost (DM)
Direct Labor Cost (DL)
Indirect Materials Cost (IM)
Indirect Labor Cost (IL)
Fixed and Miscellaneous Cost (F&M)
General and Administrative Cost (G&A)
Selling (Marketing) Cost (S)
Profit (P)
  Read Example 16.5 for additional insight regarding the distinction between Direct and Indirect Costs
Notes: <number>

## Slide 16: Manufacturing Cost Structure Combinations
Selling Price = DM+DL+IM+IL+F&M+G&A+S+P
= Cost of Goods Sold + Profit
Conversion Cost = DL+IM+IL+F&M
Prime Cost = DM+DL
Factory Overhead = IM+IL+F&M
Non Factory Overhead = G&A+S
Cost of Goods:
  Manufactured = DM+DL+IM+IL+F&M
      = Prime Cost + Factory Overhead
  Sold = DM+DL+IM+IL+F&M+G&A+S
  = Cost of Goods Manufactured + Non Factory Overhead
Notes: <number>

## Slide 17: Fixed and Variable Viewpoint
A Fixed Cost (FC) is any cost that does not vary in proportion to the quantity of output.
  Examples include rent, depreciation, lighting, and supervisor salaries.
  Fixed Costs are commonly fixed only over a certain range of production, called the relevant range.
  For example supervisor salaries or lighting are fixed for one shift operation but step to a new higher level for two shift operation.
  Successive relevant ranges are often represented graphically as a step function.
Notes: <number>

## Slide 18: Fixed and Variable Viewpoint
A Variable Cost (VC) is a cost that varies in proportion to the quantity of output.
  Common examples include direct materials and direct labor.
  Variable Costs are often represented as a linear function of output
    VC(x) = rate * x; where x is the level of production
Total Cost is the sum of fixed costs and variable costs
  TC(x) = FC + VC(x)
Notes: <number>

## Slide 19: Breakeven
Total Revenue (TR) is the sum of revenues received for the units sold.
Total Revenue is often represented as a linear function of units sold.
    TR(x) = price * x; where x is the number of units sold
If steady state inventory is assumed then units sold will be equal to the units produced.
The point of Breakeven, where total costs equal total revenues, can be found by solving:
  TR(x) = FC + VC(x)
Notes: <number>

## Slide 20: Breakeven Graph
Profit
Loss
Notes: <number>

## Slide 21: Significance of Breakeven
If production (sales) is less than breakeven, a loss will occur.
If production (sales) is greater than breakeven, a profit will occur.
Lower values of the breakeven quantity are generally desirable.
Lower values can be achieved by:
  increasing the revenue rate (the slope of the revenue line),
  decreasing the variable cost rate (the slope of the total cost line),
  reducing the fixed cost (the intercept of the total cost line).
Engineering Economy projects frequently target one of these areas for improvement.
Notes: <number>

## Slide 22: Example 16.6
Determination of breakeven value
R(x) = $5.00(x)
FC = $300
VC(x) = ($2.50+$1.00)(x) = $3.50(x)
Breakeven:
  R(x) = FC + VC(x)
  $5.00(x) = $300 + $3.50(x)
  x = 200 units
Notes: <number>

## Slide 23: Example 16.6 (continued)
Net Profit for a lot size of 1,000 units
Profit (Loss) = TR(x) – TC(x)
  = TR(x) – (FC + VC(x))
  = TR(x) – FC – VC(x)
  = $5.00(x) - $300 - $3.50(x)
  = $5.00(1,000) - $300 - $3.50(1,000)
  = $1,200 profit
  Another Breakeven Example is provided in Example 16.7
Notes: <number>

## Slide 24: Generalizations of Breakeven
The concept of breakeven is very general and can be applied to:
  Functions that do not represent revenue and/or cost,
  More than two functions,
    This may result in multiple breakeven values
    See Figure 16.4 for an example
  Non-linear functions.
    Example 16.9 includes a non-linear breakeven
Notes: <number>

## Slide 25: Average and Marginal Viewpoint
Average cost (AC) is the ratio of total cost to units of output.
AC(x) = TC(x) / x
  = (FC + VC(x)) / x
  = FC / x + VC(x) / x
If variable cost is linear with respect to x, then VC(x)/x is a constant (the variable cost rate), so,
  AC(x) = FC / x + VC rate
Notes: <number>

## Slide 26: Economies of Scale
Expressing average cost in this way,
  AC(x) = FC / x + VC rate
  leads to the idea of economies of scale.
As production volume (x) increases, average cost decreases.
  This results from spreading the fixed cost (FC) over a larger and larger number of units.
  The fixed cost per unit (FC / x) is decreasing while the variable cost rate remains constant resulting in lower average cost per unit.
Notes: <number>

## Slide 27: Average and Marginal Viewpoint
Marginal Cost (MC) is the incremental cost of additional production.
In the discrete case, marginal cost is the cost of producing one more discrete unit.
  the incremental cost increase of going from x units produced to (x+1) units produced.
  it is usually determined through difference equations; TC(x+1) – TC(x)
  Definitional Note: The marginal cost at x=5 is the additional cost incurred in producing the 6th unit, not the additional cost incurred in producing the 5th unit. Marginal cost can rightfully by defined either way, be careful of the definition in use.
Notes: <number>

## Slide 28: Average and Marginal Viewpoint
In the continuous case, marginal cost is the instantaneous rate of the change of the cost function.
It is determined by differentiating the cost function.
dTC(x)/dx evaluated at x
Notes: <number>

## Slide 29: Example 16.8
Determine the marginal cost for the cost function:
  TC(x) = $60,000 + $30(x) at x=10
Discrete Approach
  MC(10) = TC(11) - TC(10)
  = ($60,000+$30(11)) – ($60,000+$30(10))
  = $60,330 – $60,300 = $30
Continuous Approach
  MC(x) = d/dx[$60,000 + $30(x)] = $30
Similar results are obtained for x=20
It is worthwhile to note that since the variable costs are linear ($30*x), the marginal cost is a constant.
Notes: <number>

## Slide 30: Cost Relationships: Marginal, Average, and Total
Marginal Cost and Total Cost:
  If MC(x) > 0 then TC(x+1) > TC(x)
  If MC(x) = 0 then TC(x+1) = TC(x)
  If MC(x) < 0 then TC(x+1) < TC(x)
Marginal Cost and Average Cost:
  If MC(x) < AC(x) then AC(x+1) < AC(x)
  If MC(x) = AC(x) then AC(x+1) = AC(x)
  If MC(x) > AC(x) then AC(x+1) > AC(x)
Notes: <number>

## Slide 31: Example 16.9
Example 16.9 is an extended example that illustrates many of the concepts in this section for the non-linear case.
In particular, it includes:
  Selling price that varies with demand,
  Linear cost but non-linear revenue and profit,
  Determination of marginal revenue and average profit functions,
  The distinction between maximizing revenue and maximizing profit,
  Multiple breakeven points.
Notes: <number>

## Slide 32
True or False: When conducting an economic analysis, an engineer should consider costs from one and only one cost viewpoint.
True or False: The cost of foregoing an opportunity to earn interest, or a return, on investment funds is referred to as a sunk cost.
True or False: Prime cost is the sum of direct material cost and direct labor cost.
True or False: If the cost function for producing x units is TC(x) = 700+0.6x and the revenue function is TR(x) = 2.0x; then the breakeven value is 500 units.
True or False: The average cost function for Question 4 is given by AC(x) = 500 + 1.4x
True or False: The tradeoff being considered when determining the level of detail of an estimate is the cost of making the estimate versus the cost of errors resulting from an inaccurate estimate
Pit Stop #16 – Is Accounting a Foreign Language?
Notes: <number>

## Slide 33
True or False: An income statement shows the assets, liabilities, and net worth of a firm at a point in time.
True or False: The fundamental equation of accounting states that assets = liabilities + net worth
True or False: EBIT can also be referred to as operating earnings.
True or False: In cost accounting, the acronym ABC refers to a Pareto analysis of costs where A items are most important, C items are least important, and B items are somewhere between.
True or False: EVA is a management tool that focuses manager’s attention on adding value for the shareholders.
Pit Stop #16 – Is Accounting a Foreign Language?
Notes: <number>

## Slide 34
True or False: When conducting an economic analysis, an engineer should consider costs from one and only one cost viewpoint. False, all viewpoints should be considered.
True or False: The cost of foregoing an opportunity to earn interest, or a return, on investment funds is referred to as a sunk cost. False, the cost of foregoing an opportunity is the opportunity cost.
True or False: Prime cost is the sum of direct material cost and direct labor cost. True
True or False: If the cost function for producing x units is TC(x) = 700+0.6x and the revenue function is TR(x) = 2.0x; then the breakeven value is 500 units? True
True or False: The average cost function for Question 4 is given by AC(x) = 500 + 1.4x? False, the average cost function is AC(x)=700/x + 0.6
True or False: The tradeoff being considered when determining the level of detail of an estimate is the cost of making the estimate versus the cost of errors resulting from an inaccurate estimate. True
Pit Stop #16 – Is Accounting a Foreign Language?
Notes: <number>

## Slide 35
True or False: An income statement shows the assets, liabilities, and net worth of a firm at a point in time. False, an income statement shows revenues, expenses, and resulting profit over a period of time.
True or False: The fundamental equation of accounting states that assets = liabilities + net worth. True
True or False: EBIT can also be referred to as operating earnings. True
True or False: In cost accounting, the acronym ABC refers to a Pareto analysis of costs where A items are most important, C items are least important, and B items are somewhere between. False, in cost accounting, ABC is the acronym for Activity Based Costing.
True or False: EVA is a management tool that focuses manager’s attention on adding value for the shareholders. True
Pit Stop #16 – Is Accounting a Foreign Language?
Notes: <number>