## Slide 1: Indirect Haemagglutination
IHA
RPHA

## Slide 2
Secondary Serological Tests Agglutination/Haemagglutination HA
Definition : Ag-Ab interaction where Ag is a particulate material ( cell: bacteria, carrier)
Y
Y
Y
+
↔
Agglutination test: Qualitative/ Quantitative(Ab titer) agglutination test. It is used to determine Ag or Ab presence and amount(titer)
Cross-linking of red cells is called haemagglutination
DIRECT HA: Used to measure antibodies to red cell antigens itself
Direct
Self Ag

## Slide 3: Indirect Haemagglutination IHA
Definition : An agglutination test where a soluble antigen is coated onto a particle cell .
INDIRECT HA: Used to measure antibodies to non self antigens coated to the surface of red cells
Y
Y
Y
+
↔
Indirect
Coated Ag

## Slide 4: Agglutination Inhibition
Definition –The test is based on the inhibition of agglutination due to competition with a soluble Ag
Y
Y
Y
+
↔
Prior to Test
Y
+
↔
Y
Y
+
Test
Patient’s sample

## Slide 5: Reversed passive haemagglutination
It is an agglutination where Ab is coated on the red blood cell.
+
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
TEST Ag
Coated Ab on RBC
Reversed passive HA

## Slide 6: Methods to coat Ag on RBC’s
1-Spontaneous
2-Chemical methods: 1% tannic acid. Barium chloride, gluteraldehyde.
3-Metal bridges: Cr=Cr bridge
Carrier particle: Latex, RBC’s, charcoal, protein A of Staph.

## Slide 7: Indirect HA for detection of Ab to Leishmaniasis
This test is used to diagnose patients with L. donavani infection.
RBC’s are coated with purified L. donavani Ag ( Sudan strain) .It is derived from the premastigote form of Leishmaniasis cultures.
Patient and positive control sera are must be diluted 1:8 before use.

## Slide 8: Test procedure
Deliver 50 ul of diluent in wells 2-11.
Deliver 50ul of serum (diluted 1:8) in well 1&2.
Change the tip , mix and transfer 50ul from well 2 to well 3.
Repeat the previous step till well 10.
Discard 50ul from well 10.
Deliver 50 ul of –ve serum to well 12.
Deliver 25ul of Leish. coated RBC to all wells.
Cover and incubate the plate at RT for 2-3 hours.

## Slide 9: Procedure outline
 |  |  |  |  |  |  |  |  |  | 50ul diluent | 
 |  |  |  |  |  |  |  |  | 50ul | Serum50ul | Serum 50ul
50ul –ve serum |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | 25ul | Coated Ag
-ve | -ve | 4096 |  |  |  |  |  |  | 1:32 | 1:16 | 1:8
1 2 3 4 5 6 7 8 9 10 11 12

## Slide 10: Results
Positive result: Cross-linked cells settle in a diffuse pattern(called thin film ,membrane, sheath)
Negative result: Non-cross-linked cells settle in a bead to the bottom of the well.
Ab titer

## Slide 11: Reading of results
2 negative controls are used :
Buffer control(well11)
-ve control serum(well12)
Positive control serum is included in kit with specified Ab titer ( 1:512).
High titers 1:512 ,1:2048 are regarded as cases with Leishmaniasis.
Lower titers of 1:32 to 1:64 should be tested with other kits.

## Slide 12: Non serological HA
It is agglutination of RBC by a virus, bacteria, parasite not by an antibody.
Y
Y
Y
+
↔
Y
Y
Y
Ab
Bacteria /Virus