## Slide 1: HPLC
Notes: <number>

## Slide 2: CHROMATOGRAPHY
Stationary phase may be solid (adsorption) or liquid (partition)
Mobile phase may be gas (GC) or liquid( LC)

## Slide 3: H
P
igh
erformance
L
iquid
C
hromatography
Notes: <number>

## Slide 4: HPLC principle
it is a technique by which a mixture sample is separated into components for identification, quantification and purification of mixtures

## Slide 5: Instrumentation

## Slide 6
The heart of a HPLC system is the column.
The column contains the particles that contains the stationary phase.
The mobile phase is pumped through the column by a pump
Solvents must be degassed to eliminate formation of bubbles .

## Slide 7
Pump:
The role of the pumpis to force a liquid (mobile phase) through the liquid chromatograph at a specific flow rate
a pump can deliver a constant mobile phase composition (isocratic) which the m.ph composition remains unchanged during the analysis.
or (gradient) which the m.ph changed during the analysis..

## Slide 8
2. Injector:
•The injector serves to introduce the liquid sample into the flow stream of the mobile phase.
May be auto-sampler or manual

## Slide 9: There are a wide variety of stationary phases available for HPLC :
Normal Phase. - Polar stationary phase and non-polar solvent.
E.g. silica gel
• Reverse Phase.
- Non-polar stationary phase and a polar solvent.
E.g. silica gel -C18
Notes: <number>
-

## Slide 10
ion exchange:
stationary phase contains ionic groups and the mobile phase is an aqueous buffer
Size Exclusion
there is no interaction between the sample compounds and the column .
Large molecules elute first. Smaller molecules elute later

## Slide 11: Chromatogram

## Slide 12: parameters of HPLC :
1- Qualitative analysis
the most common parameter for compound is retention time
(the time it takes for that specific compound to elute from the column after injection)

## Slide 14
Capacity Factor (k’):
Is a measure for the position of a sample peak in the chromatogram.
k’ = (tR1-to)/to

## Slide 15
Selectivity Factor ():
Also called separation or selectivity coefficient is defined as
 = k2’/k1’ = (tR2-to) / (tR1-to)

## Slide 16
2- Quantitative Analysis
The measurement of the amount of compound in a sample (concentration)
1.determination of the peak height
2.determination of the peak area

## Slide 18
Resolution (RS)
of a column provides a quantitative measure of its ability to separate two analytes
Rs = 2(TR2- TR1 ) / W2+W1

## Slide 19
Theoretical Plates (N): The number of theoretical plates characterizes the efficiency of a column.
N = 16 (tR/W)2