## Slide 1
After completing this Lesson, you will be able
to answer:
1. What is humidity?
2. What is relative humidity?
3. How relative humidity is measured?
4. What is a Hygrometer?
5. How Wet- and Dry Bulb Psychrometer and
Hair Hygrometer measure relative humidity?
Relative Humidity
Virtual Academy for the Semi Arid Tropics
Course on Crop-Weather Relationships

## Slide 2
Humidity refers to the amount of moisture (water vapor) in the surrounding air.
Relative Humidity is a measure of the amount of moisture in the air compared with the amount of moisture the air can hold.
Relative humidity is expressed as a percentage of how much moisture the air could possibly hold at the temperature it happens when you measure it.
The "wetter or damper" you feel,, the higher is the relative humidity. If you feel the air is dry around you, the relative humidity is low.
Relative Humidity

## Slide 3
We are very sensitive to humidity. Sweating keeps our body cool and maintain its current temperature.
If the air is at 90% relative humidity, sweat will not evaporate into the air. As a result, we feel much hotter than the actual temperature when the relative humidity is high.
If the relative humidity is low, we can feel much cooler than the actual temperature because our sweat evaporates easily, cooling the body.
Relative Humidity

## Slide 4
How relative humidity (RH) is measured?
Humidity is measured by means of a hygrometer.
There are different types of hygrometers.
The most common hygrometers are Wet- and Dry- Bulb Psychrometer and Hair Hygrometer.
Lesson 2: Relative Humidity

## Slide 5
How relative humidity (RH) is measured?
Wet- and Dry Bulb Psychrometer
  It consists of two identical mercury thermometers,
  one of which has a wet cotton or linen wick around its bulb.
  Evaporating water from the wick absorbs heat from the thermometer bulb, causing the thermometer reading to drop.
  The difference between dry-bulb and wet-bulb temperatures is compared on psychrometric charts.
Lesson 2: Relative Humidity

## Slide 6
How relative humidity (RH) is measured?
Wet- and Dry Bulb Psychrometer
Wet - and Dry Bulb Psychrometer
Lesson 2: Relative Humidity

## Slide 7
How relative humidity (RH) is measured?
Wet- and Dry Bulb Psychrometer Psychrometric Chart.
If the difference between wet and dry bulb is 6º F and the temperature is 72º F (dry bulb), then the RH is 54%.
Lesson 2: Relative Humidity

## Slide 8
How relative humidity (RH) is measured?
Hair Hygrometer
Humidity stretches
the hair (human /
animal / synthetic)
while dryness
shortens it.
The hygrometer has the job of stretching a hair between a fixed
and a movable point
to measure humidity
over time.
Hair Hygrometer
Lesson 2: Relative Humidity

## Slide 9
How relative humidity (RH) is measured?
  Other kinds of hygrometers use materials with electrical resistance that varies with the amount of moisture absorbed.
  With such hygrometers, a measurement of electrical resistance can be calibrated as a humidity measurement.
Lesson 2: Relative Humidity