## Slide 1: INJURY & ILLNESS RECORD KEEPING AND INCIDENCE RATES

## Slide 2
INCIDENT RECORDS
Records of incidents and injuries are essential to maintain efficient and successful safety programs, just as records of production, costs, sales, and profits and losses are essential to efficient and successful business operations.
Uses of Records
A good record-keeping system can help the safety professional in the following ways:
  Provide safety personnel with the means for an objective evaluation of their incident problems and with a measurement of the overall progress and effectiveness of their safety program.
  Identify high incident rate units, plants, or departments and problem areas so extra effort can be made in those areas.
  Provide data for an analysis of incidents pointing to specific causes or circumstances, which can then be attacked by specific countermeasures.
  Create interest in safety among supervisors or team leaders by furnishing them with information about their departments' incident experience.
  Provide supervisors and safety committees with hard facts about their safety problems so their efforts can be concentrated.
  Measure the effectiveness of individual countermeasures.
  Assist management in performance evaluation.

## Slide 3
Record-Keeping Systems
An incident report should accomplish three things: (a) establish all causes contributing to the incident; (b) reveal questions the investigator should ask to determine all environmental and human causes; and (c) provide a means of accumulating incident data.
Such a form is more likely to be filled out accurately and will present fewer problems for those who process and analyze the data.
A system that does a good job of collecting the basic facts, however, makes it easier later on to pinpoint the data relating to a specific problem.
In addition to the system presented here, which is primarily a manual, paper-based system, there are a number of personal computer-based record-keeping systems available on the market today.
The First Aid Report
The collection of injury data generally begins in the first aid department. The first aid nurse fills out a report for each new case.
Copies are sent to the safety department or safety committee, the worker's supervisor, and other departments as management may wish.

## Slide 4
Employee Injury and Illness Record
After cases are closed, the first aid report and the supervisor's report are filed by source of injury (type of machine, tool, material, etc.), type of event or exposure, or another factor that will facilitate use of the reports for incident prevention.
Filing Reports
After injury reports have been used to compile monthly summaries, the incomplete reports can be kept in a temporary file for convenient reference as later information about the injuries becomes available.
When injury reports are complete, they should be filed in a convenient system that permits quick access of information for special studies of incident conditions.
For example, the reports can be filed by agency of the injury, by occupation of the injured person, by department.
The employee injury card should be cross-referenced to the file location of the detailed incident report.

## Slide 5
Monthly Summary of Injuries and Illnesses
Managers and supervisors should prepare a monthly summary of injuries and illnesses to reveal the current status of incident experience.
This monthly summary of injury and illness cases allows for tabulating monthly and cumulative totals and the computation of OSHA incidence rates.
This form would be filled out on the basis of the individual report forms that were processed during the month or from OSHA form No. 300, Log and Summary of Occupational Injuries and Illnesses.
The monthly summary should be prepared as soon after the end of each month as the information becomes available but not later than the 20th of the following month.
Annual Report
Every establishment subject to the OSHAct is obliged to post its annual summary by February 1st for 30 days. The cumulative totals on OSHA form No. 300, Log and Summary of Occupational Injuries and Illnesses, serve as the annual report.
For management purposes, however, the annual report fulfills a more direct function. Managers and others prepare monthly summaries of injuries and illnesses primarily to show the trend of safety performance during the year.
However, annual reports are prepared to compare data for the longer periods with the experience of previous years and with the experience of similar organizations and of the industry as a whole.

## Slide 6
Uses of Reports
Reports to Management
Management is increasingly interested in the incident experience of its company. Therefore, monthly and other periodic summary reports showing the results of the safety program should be provided to the responsible executive.
Such reports do not need to contain details or technical language. They can be supplemented by simple charts or graphs to compare current incident rates with those of the previous period and the rates of other companies in the industry.
In a large company, departmental data help the executive visualize incident experience in various plant operations and provide a measure for better evaluation of progress made in the elimination of incidents.
It can be particularly valuable to compare cost figures, if they can be obtained, for different periods.
Bulletins to Supervisors
Supervisors are primarily interested in their own department and workers. One of the most effective ways to create and maintain the interest of supervisors in incident prevention is to keep them informed about the incident records of their departments.
Department injury rates based on sufficient amounts of exposure reflect the effectiveness of the supervisors' safety activities.
Because interest increases with knowledge, management can send supervisors bulletins containing analyses of the principal causes of incidents in each department.

## Slide 7
Bulletin Board Publicity
Posting a variety of materials on bulletin boards is one of the best ways to maintain the interest of employees in safety.
Incident records furnish many items, such as the following:
    no-injury records
    unusual incidents
    frequent causes of incidents
    charts showing reductions in incidents
    simple tables comparing departmental records
    standings in contests.

## Slide 8
Employers Subject to the Record-Keeping Requirements
Employers with 11 or more employees (at any one time in the previous calendar year) in the following industries must keep OSHA records. The industries are identified by name and by the appropriate Standard Industrial Classification (SIC) code:
    agriculture, forestry, and fishing (SIC 01-02 and 07-09)
    oil and gas extraction (SIC 13 and 1477)
    construction (SIC 15-17)
    manufacturing (SIC 20-39)
    transportation and public utilities (SIC 41-42 and 44-49)
    wholesale trade (SIC 50-51)
    building materials and garden supplies (SIC 52)
    general merchandise and food stores (SIC 53 and 54)
    hotels and other lodging places (SIC 70)
    repair services (SIC 75 and 76)
    amusement and recreation services (SIC 79)
    health services (SIC 80).
Employers in other industries are normally exempt from OSHA record keeping, as employers with no more than 10 full-time or part-time employees at any one time in the previous calendar year.
Even exempt employers, however, must comply with OSHA standards and display the OSHA poster. They must also report orally to OSHA within eight hours any incident that results in one or more fatalities or the inpatient hospitalization of three or more employees.
The following employers and individuals never have to keep OSHA injury and illness records:
    self-employed individuals
    partners with no employees
    employers of domestics in the employers' private residence for the purpose of housekeeping or child care, or both
    employers engaged in religious activities concerning the conduct of religious services.

## Slide 9
OSHA Record-Keeping Forms
Only two forms are used for OSHA record keeping: No. 300 and No. 101.
The OSHA Injury and illness Log and Summary, OSHA No. 300
The log is used for recording and classifying occupational injuries and illnesses and for noting the extent of each case.
The log consists of three parts: a descriptive section that identifies the employee and briefly describes the injury or illness, a section covering the extent of the injuries recorded, and a section on the type and extent of illnesses.
Usually, the OSHA No. 300 form is used by employers as their record of occupational injuries and illnesses.
The Supplementary Record of Occupational Injuries and Illnesses, OSHA No. 101
For every injury or illness entered on the log, it is necessary to record additional information on the supplementary record, OSHA No. 101.
To eliminate duplicate recording, workers' compensation, insurance, or other reports may be used as supplementary records if they contain all of the items on the OSHA No. 101.

## Slide 10
Categories for Evaluating the Extent of Recordable Cases
Once the employer decides that a recordable injury or illness has occurred, the case must be evaluated to determine its extent or outcome.
There are three categories of recordable cases: fatalities, lost workday cases, and cases without lost workdays. Every recordable case must be placed in only one of these categories.
Fatalities
All work-related fatalities must be recorded, regardless of the time between the injury and the death, or the length of the illness.
Lost Workday Cases
Lost workday cases occur when the injured or ill employee experiences either days away from work, days of restricted work activity, or both.
In these situations, the injured or ill employee is affected to such an extent that (1) days must be taken off from the job for medical treatment or recovery, or (2) the employee is unable to perform his normal job duties over a normal work shift (which could be an extended hour shift of 8 to 12 hours), even though the employee may be able to continue working.

## Slide 11
1. Lost workday cases involving days away from work refer to cases
when the employee ordinarily would have been on the job but could not work because of the job-related injury or illness.
2. Lost workday cases involving days of restricted work activity are
those cases in which, because of injury or illness, (1) the employee was temporarily assigned to another job, (2) the employee worked at a permanent job less than full time, or (3) the employee worked at his permanently assigned job but could not perform all the duties normally connected with it.
Restricted work activity occurs when the employee, because of the job-related injury or illness, is physically or mentally unable to perform all or any part of the normal job duties over all or any part of the normal workday or shift.
Injuries and illnesses are not considered lost workday cases unless they affect the employee beyond the day of injury or start of illness.
When counting the number of days away from work or days of restricted work activity, do not include the initial day of injury.

## Slide 12
Employer Reporting Obligations
The Annual Survey of Occupational Injuries and Illnesses
  The survey is conducted on a sample basis. Firms required to submit reports of their injury and illness experience are contacted by OSHA or a participating state agency.
Access to OSHA Records
  To ensure the reliability of the OSHA record-keeping process, OSHA has established regulations regarding access to OSHA records.
  All OSHA records that are being kept by employers for the five-year preservation period should be available for inspection and copying by authorized federal and state government officials.
  Employees, former employees, and their representatives are allowed access only to the log, OSHA No. 300.

## Slide 13
INCIDENCE RATES
Safety performance is relative. Only when a company compares its injury experience with that of its entire industry, or with its own previous experience, can it obtain a meaningful evaluation of its safety accomplishments.
To make such comparisons, a method of measurement is needed that will adjust for the effects of certain variables contributing to differences in injury experience.
Injury totals alone cannot be used for two reasons.
  First, a company with many employees may be expected to have more injuries than a company with few employees.
  Second, if the records of one company include all the injuries treated in the first aid room, while the records of a similar company include only injuries serious enough to cause lost time, obviously the first company's total will be larger than the second company's figure.

## Slide 14
Formulas for Rates
Incidence rates are based on the exposure of 100 full-time workers using 200,000 employee-hours as the equivalent (100 employees working 40 hours per week for 50 weeks per year).
An incidence rate can be computed for each category of cases or days lost depending on what number is put in the numerator of the formula.
The denominator of the formula should be the total number of hours worked by all employees during the same time period as that covered by the number of cases in the numerator.
Incidence Rate No. of injuries and illnesses x 200,000
of Recordable Cases = -------------------------------------------------------------
Total hours worked by all employees
during period covered
or
No. of lost work days x 200,000
= ------------------------------------------------------------
Total hours worked by all employees
during period covered

## Slide 15
There are two other formulas that can be used to measure the average severity of the recorded cases:
Total lost workdays
Average lost workdays = -----------------------------------------------
Total lost workday cases
Average days Total days away from work
away from work = ---------------------------------------------------
Total days-away-from-work cases
If these numbers are small, then it is known that the cases are relatively minor. If, however, the numbers are large, then the cases are of greater average severity and should receive serious attention.
For example, to calculate the incidence rate for total recordable cases at the end of the year, one would simply multiply the number of recordable cases by 200,000 and divide that by the number of hours worked by all employees for the whole year.
The incidence rates may also be interpreted as the percentage of employees who will suffer the degree of injury for which the rate was calculated.
That is, if the incidence rate of lost workday cases is 5.1 per 100 full-time workers, then about 5% of the establishment's employees incurred a lost-workday injury.

## Slide 16
The INCIDENCE rate is really a general term. In addition to the total injury-illness incidence rate, we have the following;
    1. Injury incidence rate
    2. Illness incidence rate
    3. Fatality incidence rate
    4. Lost-workday-cases incidence rate (LWDI)
    5. Number-of-lost-workdays rate
    6. Specific-hazard incidence rate
All of the foregoing rates use the standard 200,000 factor.
Note the difference between rates 4 and 5 in the above mentioned list.
Rate 4 counts cases in which one or more workdays were lost or in
which the worker was transferred to another job.
Rate 5 counts the total number of workdays lost or days in which the
worker was transferred to another job.

## Slide 17
In counting the number of lost workdays, the date of the injury or start of illness should not be counted, even though the employee may leave work for most of that day.
Thus, if the employee returns to his regular job and is able to perform all regular duties full time on the day after the injury or illness, no lost workdays are counted.
The most widely recognized standard incidence rate is the lost workday cases incidence rate, commonly known as the LWDI.
A somewhat surprising characteristic of the LWDI is that it considers injuries only — not illnesses.
Illnesses are more difficult to track than injuries because there are often time delays in their diagnosis. Also, it is more difficult to prove work-relatedness for chronic exposures, which may have a variety of simultaneous causes.
Because it is based on clear evidence that LWDI is considered a more precise and healthy measure of the effectiveness of the firm’s overall safety and health program.
Finally, the LWDI does not include fatalities, whether they are by illness or injury.
Fatalities should always be considered a rare occurrence of serious importance and as such should not be averaged among the more common injury statistics on which the LWDI is based.

## Slide 18
CASE STUDY
A metal products fabrication and assembly plant employs 250 workers and has the following injury-illness experience for the year.
File 1/January 31: Press-blanking operator scratches hand from punch press; first aid received, no medical treatment; worker remains on the job.
File 2/February 19: Maintenance worker, not wearing eye protection, operating grinding machine in tool room, incurs eye injury from flying chip; medical treatment required; injury occurs on Tuesday, employee returns to regular job at regular time on Thursday.
File 3/February 27: Assembly worker becomes “ill” due to noxious odors from remodeling operation in the assembly area; receives permission from supervisor to take the rest of the day off; does not go to a doctor or clinic; reports to regular work on time the next day.
File 4/March 2: Sewing machine operator’s right ring finger pulled into unguarded drive belt pulley on sewing machine; small fracture revealed by X ray; splint applied; worker returns to regular work at regular time the next day.
File 5/March 19: Dockworker sprains ankle on loading dock; moved to office job for two workweeks.
File 6/May 2: Maintenance worker entangles finger in rope as winch is released; taken to clinic for X ray; no fractures found; no treatment; worker returns to regular work the next day.
File 7/June 7: Yard worker exposed to poison ivy while clearing weeds in tank-farm area behind plant; Rash develops; treated with steroid drug by prescription; no time lost.
File 8/July 6: Assembly worker loses two workdays getting better from severe allergic reaction to stings incurred while cleaning out his attic at home; medical treatment with prescription drugs.
File 9/August 4: Maintenance worker using ungrounded portable electric drill to repair equipment in assembly area is electrocuted. Date of death: August 4.
File 10/August 7: Loaded pallet in loading dock area falls from forklift on dock- worker’s left foot; worker examined in hospital emergency room and X ray revealed no fractures or other injuries; worker receives therapy and goes home; worker reports back to his regular job on time the next day and wears his company-issued safety shoes.
File 11/August 9: Maintenance worker in the tool room incurs injury from foreign object in the eye; irrigation method used to remove foreign object, worker returns to regular job.
File 12/September 11: Worker in final assembly diagnosed with carpal tunnel syndrome (CTS) from repetitive work; surgery prescribed; worker misses three weeks of work before returning to regular job with engineering improvements to the workstation.

## Slide 19
ANALYSIS
The first step is to complete the OSHA 300 Log of Occupational Injuries and Illnesses.
File 1 The key word is “first aid.” This case is not recordable.
File 2 This is a lost-workdays injury case. Do not count the date of injury (Tuesday). Do not count Thursday either because the worker returned to work at the regular time. Only one day was lost.
File 3 This case is not recordable. The worker felt “ill,” but there was no medical treatment, and although the worker left work one afternoon. The worker returned to work on time the next day, so no lost time is counted.
File 4 This is a recordable injury, as the X ray was positive, revealing a fracture, which is always recordable. The worker returned to her regular work at the regular time the next day, however, so no time was lost.
File 5 This is a lost time injury. Even though the worker returned to work, he was assigned to a different job, so OSHA’s position is that the days at the restricted work activity count as lost workdays.
File 6 Unlike File 4, the X ray in this case was negative. Since there was no fracture and no medical treatment and the worker returned to the same job the next day on time, this case is not recordable.
File 7 Poison ivy from on-the-job exposure is classified as an occupational illness and is identified “Skin Disorder.”
File 8 Incidents occurring off the job are not recordable.
File 9 This is an injury-type fatality and should be recorded.
File 10 The negative X ray and whirlpool therapy during the first visit to medical personnel are both considered first aid not medical treatment. This case is not recordable.
File 11 Since the irrigation method was used and the object was not embedded in the eye, this eye injury is considered a first-aid case and is thus not recordable.
File 12 Because CTS is due to “repeated motion,” it is classified as a illness. This is a recordable lost time illness. The lost time is in the days-away-from-work category.

## Slide 20
Calculation of Incidence Rates:
2 x 200,000
LWDI (injuries only) = ------------------------------ = 0.8
250 x 2000
3 x 200,000
Injury incidence rate = ------------------------------- = 1.2
250 x 2000
2 x 200,000
Illness incidence rate = ------------------------------ = 0.8
250 x 2000
1 x 200,000
Fatality incidence rate = ----------------------------- = 0.4
250 x 2000
26 x 200,000
Number-of-lost-workdays rate = ---------------------- = 10.4
250 x 2000
Specific-hazard 1 x 200,000
incidence rate (eye injuries) = ------------------------- = 0.4
250 x 2000

## Slide 21
Some explanation for the Case Study
The LWDI is calculated in a prescribed way that excludes all fatalities and all illnesses, regardless of whether time was or was not lost.
Remember that the LWDI is an incidence rate and should not be confused with the number-of-lost-workdays rate.
In the specific-hazard incidence rate calculation, only one eye injury (File 2) was included in the calculation. The File 11 eye injury satisfied the definition of first aid and thus, as a non recordable injury, was excluded from the calculation.
The 250-employee firm in Case Study provides sufficient data to show meaningful calculations for the various incidence rates. But many firms are much smaller.
For very small firms, the calculations are obviously inappropriate. Recognizing that the general injury-illness recordkeeping system was designed for larger firms.