## Slide 1: Laboratory Quality Control
An Overview

## Slide 2: Definitions (1)
Quality Control - QC refers to the measures that must be included during each assay run to verify that the test is working properly.
Quality Assurance - QA is defined as the overall program that ensures that the final results reported by the laboratory are correct.
“The aim of quality control is simply to ensure that the results generated by the test are correct. However, quality assurance is concerned with much more: that the right test is carried out on the right specimen, and that the right result and right interpretation is delivered to the right person at the right time”

## Slide 3: Definitions (2)
Quality Assessment - quality assessment (also known as proficiency testing) is a means to determine the quality of the results generated by the laboratory. Quality assessment is a challenge to the effectiveness of the QA and QC programs.
**Quality Assessment may be external or internal, examples of external programs include NEQAS (national eternal quality assessment scheme), HKMTA, and Q-probes.

## Slide 4: Variables that affect the quality of results
    The educational background and training of the laboratory personnel
    The condition of the specimens
    The controls used in the test runs
    Reagents
    Equipment
    The interpretation of the results
    The transcription of results
    The reporting of results

## Slide 5: Errors in measurement
True value - this is an ideal concept which cannot be achieved.
Accepted true value - the value approximating the true value, the difference between the two values is negligible.
Error - the discrepancy between the result of a measurement and the true (or accepted true value).

## Slide 6: Sources of error
    Input data required - such as standards used, calibration values, and values of physical constants.
    Inherent characteristics of the quantity being measured - e.g. CFT (complement fixation test) and HAI (hemagglutinating inhibiting) titer.
    Instruments used - accuracy, repeatability.
    Observer fallibility - reading errors, blunders, equipment selection, analysis and computation errors.
    Environment - any external influences affecting the measurement.
    Theory assumed - validity of mathematical methods and approximations.

## Slide 7: Random Error
    An error which varies in an unpredictable manner, in magnitude and sign, when a large number of measurements of the same quantity are made under effectively identical conditions.
    Random errors create a characteristic spread of results for any test method and cannot be accounted for by applying corrections. Random errors are difficult to eliminate but repetition reduces the influences of random errors.
    Examples of random errors include errors in pipetting and changes in incubation period. Random errors can be minimized by training, supervision and adherence to standard operating procedures.

## Slide 8: Random Errors

## Slide 9: Systematic Error
    An error which, in the course of a number of measurements of the same value of a given quantity, remains constant when measurements are made under the same conditions, or varies according to a definite law when conditions change.
    Systematic errors create a characteristic bias in the test results and can be accounted for by applying a correction.
    Systematic errors may be induced by factors such as variations in incubation temperature, blockage of plate washer, change in the reagent batch or modifications in testing method.

## Slide 10: Systematic Errors