## Slide 1: Physical Transmission

## Slide 2: Computer Network Components
Components of a computer network:
    Computer with NIC (PCs, laptops, handhelds)
    routers & switches (IP router, Ethernet switch)
    Links” Transmission media” (wired, wireless)
    protocols (IP,TCP,CSMA/CD,CSMA/CA)
    applications (network services) i.e. Network Operating System (NOS)
    humans and service agents

## Slide 4: Physical Transmission
Physical Transmission
Transmission Media
Wire
Coaxial cable
Twisted Pair
STP
Fiber Optic
Wireless
Radio waves
Microwave
Infrared
Satellite
Laser
Signaling Techniques
Baseband
Transmission
Broadband
Transmission
UTP

## Slide 5: Transmission Media
Anything that can carry information from a source to a destination.

## Slide 6: Transmission Media
LANs can be connected together using a variety of transmission media types.
Each type has its own advantages and disadvantages which will examine in this section

## Slide 7: Transmission Media
Computers and telecommunication devices use signals to represent data.
These signals are transmitted from a device to another in the form of electromagnetic energy.
  Examples of Electromagnetic energy include:
    power, radio waves, infrared light, visible light, ultraviolet light, and X and gamma rays.

## Slide 8: Transmission Media
Not all portion of the spectrum are currently usable for telecommunications
Each portion of the spectrum requires a particular transmission medium

## Slide 9: Transmission Media
There are two categories of Transmission media:
  Wired (Guided) media
    A signal traveling along guided media is directed and contained by the physical limits of the medium
  Wireless (Unguided) media
    Unguided media transport signals without using a physical conductor.

## Slide 10: Design Factors for Transmission Media
Bandwidth: All other factors remaining constant, the greater the band-width of a signal, the higher the data rate that can be achieved.
Transmission impairments. Limit the distance a signal can travel.
Interference: Competing signals in overlapping frequency bands can distort or wipe out a signal.
Number of receivers: Each attachment introduces some attenuation and distortion, limiting distance and/or data rate.

## Slide 11: 1. Wired (Guided) media

## Slide 12: I. Wired (Guided) media:
There are three categories of guided media:
Coaxial Cable
Twisted Pair :
      Unshielded twisted pair (UTP)
      Shielded twisted pair (STP)
Fiber Optic Cable

## Slide 13: Twisted Pair Wires
Consists of two insulated copper wires, each with its own plastic insulation, twisted together arranged in a regular spiral pattern to minimize the electromagnetic interference between adjacent pairs
Often used at over distances to carry voice as well as data communications
Low frequency transmission medium

## Slide 14: Types of Twisted Pair
STP (shielded twisted pair)
  the pair is wrapped with metallic foil or braid to insulate the pair from electromagnetic interference
UTP (unshielded twisted pair)
  each wire is insulated with plastic wrap, but the pair is encased in an outer covering

## Slide 16: Unshielded Twisted Pair (UTP)
Advantages of UTP are its cost and ease of use. UTP is cheap, flexible, and easy to install.

## Slide 17: Shielded Twisted Pair (STP)
Materials and manufacturing requirements make STP more expensive than UTP but less susceptible to noise.

## Slide 18: Twisted Pair Advantages
Inexpensive and readily available
Flexible and light weight
Easy to work with and install

## Slide 19: Twisted Pair Disadvantages
Susceptibility to interference and noise
Relatively low bandwidth (3000Hz)

## Slide 20: Coaxial Cable (or Coax)
Used for cable television, LANs, telephony
Applications include some traditional Ethernet LANs like 10Base-2, or 10-Base5.
Has an inner conductor surrounded by a braided mesh
Both conductors share a common center axial, hence the term “co-axial”

## Slide 21: Coax Layers
copper or aluminum
conductor
insulating material
shield (braided wire)
outer jacket
(polyethylene)

## Slide 22: Coaxial Cable (or Coax)
It has two types :
  Thicker used with large networks.
  Thinner used with small networks.

## Slide 23: Coax Advantages
Higher bandwidth
  400 to 600Mhz
Much less susceptible to interference than twisted pair
It will not cause a toxic gas when its burned. That’s why they use it in some buildings.

## Slide 24: Coax Disadvantages
High attenuation rate makes it expensive over long distance
It’s not used anymore due to high cost and other technical factors.

## Slide 25: Fiber Optic Cable
Relatively new transmission medium used by telephone companies in place of long-distance trunk lines
Also used by private companies in implementing local data communications networks
Require a light source with injection laser diode (ILD) or light-emitting diodes (LED)

## Slide 26: Fiber Optic Cables
Optical fiber is made of glass or plastic and transmits signals in the form of light.
The cable consists of a strand of glass (core) surrounded by a glass tube (cladding).
Its surrounded by a plastic isolation layer for protection .

## Slide 27: Fiber Optic

## Slide 28: Fiber Optic Types
Digital data is converted to light
Single mode - one light source flashes a light down the cable.
Multimode - supports many simultaneous light transmissions.

## Slide 29
fiber optic multimode
step-index
fiber optic multimode
graded-index
fiber optic single mode

## Slide 30
Fiber Optic Signals

## Slide 31: Fiber Optic Advantages
greater capacity (bandwidth of up to 2 Gbps)
Speed (100 - 500 mbps)
smaller size and lighter weight
lower attenuation
immunity to environmental interference
highly secure

## Slide 32: Fiber Optic Disadvantages
expensive over short distance
requires highly skilled installers
adding additional nodes is difficult

## Slide 33: Type of Cable depends on:
Transmission speed.
Maximum cable length.
Shielded requirements.
Price.

## Slide 34: Comparison of Physical Media

## Slide 35: Comparison of Physical Media

## Slide 36: Wireless media

## Slide 37: II. Wireless Network
Transmission is sent and received through invisible waves
Less expensive than copper or fiber optic lines.
Allows the user to move freely around the office or campus and still remain connected to the network
Fastest-growing segment of network media today

## Slide 38: II. Wireless Network
Transmission and reception via antenna
  Desirable to make antenna one-quarter or one-half the wavelength
Directional
  Use directional antennas - point to point line of sight communications
  Higher frequency ranges cannot penetrate walls.
Omnidirectional
  Signal spreads in all directions
  Can be received by many antennas
  They can penetrate through walls.

## Slide 39: II. Wireless Transmissions
Electromagnetic Spectrum divided to :
Radio waves
Microwave waves
Infrared waves
Satellite
Laser

## Slide 40: II. Wireless Transmissions
Radio waves:
  frequency signals can be transmitted over radio waves similar to local radio station transmissions.
Microwave waves:
  faster than radio
  consist of number of dishes installed on high towers or high places, distance must be 50 kilometers or less.
  Its fast but it may have noise and interference.
  Used for telephone and television networks

## Slide 41: II. Wireless Transmissions
Infrared waves:
  transmits data using infrared (IR) light.
Satellite:
  high frequency signals are sent from a dish and caught by a satellite to enlarge then send back to earth where another dish will receive it .
Laser

## Slide 42: Wireless Transmission
Frequencies
  2GHz-40GHz: microwave frequencies (directional point-to-point)
  30MHz-1GHz: omnidirectional (broadcast radio)
  300GHz-200THz: Infrared (short-range communication)

## Slide 43: Data and Signals

## Slide 44: Data
Analog data: refers to information that is continuous as analog clock and human voice.
Digital data: refers to information that has discrete states as digital clock and data stored in computer memory in forms of 1s and 0s.

## Slide 45: Data
To be transmitted, data (analog or digital) must be transformed to electromagnetic signals.

## Slide 46: Signals
Signals can be analog or digital.
Analog signals can have an infinite number of values in a range
Digital signals can have only a limited number of values.

## Slide 47: Digital VS Analog signals

## Slide 48: Bandwidth & Bit Rate
Bandwidth:
  The difference between the highest and the lowest frequencies of a signal.
  It also measures the capacity of information a line or a network can carry.
  Measurement:
    Digital bandwidth: bits per second (bps)
    Analog bandwidth: hertz
Bit Rate: The number of bits transmitted per second
Bit rate and bandwidth are proportional to each other.

## Slide 49: b. Signaling Techniques
There are two ways that a signal is sent across a
network medium:
I. Baseband Transmission
II. Broadband Transmission

## Slide 50: I. Baseband Signaling
Baseband:
    Uses Digital Signaling
    Single Frequency
    Transmits Bi-directionally
    Uses Repeaters

## Slide 51: Repeater
A simple hardware device that moves all packets from one local-area network segment to another by regenerating, retiming, and amplifying the electrical signals.
The main purpose of a repeater is to extend the length of the network transmission medium beyond the normal maximum cable lengths.

## Slide 52: II. Broadband Signaling
Broadband
    Uses Analog Signaling
    Multiple Frequencies
    Transmits Uni-directionally
    Uses Amplifiers

## Slide 53: Amplifier
An electronic device that increases the voltage, current or power of the signal.
Unlike repeaters, amplifiers strengthen the signal along with its noise.

## Slide 54: Transmission Impairments

## Slide 55: Transmission Impairments
This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium.
In other words, the signal has changed over the medium..

## Slide 56
Impairment Causes
Attenuation
Distortion
Noise

## Slide 57: a) Attenuation
Loss of signal power

## Slide 58: b) Distortion
Distortion : means that signal changes its form or shape.
  Sometimes caused by dirty or corroded connectors or bad cables
Sender
Receiver

## Slide 59
Noise (Interference)
Thermal noise
Induced noise
Crosstalk noise
Impulse Noise
Interference is caused when a strong external signal interferes with a signal.
  is the random motion of electrons in a wire which creates an extra signal not originally sent by the transmitter
  Comes from sources such as motors and appliances
  Is the effect of one wire on the other
  Is the effect of one wire on the other
  is a spike ( a signal with high energy in a very short time) that comes from power lines, lighting and so on.