## Slide 1: Lecture 5- Data Link Layer

## Slide 2: The Data Link Layer
Data link layer is responsible for carrying a packet ( called frame) from one hop to the next hop.
Specific responsibilities of the data link layer include framing, addressing, flow control, error control, and media access control.

## Slide 3: Outlines
Packetizing
  Packets’ Function
  Packets’ Components
Error Detection
  Parity Check
  Cycle Redundancy Check
  Checksum
Multiple Access Methods

## Slide 4: Packetizing

## Slide 5: How Networks Send Data
To send data over a network, the data is broken down into small, manageable packets , each wrapped with the essential information needed to get it from its source to the correct destination .
In the sender, data is disassembled in small chunks.
Then it reassemble in the proper order when it reaches its destination.

## Slide 6: Packets’ Function in Network Communications
Networks cannot operate if computers put large amounts of data on the cable at the same time.
Notes: As you see in the figure, a computer sending large amounts of data causes other computers to wait (increasing the frustration of the other users) while the data is being moved. This is not called "sharing"; it is called "monopolizing the network.“
In order for many users at once to transmit data quickly and easily across the network, the data must be broken into small, manageable chunks. This way, users each get their share of access to the network. These chunks are called packets, or frames

## Slide 7: Packets’ Function in Network Communications
There are two reasons why putting large chunks of data on the cable at one time slows down the network:
  Large amounts of data sent as one large unit tie up the network and make timely interaction and communications impossible because one computer is flooding the cable with data.
  The impact of retransmitting large units of data further multiplies network traffic.
Notes: This way, only a small section of data is affected, and, therefore, only a small amount of data must be retransmitted, making it relatively easy to recover
from the error.
.

## Slide 8: Packets’ Function in Network Communications
These effects are minimized when the large data units are reformatted into smaller packages for better management of error correction in transmission.
Notes: This way, only a small section of data is affected, and, therefore, only a small amount of data must be retransmitted, making it relatively easy to recover
from the error.
.

## Slide 9: Packets’ Components
  Packets contents are based on the protocol used , but they basically contain:
  Source address
  Destination address
  Data to be sent ( files & messages)
  Other information like:
    Giving instructions to the network on how to send data
    Telling the receiving computer how to collect and arrange packets.
    Checking data from errors (determine the need to resend the data)

## Slide 10: A Typical data packet on the Network
error-checking component

## Slide 11: Error Detection

## Slide 12: Accuracy of the Transmitted Data
Data can be corrupted during transmission.
For reliable communication, errors must be detected and corrected.

## Slide 13: Single-Bit Error
  In a single-bit error, only one bit in the data unit has changed. (0 → 1 or 1 → 0)

## Slide 14: Burst Error
Two or more bits in the data unit have changed
Burst error does not necessarily mean that the errors occur in consecutive bits
Corrupted Bits = 4 bits

## Slide 15: Error Detection
Error detection uses the concept of redundancy, which means adding extra (redundant) bits for detecting errors at the destination
Notes: Redundancy is achieved through various coding schemes. The sender adds redundant
bits through a process that creates a relationship between the redundant bits and the
actual data bits. The receiver checks the relationships between the two sets of bits to
detect or correct the errors

## Slide 16: Error Detection Methods
Parity Check
Cycle Redundancy Check
Checksum
Error Detection Methods
Three types of redundancy checks:

## Slide 17: Parity Check
The most common and least expensive
a parity bit (extra bit)is added to every data unit so that the total number of 1’s is even or odd.
Simple parity check can detect single bit errors.
It can detect burst errors only if the total number of errors in each data unit is odd.

## Slide 18: Parity Check
1 | 1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Sender
Receiver
1 | 0 | 1 | 0 | 1 | 0 | 0
Data
Data + Redundancy Bits
The Medium
1 | 0 | 1 | 0 | 1 | 0 | 0
Even?
Yes , Drop parity bit & accept data
No
Reject Data
Calculate Parity bit
Count bits

## Slide 19: Cyclic Redundancy Check (CRC)
Used for error checking
Before sending data ,some calculation are done on the data packets to generate a CRC number
When data is received , the same calculation is done again to find out if the CRC number is the same .
  If CRC the same : data is correct
  If CRC are different : data has a problem and need to be sent again.
CRC Can detect single bit & burst errors.

## Slide 20: Checksum
to generate an error-detection character appended to the data.
This calculation is applied in both the sender side and the receiver side
  A match between receiver checksum and transmitted checksum indicates good data.
  A mismatch indicates an error has occurred.
Capable of detecting single or burst errors.
It is simple to implement in either hardware or software.

## Slide 21: Multiple Access Methods

## Slide 22: Multiple Access Methods
When nodes or stations are connected and use a common link (cable or Air) , called a multipoint or broadcast link, we need a multiple-access protocol to coordinate access to the link.
It is a set of rules that defines how a stations puts data onto the link and takes data from the link .

## Slide 23: Multiple Access Methods
Many formal protocols have been devised to handle access to a shared links. We categorize them into three groups.
Multiple Access Protocols
Controlled Access Protocol
Ex: Polling and Token passing
Random Access protocols
Ex: CSMA/CD and CSMA/CA
Channelization protocol
Ex: FDMA, TDMA, and CDMA

## Slide 24: CONTROLLED ACCESS
In controlled access, the stations consult one another to find which station has the right to send.
A station cannot send unless it has been authorized by other stations.
Notes: In these access methods, no contention and no collision take place.

## Slide 25: Polling Access Method
In this access method, one station is designated as the primary device and the other are secondary stations.
All access to the network is controlled by the primary station.
The primary queries (polls) each of the secondary stations in turn, if it has information to be transmitted.
Only when it is polled does the secondary have access to the communication channel.

## Slide 26: Token-Passing Access Method
In this access method, a special type of packet, called a token, circulates around a cable ring from station to station .
When any station on the ring needs to send data across the network, it must wait for a free token.
When a free token is detected, the station will take control of it if the station has data to send.

## Slide 27: Random Access Methods
In random access or contention methods, no station is superior to another station and none is assigned the control over another (i.e. each station has the right to the medium without being controlled by any other station).
It is named contention method because stations on the network contend, or compete, for an opportunity to send data.

## Slide 28: Carrier-Sense Multiple Access
In this way of methods, each station first listen to the cable (or check the state of the cable ) before sending.
When the station "senses" that the cable is free ( that there is no traffic on the cable) it can send a frame. Once the station has transmitted frame on the cable, no other station can transmit data until the original data has reached its destination and the cable is free again.

## Slide 29: Collisions
Even though each station listens for network traffic before it attempts to transmit, an access conflict -collision- will happen if more than one station tries to send at the same time.
When a collision happened, the frames will be either destroyed or modified
The collisions occur because it takes time for signals to propagate through the link.
Two specialized methods of collision management have been developed to improve performance:
  Collision Detection (CD)
  Collision Avoidance (CA).

## Slide 31: Carrier-Sense Multiple Access With Collision Detection (CSMA/CD)
The carrier-sense multiple access with collision detection (CSMA/CD) adds a procedure to handle a collision.
In this method, a station monitors the medium after it sends a frame to see if the transmission was successful. If so, the station is finished. If, however, there is a collision, the frame is sent again.
In the case of collision, the two stations involved stop transmitting for a random period of time and then attempt to retransmit.
Each station determines its own waiting period; this reduces the chance that the computers will once again transmit simultaneously.

## Slide 32: Carrier-Sense Multiple Access With Collision Avoidance (CSMA/CA)
The Carrier-Sense Multiple Access With Collision Avoidance (CSMA/CA) differs from the previous method in that there is no collision.
Each station signals its intent to transmit before it actually transmits data.

## Slide 33: CHANNELIZATION
Channelization is a multiple-access method in which the available bandwidth of a link is shared in time, frequency, or through code, between different stations.
Used for wireless communications.

## Slide 34: Frequency-Division Multiple Access
In frequency-division multiple access (FDMA), the available bandwidth is divided into frequency bands.
Each station is allocated a band to send its data. In other words, each band is reserved for a specific station, and it belongs to the station all the time.

## Slide 35: Time-division Multiple Access
In time-division multiple access (TDMA), the stations share the bandwidth of the channel in time.
Each station is allocated a time slot during which it can send data.
Each station transmits its data in is assigned time slot.

## Slide 36: Code-Division Multiple Access
In the code-division multiple access (CDMA), each station assigned a code that used to send its data.
CDMA differs from FDMA because only one channel occupies the entire bandwidth of the link.
It differs from TDMA because all stations can send data simultaneously; there is no timesharing.