## Slide 1: MICROSCOPY
Prepared by : Reem Aldossari

## Slide 2
APPLICATIONS OF COMPOUND
MICROSCOPE
It is used to study cells parts.
The organization of tissues and the structure of developing embryos, among many other important applications
And such more ….

## Slide 3
Parts of the Microscope:
The parts of the microscope can be grouped in three systems:
1. The magnification system.
2. The mounting and movement system.
3. The illumination system.

## Slide 4
The mounting and movement system
The body tube:
carries the ocular lenses
The arm:
Supports and connects the
upper part of the microscope
The coarse focusing knob:
for stage movement
The fine focusing knob:
for image sharpness
The nose piece:
Carries the objective lenses and
move them accordingly above the
stage
The stage:
Horizontal platform upon which
the slide of interest rest
The base:
Supports the microscope

## Slide 5
The ocular lenses:
5X, 10X, and 15X
The objective lenses:
Scanning lens: 3.5X or 4X or 5X
Low power lens: 10X
High power lens: 40X
Oil immersion lens: 100X
THE MAGNIFICATION SYSTEM
How to calculate the magnification power?
Magnification power = ocular lens xobjective lens.
(e.g.) 10X x 40X = 400X hint: Don’t forget the unit

## Slide 6
THE ILLUMINATION SYSTEM
The illuminator:
light source
The iris diaphragm:
controls the amount of light
reaching the slide
The condenser:
collects and concentrate the light

## Slide 7
It is the functional and structural unit in organisms.
different cell structures depending on their location
and function in the body.
3 major cell components:
Genetic material.
Cytoplasm.
Cell membrane.
THE CELL

## Slide 8
CELL TYPES
Two major cell types depending on the arrangement
of the genetic material inside the cell:
Prokaryotic cells (pro = before; Karyone = nucleus):
Nucleus is absent. The region where the DNA is
located in the cytoplasm is called nucleoid
Eukaryotic cells (True nucleated cells):
Nucleus is present. DNA is associated with
protein making chromatin

## Slide 9
PROKARYOTES: BACTERIA
Bacillus:
Rod shape and occur in strands.
Coccus:
Rounded and occur in colonies or strands.

## Slide 10
EUKARYOTES
Plant cells:
Have cell wall.
example: onion cells.
Rectangular with eccentric nucleus .
Onion cells
Animal cells
Animal cells :
Does NOT have cell wall.

## Slide 12
Simple Squamous Epithelium ( Lining of mouth )
1- Cell membrane
2- Cytoplasm
3- Nucleus

## Slide 13
Thank you
for your attention