## Slide 1: Microscopes
Object: To study the structure and function of compound microscope.
Microscopes
    Microscopes are devices that produce magnified images of structures that are too small to see with the naked eye.
    Resolution Power: The minimum distance of 0.2 m or 200 nm between the two particles

## Slide 2: Microscopes
  Light microscopes produce magnified images by focusing visible light rays.
  Electron microscopes produce magnified images by focusing beams of electrons.

## Slide 3: Microscopes
  Light Microscopes
    The most commonly used microscope is the light microscope.
    Light microscopes produce clear images of objects at a magnification of about 1000 times.

## Slide 4: Microscopes
Compound light microscopes allow light to pass through the specimen and use two lenses to form an image.
Light microscopes make it possible to study dead organisms and their parts, and to observe some small organisms and cells while they are still alive.

## Slide 5: Magnification Power (MP):
MP = Power of eye piece X Power of object piece
The total magnification is the eye x objective
 | Object lens | eye lens | Total Magnification
Scanning | 4x | 10x | 40x
Low Power | 10x | 10x | 100x
High Power | 40x | 10x | 400x
Oil Lens | 100x | 10x | 1000x

## Slide 6: Carrying a Microscope:
A
B

## Slide 9
Microscope Parts
Ocular
Body tube
Stage clip
Revolving nose piece
Objective
Arm
Stage
Diaphragm
Lever to move stage clip
Course adjustment
Fine adjustment
Light source
Base

## Slide 16: Microscopes
  Electron Microscopes (EM):
    Light microscopes cannot produce clear images of objects smaller than 200 nm.
    Resolution power for EM is about 0.5 nm..
    To study even smaller objects, scientists use electron microscopes.

## Slide 19: Microscopes
Electron microscopes use beams of electrons, rather than light, to produce images.
The best electron microscopes can produce images almost 1000 times more detailed than light microscopes can.

## Slide 25
برغـوث القطط
Cat flea

## Slide 26
رأس يراقة الذبابة الزرقاء

## Slide 27
خنفساء الطحين
Red Flour Beetle
head of a bedbug

## Slide 28
عـث الغـبـار
Dust mite

## Slide 29
Wasp’s Head

## Slide 30
Head of Honey Bee

## Slide 31
Bedbug

## Slide 33: Preparing Slides:
Using a pipet or dropper, add a drop of water or another solvent to a clean microscope slide. Then, place the specimen in the water.
Place the edge of a cover-slip on the slide so that it touches the edge of the water.
Slowly lower the cover-slip to prevent the formation of air bubbles.

## Slide 36
1
2
3
Epithelial (cheek) Cells:
1- Nucleus 3 - Cytoplasm
2- Plasma membrane

## Slide 39: Onion Cells Preparation

## Slide 40: Obtaining sample of onion epidermis

## Slide 41
Onion Cells:
1- Nucleus 3 - Cytoplasm
2- Cell Wall 4 - Plasma membrane
1
2
3
4