## Slide 1
Microscopy
Supervised by : Dr. Sherifa
Prepared by : Reem Aldossari
Lama Al abdi

## Slide 2
Genera!y, It is an instrument used to examine and
monitor objects we can’t see with the naked eye.
It has many applications.
Microscope

## Slide 3
There are different classes and types of microscopes depending
on the magnification power, their applications, and how they
are operated:
Simple Microscopes
Inverted microscope.
Light (compound) microscope.
Fluorescent Microscope
Types of microscopes

## Slide 4
-Simple Microscopes A magnifying glass, an ordinary double convex lens having a short focal length, is a simple microscope.
-A simple microscope has only one lens .
Simple Microscopes

## Slide 5
The compound
microscope is made of 3
systems:
The mounting and
movement System.
The magnification
System.
The iumination System.
Compound Microscope

## Slide 6
The mounting and movement system
The body tube:
carries the ocular lenses
The arm:
Supports and connects the
upper part of the microscope
The coarse focusing knob:
for stage movement
The fine focusing knob:
for image sharpness
The nose piece:
Carries the objective lenses and
move them accordingly above the
stage
The stage:
Horizontal platform upon which
the slide of interest rest
The base:
Supports the microscope

## Slide 7
The ocular lenses:
5X, 10X, and 15X
The objective lenses:
Scanning lens: 3.5X or 4X or 5X
Low power lens: 10X
High power lens: 40X
Oil immersion lens: 100X
THE MAGNIFICATION SYSTEM
How to calculate the magnification power?
Magnification power = ocular lens xobjective lens.
(e.g.) 10X x 40X = 400X hint: Don’t forget the unit

## Slide 8
THE ILLUMINATION SYSTEM
The illuminator:
light source
The iris diaphragm:
controls the amount of light
reaching the slide
The condenser:
collects and concentrate the light

## Slide 9
The light source and the
condenser are placed on
top of the stage while as
the objective lenses are
placed underneath
pointing up.
Useful for observing living
cells or organisms at the
bottom of a large container.
Inverted Microscope

## Slide 10: Fluorescent Microscope
The "fluorescence microscope" refers to any microscope that uses fluorescence to generate an image.

## Slide 11
Histo Chemical stains
Glycogen ( carmine stain )

## Slide 12
Protein ( bromophenol blue )

## Slide 13
Lipids ( Sudan black B)

## Slide 14
Thank you for your attention