## Slide 1: Network Topologies

## Slide 2: Objectives
Describe the basic and hybrid LAN physical topologies, and their uses, advantages and disadvantages.
Describe the backbone structures that form the foundation for most LANs

## Slide 3: Simple Physical Topologies
Physical topology: physical layout of nodes on a network
Three fundamental shapes:
  Bus
  Ring
  Star
  Mesh
May create hybrid topologies
Topology integral to type of network, cabling infrastructure, and transmission media used

## Slide 4: Why we need a topology
Choosing one topology over another can impact :
  type of equipment the network needs
  capabilities of the equipment
  network’s growth
  way a network is managed

## Slide 5: Bus

## Slide 6: Simple Physical Topologies
A Bus topology consists of a single cable—called a backbone— connecting all nodes on a network without intervening connectivity devices

## Slide 7: Bus (continued)
Devices share responsibility for getting data from one point to another
Terminators stop signals after reaching end of wire
  Prevent signal bounce
Inexpensive, not very scalable
Difficult to troubleshoot, not fault-tolerant

## Slide 8: Bus
Advantages
Works well for small networks
Easy to install
Relatively inexpensive to implement
Disadvantage
Management costs can be high
Network disruption when computers are added or removed
A break in the cable will prevent all systems from accessing the network.
Difficult to troubleshoot

## Slide 9: Ring

## Slide 10: Simple Physical Topologies
Ring topology
  Each node is connected to the two nearest nodes so the entire network forms a circle
  One method for passing data on ring networks is token passing
  Data travels around the network
  Traffic flows in one direction
  Slow performance
  One workstation goes down; whole network goes down
  Network is highly dependent

## Slide 11: Ring
Advantages
Cable faults are easily located, making troubleshooting easier
Ring networks are moderately easy to install
Disadvantage
Expensive
Requires more cable and network equipment at the start
Expansion to the network can cause network disruption
A single break in the cable can disrupt the entire network

## Slide 12: Star

## Slide 13: Simple Physical Topologies
Star topology
  Every node on the network is connected through a central device called hub or switch.

## Slide 14: Star (continued)
Any single cable connects only two devices
  Cabling problems affect two nodes at most
Requires more cabling than ring or bus networks
  More fault-tolerant
Easily moved, isolated, or interconnected with other networks
  Scalable
Supports max of 1024 addressable nodes on logical network

## Slide 15: Star
Advantages
Good option for modern networks
Low startup costs
Easy to manage
Offers opportunities for expansion
Most popular topology in use; wide variety of equipment available
Disadvantage
Hub is a single point of failure
Requires more cable than the bus

## Slide 16: Mesh

## Slide 17: Simple Physical Topologies
Mesh Topology: Each computer connects to every other.
High level of redundancy.
Rarely used.
  Wiring is very complicated
  Cabling cost is high
  Troubleshooting a failed cable is tricky
  A variation hybrid mesh – create point to point
connection between specific network devices, often
seen in WAN implementation.

## Slide 18: Mesh
Advantages
Robust
There is the advantage of privacy or security
The network can be expanded without disruption to current uses
Point to point links make fault identification and fault isolation easy
Disadvantage
Requires more cable than the other LAN topologies
Complicated implementation
  Installation and reconnection are difficult.
  Sheer bulk of wiring can be greater than the available space can accommodate
  Expensive

## Slide 19: Hybrid Physical Topologies
One example of Hybrid Topology is Tree topology
Tree topology is a combination of Bus and Star topology.
It consists of groups of star-configured workstations connected to a linear bus backbone cable.
If the backbone line breaks, the entire segment goes down
An example of this network could be cable TV technology

## Slide 20: Choosing a Topology
  BUS
    network is small
    network will not be frequently reconfigured
    least expensive solution is required
    network is not expected to grow much
  STAR
    it must be easy to add/remove PCs
    it must be easy to troubleshoot
    network is large
    network is expected to grow in the future
  RING
    network must operate reasonably under heavy load
    higher speed network is required
    network will not be frequently reconfigured