## Slide 1: Optical Microscopy
Study of how light passes through thin sections – rock cut and polished to about 0.3 mm thickness
Use properties of light absorption and propogation through a mineral  affected by atomic arrangement and composition
Learn the properties of light associated with techniques governing the use of a petrographic microscope
Notes: <number>

## Slide 2
Why use the microscope??
Identify minerals (no guessing!)
Determine rock type
Determine crystallization sequence
Document deformation history
Observe frozen-in reactions
Constrain P-T history
Note weathering/alteration
Fun, powerful, and cheap!
Notes: <number>

## Slide 3: Minerals and propogation of light
Opaque minerals – minerals in which light does not go through  always black even in thin sections. Typically these have molecules with higher atomic density (which includes many ore minerals). How light reflects off of these minerals is used to identify them with a reflected light microscope.
Nonopaque minerals – minerals in which light does go through  use these properties to identify them with the petrographic microscope
Notes: <number>

## Slide 4
The petrographic microscope
Also called a polarizing microscope
In order to use the scope, we need to understand a little about the physics of light, and then learn some tools and tricks…
Notes: <number>

## Slide 5
What happens as light moves through the scope?
light source
your eye
light ray
waves travel from source to eye
wavelength,
amplitude, A
light travels as waves
Frequency = # of waves/sec to pass a given point (hz)
f = v/ v = velocity
Notes: <number>

## Slide 6
We are dealing with white light in microscopy:
Violet (400 nm)  Red (700 nm)
White = ROYGBV
(can be separated by dispersion in a prism)
Notes: <number>

## Slide 7
light vibrates in
all planes that contain
the light ray
(i.e., all planes
perpendicular to
the propagation
direction
plane of
vibration
vibration direction
propagation direction
What happens as light moves through the scope?
Notes: <number>

## Slide 8
1) Light passes through the lower polarizer
west (left)
east (right)
Plane polarized light
PPL=plane polarized light
Unpolarized light
Only the component of light vibrating in E-W direction can pass through lower polarizer – light intensity decreases
Though polarized, still white light!
Notes: <number>

## Slide 9
Mineral properties: color & pleochroism
Color is observed only in PPL
Not an inherent property - changes with light type/intensity
Results from selective absorption of certain  of light
Pleochroism results when different  are absorbed differently by different crystallographic directions -
rotate stage to observe
plag
hbl
plag
hbl
Plagioclase is colorless
Hornblende is pleochroic
Notes: <number>

## Slide 10
Mineral properties: Index of refraction (R.I. or n)
Light is refracted when it passes from one substance to another; refraction is accompanied by a change in velocity
n1
n2
n2
n1
n2>n1
n2<n1
n is a function of crystallographic orientation in anisotropic minerals
  isotropic minerals: characterized by one RI
  uniaxial minerals: characterized by two RI
  biaxial minerals: characterized by three RI
n gives rise to 2 easily measured parameters: relief & birefringence
Notes: <number>

## Slide 11
Mineral properties: relief
Relief is a measure of the relative difference in n between a mineral grain and its surroundings
Relief is determined visually, in PPL
Relief is used to estimate n
olivine
plag
olivine: n=1.64-1.88
plag: n=1.53-1.57
epoxy: n=1.54
- Olivine has high relief
- Plag has low relief
Notes: <number>

## Slide 12
What causes relief?
nxtl > nepoxy
nxtl < nepoxy
nxtl = nepoxy
Hi relief (+)
Lo relief
Hi relief (-)
Difference in speed of light (n) in different materials causes refraction of light rays, which can lead to focusing or defocusing of grain edges relative to their surroundings
Notes: <number>

## Slide 13
2) Insert the upper polarizer
west (left)
east (right)
Now what happens?
What reaches your eye?
Why would anyone design a microscope that prevents light from reaching your eye???
XPL=crossed nicols (crossed polars)
south (front)
north (back)
Black!! (“extinct”)
© Jane Selverstone, University of New Mexico, 2003
Notes: <number>

## Slide 14
3) Now insert a thin section of a rock
west (left)
east (right)
Light vibrating E-W
How does this work??
Unpolarized light
Light vibrating in many planes and with many wavelengths
Light and colors reach eye!
Notes: <number>

## Slide 15
Conclusion has to be that minerals somehow reorient the planes in which light is vibrating; some light passes through the upper polarizer
Notes: <number>

## Slide 16
4) Note the rotating stage
Most mineral grains change color as the stage is rotated; these grains go black 4 times in 360° rotation-
exactly every 90o
Glass and a few minerals stay black in all orientations
These minerals are anisotropic
These minerals are isotropic
Notes: <number>

## Slide 17
Some generalizations and vocabulary
All isometric minerals (e.g., garnet) are isotropic – they cannot reorient light. Light does not get rotated or split; propagates with same velocity in all directions
  These minerals are always black in crossed polars.
All other minerals are anisotropic – they are all capable of reorienting light (transmit light under cross polars).
All anisotropic minerals contain one or two special directions that do not reorient light.
  Minerals with one special direction are called uniaxial
  Minerals with two special directions are called biaxial
Notes: <number>

## Slide 18
Isotropic
Uniaxial
Biaxial
How light behaves depends on crystal structure
Isometric
  All crystallographic axes are equal
Orthorhombic, monoclinic, triclinic
  All axes are unequal
Hexagonal, tetragonal
  All axes  c are equal but c is unique
Notes: <number>

## Slide 19
Isotropic minerals: light does not get rotated or split; propagates with same velocity in all directions
Anisotropic minerals:
    Uniaxial - light entering in all but one special direction is resolved into 2 plane polarized components that vibrate perpendicular to one another and travel with different speeds
    Biaxial - light entering in all but two special directions is resolved into 2 plane polarized components…
  Along the special directions (“optic axes”), the mineral thinks that it is isotropic - i.e., no splitting occurs
  Uniaxial and biaxial minerals can be further subdivided into optically positive and optically negative, depending on orientation of fast and slow rays relative to xtl axes
Notes: <number>

## Slide 20: ‘Splitting’ of light  what does it mean?
For some exceptionally clear minerals where we can see this is hand sample this is double refraction  calcite displays this
Light is split into 2 rays, one traveling at a different speed, and this difference is a function of thickness and orientation of the crystal  Norden Bombsight patented in 1941 utilized calcite in the lenses to gauge bomb delivery based on speed, altitude of plane vs target
ALL anisotropic minerals have this property, and we can ‘see’ that in thin sections with polarized light!
Notes: <number>

## Slide 21: Anisotropic crystals
O E
Double images:
Ray  2 rays with different propagation and vibration directions
Each is polarized (  each other)
Fig 6-7 Bloss, Optical Crystallography, MSA
Calcite experiment and double refraction
O-ray (Ordinary)  ω
Obeys Snell's Law and goes straight
Vibrates  plane containing ray and c-axis (“optic axis”)
E-ray (Extraordinary)  ε
deflected
Vibrates in plane containing ray and c-axis
..also doesn't vibrate  propagation, but we'll ignore this
Notes: <number>

## Slide 22
O E
Fig 6-7 Bloss, Optical Crystallography, MSA
IMPORTANT: A given ray of incoming light is restricted to only 2 (mutually perpendicular) vibration directions once it enters an anisotropic crystal
Called privileged directions
Each ray has a different n
   = no
   = nE
  in the case of calcite  < 
…which makes the O-ray dot appear above E-ray dot
Different rays going different speeds means they are at different wavelengths
Notes: <number>

## Slide 23
If I slow down 1 ray and then recombine it with another ray that is still going faster, what happens??
Notes: <number>

## Slide 24: Difference between our 2 rays
Apparent birefringence –  – difference in refractive index (speed) between the 2 rays
Retardation –   distance separating the 2 rays
Retardation therefore is a function of the apparent birefringence and the thickness of the crystal  ideally all thin sections are 0.3 mm, but mistakes do happen…
Notes: <number>

## Slide 25
Polarized light going into the crystal splits  into two rays, going at different velocities and therefore at different wavelengths (colors)
one is O-ray with n = 
other is E-ray with n = 
When the rays exit the crystal they recombine
When rays of different wavelength
combine  what things happen?


polarizer
Notes: <number>

## Slide 26
Notes: <number>

## Slide 27: Michel-Lévy Color Chart – Plate 4.11
Notes: <number>

## Slide 28
  1) Find the crystal of interest showing the highest colors ( depends on orientation)
  2) Go to color chart
    thickness = 30 microns
    use 30 micron line + color, follow radial line through intersection to margin & read birefringence
  Suppose you have a mineral with second-order green
  What about third order yellow?
Estimating birefringence
Notes: <number>

## Slide 29
Example: Quartz  = 1.544  = 1.553


1.553
1.544
Data from Deer et al
Rock Forming Minerals
John Wiley & Sons
Notes: <number>

## Slide 30
Example: Quartz  = 1.544  = 1.553
Sign??
(+) because  > 
   -  = 0.009 called the birefringence () = maximum interference color (when seen?)
  What color is this?? Use your chart.
Notes: <number>

## Slide 31
What interference color is this?
Notes: <number>

## Slide 32
Colors one observes when polars are crossed (XPL)
Color can be quantified numerically:  = nhigh - nlow
Notes: <number>

## Slide 33: Rotation of crystal?
Retardation also affected by mineral orientation!
As you rotate a crystal, observed birefringence colors change
Find maximum interference color for each in practice
Notes: <number>

## Slide 34: Extinction
When you rotate the stage  extinction relative to the cleavage or principle direction of elongation is extinction angle
Parallel, inclined, symmetric extinction
Divided into 2 signs of elongation based on the use of an accessory plate made of gypsum or quartz (which has a retardation of 550 nm) which changes the color  for a grain at 45º from extinction look for yellow (fast) or blue (slow)
Notes: <number>

## Slide 35
Notes: <number>

## Slide 36: Twinning and Extinction Angle
Twinning is characteristic in thin section for several common minerals – especially feldspars
The twins will go from light to dark over some angle
This is characteristic of the composition
Stage of the petrographic microscope is graduated in degrees with a vernier scale to measure the angle of extinction precisely
Notes: <number>

## Slide 37: Vernier scale
1.23
Notes: <number>

## Slide 38
Notes: <number>

## Slide 39
Notes: <number>

## Slide 40
Notes: <number>

## Slide 41
Notes: <number>

## Slide 42: Appearance of crystals in microscope
Crystal shape – how well defined the crystal shape is
  Euhedral – sharp edges, well- defined crystal shape
  Anhedral – rounded edges, poorly defined shape
  Subhedral – in between anhedral and euhedral
Cleavage – just as in hand samples!
Physical character – often note evidence of strain, breaking, etching on crystals – you will notice some crystals show those features better than others…
Notes: <number>

## Slide 43
So far, all of this has been orthoscopic (the normal way)
All light rays are ~ parallel and vertical as they pass through the crystal
Orthoscopic viewing
Fig 7-11 Bloss, Optical Crystallography, MSA
xl has particular interference color = f(biref, t, orientation)
Points of equal thickness will have the same color
isochromes = lines connecting points of equal interference color
At thinner spots and toward edges will show a lower color
Count isochromes (inward from thin edge) to determine order
Notes: <number>