## Slide 1
Parenteral
quality control

## Slide 2: Parenteral Quality Control Tests
4 main tests:
Sterility testing
Pyrogen testing
Particulate matter testing
Package integrity testing

## Slide 3: A- Sterility testing
Membrane filtration sterility testing
Direct transfer sterility testing
Product flush sterility testing

## Slide 4: A- Sterility testing
Membrane filtration sterility testing:
microorganisms will be collected on the surface of a 0.45 micron pore size filter.
Washing the filters with fluids to remove inhibitory properties (Bacteriostatic / Fungistatic properties).
This filter is segmented and transferred to appropriate media.
  fluid thioglycollate medium (FTM): support the growth of anaerobic and aerobic microorganisms
  soybean casein digest medium (SCDM): support a wide range of aerobic bacteria and fungi (i.e. yeasts and molds)
The incubation time is 7 days.

## Slide 5: A- Sterility testing
2. Direct transfer sterility testing
Method of choice for medical devices
The test article is completely immersed in the test media.
Complete immersion recommended: 2500 mL Max. Volume
After transferring, the samples are incubated for 14 days.

## Slide 6: A- Sterility testing
3. Product flush sterility testing
Recommended for transfusion and infusion assemblies that indicate a sterile fluid pathway that cannot be cut.
The products are flushed with fluid
The elute is membrane filtered
The filter is placed into media
This method is not generally used

## Slide 7: B- Pyrogen testing
USP Rabbit Pyrogen Test
Human Cell-Based Pyrogen Test
Bacterial Endotoxins Test (LAL Test)

## Slide 8: B- Pyrogen testing
USP Rabbit Pyrogen Test
Rabbits show a physiological response to pyrogen similar to humans.
Not valid for products that could mask the test by having a physiological effect on the rabbit.

## Slide 9: B- Pyrogen testing
USP Rabbit Pyrogen Test
Method:
Groups of three healthy, mature rabbits are chosen.
Accurate thermometers are inserted into the rectum of the rabbits to record their body temperature (control temp ).
Test solutions are warmed to 37 C prior to injection and then injected.
Rabbit temperatures are recorded at 30 min intervals between 1 and 3 h.

## Slide 10: B- Pyrogen testing
USP Rabbit Pyrogen Test
Results:
Temperature decreases are considered as zero rise.
If no rabbit shows an individual tempe rise of 0.5 C or more above its control temperature, the product meets the requirements for the absence of pyrogens.

## Slide 11: B- Pyrogen testing
B. Human Cell-Based Pyrogen Test
Pyrogens induce human monocytes to release pro-inflammatory cytokines such as Interleukins.
Test methods include incubation of a test sample with monocytes in whole blood or in cultured cell lines and analysis of a specific cytokine after a suitable time.

## Slide 12: B- Pyrogen testing
C. Bacterial Endotoxins Test (LAL Test)
A Limulus amebocyte lysate (LAL) reagent is the basis for an in vitro pyrogen test method that is specific for bacterial endotoxin pyrogen.
The LAL reagent was obtained horseshoe crab.

## Slide 13: B- Pyrogen testing
C. Bacterial Endotoxins Test (LAL Test)
Equal volumes of test solution and LAL reagent are mixed in glass test tubes.
After incubation at 37 C for 1 h, the tubes are observed for clot formation after inverting them.
Formation of a solid gel clot that withstands inversion of the tube constitutes a positive test.

## Slide 14: C- Particulate matter testing
Since erythrocytes have a diameter of approximately 4.5 m, particles of more than 5 m should be the basis for evaluation.
The unaided eye can see particles approximately 50 m.
10 m particles can be seen by the light scattered from them.

## Slide 15: C- Particulate matter testing
Full batch inspection
Light obscuration particle count test
Microscopic particle count test

## Slide 16: C- Particulate matter testing
Full batch inspection
100% batch inspection is recommended by GMP.
Done:
  by human inspection for all the units
  under a good light,
  and against a black and white background.
Automated inspection machines are also used.

## Slide 17: C- Particulate matter testing
B. Light obscuration particle count test
Use a suitable apparatus based on the principle of light blockage which allows an automatic determination of the size of particles and the number of particles according to size.
A shadow casts by the particle as it passes through a high intensity light beam.

## Slide 18: C- Particulate matter testing
B. Light obscuration particle count test
Mix the contents of the sample by slowly inverting the container 20 times successively.
If necessary, cautiously remove the sealing closure. Clean the outer surfaces of the container opening using a jet of particle-free water and remove the closure, avoiding any contamination of the contents.

## Slide 19: C- Particulate matter testing
B. Light obscuration particle count test
For large-volume parenterals, single units are tested.
For small-volume parenterals less than 25 ml in volume:
  contents of 10 or more units are combined in a cleaned container to obtain a volume of not less than 25 ml
  or diluting to 25 ml with particle-free water or with an appropriate particle-free solvent.
Powders for parenteral use are reconstituted with particle-free water or with an appropriate particle-free solvent.

## Slide 20: C- Particulate matter testing
C. Microscopic particle count test
The sample is filtered through a membrane filter under ultra clean conditions.
placed under a suitable binocular microscope.
count the number of particles that are equal to or greater than 10 μm and the number of particles that are equal to or greater than 25 μm.

## Slide 21: D- Package integrity testing
Bubble test
Dye Challenge test
Microbial Challenge test
Particulate Transmission

## Slide 22: D- Package integrity testing
1. Bubble test
The package is submerged in water or other suitable clear, colorless solvent.
A vacuum is exerted on the test system
The package is examined visually for evidence of gaseous leakage.

## Slide 23: D- Package integrity testing
2. Dye Challenge test
Containers are Immersed in a Dye Solution (1% methylene blue solution) and Subjected to Pressure or Vacuum Variances.

## Slide 24: D- Package integrity testing
3. Microbial Challenge test
Containers are Immersed in a Microbial Suspension (Pressure Differential) or Containers are Subjected to a Microbial Aerosol
Incubated.
N.B.: Container Contents Must Support Microbial Growth

## Slide 25: D- Package integrity testing
4. Particulate Transmission
The packages are placed in a chamber and subjected to a charged aerosolized dust.
The units are removed from the chamber and examined for dust entry.