## Slide 1
POROSITY DETERMINATION
FROM LOGS
Notes: <number>

## Slide 2: OPENHOLE LOG EVALUATION
Well Log
SP
Resistivity
Notes: <number>
This figure depicts the basic setup of the logging process. A wireline truck with a spool of logging cable is setup so that the sonde (measuring equipment) can be lowered into the wellbore. The logging tools measure different properties, such as spontaneous potential and formation resistivity, as the sonde is brought to the surface. The information is processed by a computer in the logging vehicle, and is interpreted by an engineer or geologist.

## Slide 3
Oil sand
Gamma
ray
Resisitivity
Porosity
Increasing
radioactivity
Increasing
resistivity
Increasing
porosity
Shale
Shale
POROSITY DETERMINATION BY LOGGING
Notes: <number>
An engineer or geologist can interpret the log readings to reach certain conclusions about the formation. For example, a decrease in radioactivity from the gamma ray log could indicate the presence of a sandstone formation. An increase in resistivity may indicate the presence of hydrocarbons. And, an increase in a porosity log might indicate that the formation has porosity and is permeable.

## Slide 4: POROSITY LOG TYPES
3 Main Log Types
Bulk density
Sonic (acoustic)
Compensated neutron
These logs do not measures porosity directly. To accurately calculate porosity, the analyst must know:
Formation lithology
Fluid in pores of sampled reservoir volume
Notes: <number>
.

## Slide 5: DENSITY LOGS
Uses radioactive source to generate gamma rays
Gamma ray collides with electrons in formation, losing energy
Detector measures intensity of back-scattered gamma rays, which is related to electron density of the formation
Electron density is a measure of bulk density
Notes: <number>

## Slide 6: DENSITY LOGS
Bulk density, b, is dependent upon:
  Lithology
  Porosity
  Density and saturation of fluids in pores
    Saturation is fraction of pore volume occupied by a particular fluid (intensive)
Notes: <number>

## Slide 7: DENSITY LOG
GR
API
0
200
CALIX
IN
6
16
CALIY
IN
6
16
RHOB
G/C3
2
3
DRHO
G/C3
-0.25
0.25
4100
4200
Caliper
Density
correction
Gamma ray
Density
Notes: <number>

## Slide 8
Formation (b)
Long spacing
detector
Short spacing
detector
Mud cake
(mc + hmc)
Source
Notes: <number>
To minimize the influence of the mud column, the source and detector, mounted on a skid, are shielded. The openings of the shields are applied against the wall of the borehole by means of an eccentering arm. The force exerted is substantial, and the skid has a plow shaped leading edge. Therefore, it is able to cut through soft mud cakes usually encountered at medium and shallow depths. Some mud cake may remain, however, and is “seen” by the tool as part of the formation. This must be accounted for.
A correction is needed when the contact between the skid and the formations is not perfect (due to mud cake or roughness of the borehole wall). In unfavorable cases, this correction can be fairly large. If only one detector is used, the correction is not easy to determine, as it depends on the thickness, the weight, and even the composition of the mud cake or mud interposed between the skid and formation.
Using two detectors, a correction can be made for unfavorable conditions.

## Slide 9: BULK DENSITY
Matrix
Fluids in
flushed zone
Measures electron density of a formation
Strong function of formation bulk density
Matrix bulk density varies with lithology
  Sandstone 2.65 g/cc
  Limestone 2.71 g/cc
  Dolomite 2.87 g/cc
Notes: <number>

## Slide 10: POROSITY FROM DENSITY LOG
Porosity equation
Fluid density equation
We usually assume the fluid density (f) is between 1.0 and 1.1. If gas is present, the actual f will be < 1.0 and the calculated porosity will be too high.
mf is the mud filtrate density, g/cc
h is the hydrocarbon density, g/cc
Sxo is the saturation of the flush/zone, decimal
Notes: <number>
We usually assume the fluid density (f) is between 1.0 and 1.1. If gas is present, the actual f will be < 1.0 and the calculated porosity will be too high.
mf is the mud filtrate density, g/cc
h is the hydrocarbon density, g/cc
Sxo is the saturation of the flush/zone, decimal
The bulk density log is a pad device. This means that the log must be in constant contact with the borehole wall. This is accomplished through the use of a caliper arm on the back side of the density device. When the pad loses contact with the formation either through rugosity or washouts, the bulk density reading is affected. The reading from the density log is always too low in the presence of rugosity or washout. This results in a calculated porosity that is much too high, because the density log is reading in essence the porosity of the washout or the gap between the porosity, pad, and the borehole wall. Although density logs are compensated for the presence of mudcake, this compensation is often inadequate to account for all of the effects of borehole breakouts, washouts, and rugosity.

## Slide 11: DENSITY LOGS
Working equation (hydrocarbon zone)
b = Recorded parameter (bulk volume)
 Sxo mf = Mud filtrate component
 (1 - Sxo) hc = Hydrocarbon component
Vsh sh = Shale component
1 -  - Vsh = Matrix component
Notes: <number>
b = Recorded parameter (bulk volume)
 Sxo mf = Mud filtrate component
 (1 - Sxo) hc = Hydrocarbon component
Vsh sh = Shale component
1 -  - Vsh = Matrix component

## Slide 12: DENSITY LOGS
If minimal shale, Vsh  0
If hc  mf  f, then
b =  f - (1 - ) ma
d = Porosity from density log, fraction
ma = Density of formation matrix, g/cm3
b = Bulk density from log measurement, g/cm3
f = Density of fluid in rock pores, g/cm3
hc = Density of hydrocarbons in rock pores, g/cm3
mf = Density of mud filtrate, g/cm3
sh = Density of shale, g/cm3
Vsh = Volume of shale, fraction
Sxo = Mud filtrate saturation in zone invaded by mud filtrate, fraction
Notes: <number>
d = Porosity from density log, fraction
ma = Density of formation matrix, g/cm3
b = Bulk density from log measurement, g/cm3
f = Density of fluid in rock pores, g/cm3
hc = Density of hydrocarbons in rock pores, g/cm3
mf = Density of mud filtrate, g/cm3
sh = Density of shale, g/cm3
Vsh = Volume of shale, fraction
Sxo = Mud filtrate saturation in zone invaded by mud filtrate, fraction

## Slide 13: BULK DENSITY LOG
GRC
0
150
SPC
MV
-160
40
ACAL
6
16
ILDC
0.2
200
SNC
0.2
200
MLLCF
0.2
200
RHOC
1.95
2.95
CNLLC
0.45
-0.15
DT
us/f
150
50
001) BONANZA 1
10700
10800
10900
Bulk Density
Log
RHOC
1.95
2.95
Notes: <number>

## Slide 14: NEUTRON LOG
Logging tool emits high energy neutrons into formation
Neutrons collide with nuclei of formation’s atoms
Neutrons lose energy (velocity) with each collision
Notes: <number>

## Slide 15: NEUTRON LOG
The most energy is lost when colliding with a hydrogen atom nucleus
Neutrons are slowed sufficiently to be captured by nuclei
Capturing nuclei become excited and emit gamma rays
Notes: <number>

## Slide 16: NEUTRON LOG
Depending on type of logging tool either gamma rays or non-captured neutrons are recorded
Log records porosity based on neutrons captured by formation
If hydrogen is in pore space, porosity is related to the ratio of neutrons emitted to those counted as captured
Neutron log reports porosity, calibrated assuming calcite matrix and fresh water in pores, if these assumptions are invalid we must correct the neutron porosity value
Notes: <number>

## Slide 17: NEUTRON LOG
Theoretical equation
N = Recorded parameter
 Sxo Nmf = Mud filtrate portion
 (1 - Sxo) Nhc = Hydrocarbon portion
Vsh Nsh = Shale portion
(1 -  - Vsh) Nhc = Matrix portion where  = True porosity of rock
N = Porosity from neutron log measurement, fraction
Nma = Porosity of matrix fraction
Nhc = Porosity of formation saturated with
hydrocarbon fluid, fraction
Nmf = Porosity saturated with mud filtrate, fraction
Vsh = Volume of shale, fraction
Sxo = Mud filtrate saturation in zone invaded by mud filtrate, fraction
Notes: <number>
N = Recorded parameter
 Sxo Nmf = Mud filtrate portion
 (1 - Sxo) Nhc = Hydrocarbon portion
Vsh Nsh = Shale portion
(1 -  - Vsh) Nhc = Matrix portion
where
 = True porosity of rock
N = Porosity from neutron log measurement, fraction
Nma = Porosity of matrix fraction
Nhc = Porosity of formation saturated with hydrocarbon fluid, fraction
Nmf = Porosity saturated with mud filtrate, fraction
Vsh = Volume of shale, fraction
Sxo = Mud filtrate saturation in zone invaded by mud filtrate, fraction

## Slide 18: POROSITY FROM NEUTRON LOG
GRC
0
150
SPC
MV
-160
40
ACAL
6
16
ILDC
0.2
200
SNC
0.2
200
MLLCF
0.2
200
RHOC
1.95
2.95
CNLLC
0.45
-0.15
DT
us/f
150
50
001) BONANZA 1
10700
10800
10900
Neutron
Log
CNLLC
0.45
-0.15
Notes: <number>
Uses a radioactive source to bombard the formation with neutrons
For a given formation, amount of hydrogen in the formation (I.e. hydrogen index) impacts the number of neutrons that reach the receiver
A large hydrogen index implies a large liquid-filled porosity (oil or water). The hydrogen index is calibrated to limestone porosity. If the lithology is sandstone or dolomite, the following chart can be used to correct the porosity.

## Slide 19
Upper transmitter
Lower transmitter
R1
R2
R3
R4
ACOUSTIC (SONIC) LOG
Tool usually consists of one sound transmitter (above) and two receivers (below)
Sound is generated, travels through formation
Elapsed time between sound wave at receiver 1 vs receiver 2 is dependent upon density of medium through which the sound traveled
Notes: <number>
Sonic tools are usually borehole compensated (BHC), which substantially reduces spurious effects at hole size changes as well as errors due to sonde tilt.
As shown in the figure, the BHC system uses two transmitters, one above and one below a pair of sonic receivers. When one of the transmitters is pulsed, the sound wave enters the formation, travels along the wellbore and triggers both of the receivers; the time elapsed between the sound reaching each receiver is recorded. The speed of sound in the sonic sonde and mud is less than that in the formations. Accordingly, the first arrivals of sound energy the receivers corresponds to the sound-travel paths in the formation near the borehole wall.
The BHC tranmitters are pulsed alternately, and the delta t readings are averaged. In this way, the tool is compensated for tilt.
If the travel time for the matrix is known, then porosity can be calculated.

## Slide 20
sec
50
T0
E2
E1
E3
Mud waves
Rayleigh
waves
Compressional
waves
Notes: <number>
This figure illustrates sonic log response to an acoustic wave transmitted through a compacted formation. The time, To, at which the acoustic wave was initiated at the transmitter, is shown for reference. The first arrival at the receiver is the compressional wave. The Rayleigh wave, traveling at a slower rate, arrives later and is superimposed on the compressional wave. Following the Rayleigh waves are the slower mud waves, transmitted through the mud column and the tool.
The flexibility of borehole-compensated (BHC) equipment permits the recording of acoustic logs other than delta t. These include the Amplitude Log for fracture detection, Cement Bond Log, and Variable Density Log.

## Slide 21: COMMON LITHOLOGY MATRIX TRAVEL TIMES USED
Notes: <number>

## Slide 22: ACOUSTIC (SONIC) LOG
Working equation
tL = Recorded parameter, travel time read from log
 Sxo tmf = Mud filtrate portion
 (1 - Sxo) thc = Hydrocarbon portion
Vsh tsh = Shale portion
(1 -  - Vsh) tma = Matrix portion
Notes: <number>
tL = Recorded parameter, travel time read from log
 Sxo tmf = Mud filtrate portion
 (1 - Sxo) thc = Hydrocarbon portion
Vsh tsh = Shale portion
(1 -  - Vsh) tma = Matrix portion

## Slide 23: ACOUSTIC (SONIC) LOG
If Vsh = 0 and if hydrocarbon is liquid (i.e. tmf  tf), then
tL =  tf + (1 - ) tma
or
s = Porosity calculated from sonic log reading, fraction
tL = Travel time reading from log, microseconds/ft
tma = Travel time in matrix, microseconds/ft
tf = Travel time in fluid, microseconds/ ft
Notes: <number>
s = Porosity calculated from sonic log reading, fraction
tL = Travel time reading from log, microseconds/ft
tma = Travel time in matrix, microseconds/ft
tf = Travel time in fluid, microseconds/ ft

## Slide 24: ACOUSTIC (SONIC) LOG
DT
USFT
140
40
SPHI
%
30
10
4100
4200
GR
API
0
200
CALIX
IN
6
16
Sonic travel time
Sonic
porosity
Caliper
Gamma Ray
Notes: <number>

## Slide 25: SONIC LOG
The response can be written as follows:
  tlog = log reading, sec/ft
  tma = the matrix travel time, sec/ft
  tf = the fluid travel time, sec/ft
   = porosity
Notes: <number>
Sonic log - measures the slowness of a compressional wave to travel in the formation.
where t is travel time (slowness)
  tlog is log reading, sec/ft
  tma is the matrix travel time, sec/ft
  tf is the fluid travel time, sec/ft
   is porosity
Matrix travel time (tma) is a function of lithology
tma = 53 sec/ft sandstone
tma = 46 sec/ft limestone
tma = 41 sec/ft dolomite
The sonic log measures the compressional arrival. There are several more sophisticated sonic logs that couple a different type of log and a more sophisticated processing algorithm to determine both the shear wave arrival and the compressional wave arrival. Using both the shear and compressional times, the log analyst can determine rock properties such as Poisson’s ratio, Young’s modulus, and bulk modulus. These values are very important when designing hydraulic fracture treatments or when trying to determine when a well may start to produce sand.

## Slide 26: SONIC LOG
GRC
0
150
SPC
MV
-160
40
ACAL
6
16
ILDC
0.2
200
SNC
0.2
200
MLLCF
0.2
200
RHOC
1.95
2.95
CNLLC
0.45
-0.15
DT
us/f
150
50
001) BONANZA 1
10700
10800
10900
Sonic
Log
DT
150
50
us/f
Notes: <number>

## Slide 27: EXAMPLE Calculating Rock Porosity Using an Acoustic Log
Calculate the porosity for the following intervals. The measured travel times from the log are summarized in the following table.
At depth of 10,820’, accoustic log reads travel time of 65 s/ft.
Calculate porosity. Does this value agree with density and neutron logs?
Assume a matrix travel time, tm = 51.6 sec/ft. In addition, assume the formation is saturated with water having a tf = 189.0 sec/ft.
Notes: <number>
Calculate the porosity for the following intervals. The measured travel times from the log are summarized in the following table.
Assume a matrix travel time, tm = 51.6 sec/ft. In addition, assume the formation is saturated with water having a tf = 189.0 sec/ft.

## Slide 28: EXAMPLE SOLUTION SONIC LOG
GRC
0
150
SPC
MV
-160
40
ACAL
6
16
ILDC
0.2
200
SNC
0.2
200
MLLCF
0.2
200
RHOC
1.95
2.95
CNLLC
0.45
-0.15
DT
us/f
150
50
001) BONANZA 1
10700
10800
10900
SPHI
ss
45
-15
SPHI
Notes: <number>

## Slide 29: FACTORS AFFECTING SONIC LOG RESPONSE
Unconsolidated formations
Naturally fractured formations
Hydrocarbons (especially gas)
Rugose salt sections
Notes: <number>

## Slide 30: RESPONSES OF POROSITY LOGS
The three porosity logs:
  Respond differently to different matrix compositions
  Respond differently to presence of gas or light oils
Combinations of logs can:
  Imply composition of matrix
  Indicate the type of hydrocarbon in pores
Notes: <number>

## Slide 31: GAS EFFECT
Density -  is too high
Neutron -  is too low
Sonic -  is not significantly affected by gas
Notes: <number>
Remember that the density log, the neutron log, and the sonic logs do not measure porosity. Rather, porosity is calculated from measurements such as electron density, hydrogen index and sonic travel time. The calculated density porosity is too high only because in the calculation we typically don’t account for the fluid density change. In other words, we assume the fluid density is 1 (or completely liquid filled) even though with gas that value is lower, which causes the calculated porosity to be too high. The neutron porosity is too low because the hydrogen index or the hydrogen density of gas is lower; therefore, the liquid-filled porosity is what the neutron log sees. So when gas is present, that value is lower than the actual porosity. And finally, the sonic log is not significantly affected by gas because it reads very near the wellbore and small gas saturations do not impact the overall travel time significantly.

## Slide 32: ESTIMATING POROSITY FROM WELL LOGS
Openhole logging tools are the most common method of determining porosity:
  Less expensive than coring and may be less risk of sticking the tool in the hole
  Coring may not be practical in unconsolidated formations or in formations with high secondary porosity such as vugs or natural fractures.
If porosity measurements are very important, both coring and logging programs may be conducted so the log-based porosity calculations can be used to calibrated to the core-based porosity measurements.
Notes: <number>
Determining formation porosity using open-hole porosity logging tools is the most common method of determining porosity for several reasons:
  Coring is often more expensive than logging and may be riskier in terms of sticking the tool in the hole.
  Coring may not be practical in soft unconsolidated formations or in formations with a high degree of secondary porosity such as vugs or natural fractures.
When porosity measurements are considered very important, both coring and logging programs are generally conducted. When both measurements are available, the log-based porosity calculations are usually calibrated to the core-based porosity measurements.

## Slide 33
Influence Of Clay-Mineral Distribution
On Effective Porosity
Dispersed Clay
Pore-filling
Pore-lining
Pore-bridging
Clay Lamination
Structural Clay
(Rock Fragments,
Rip-Up Clasts,
Clay-Replaced Grains)

e

e

e
Clay
Minerals
Detrital Quartz
Grains

e
e

Notes: <number>

## Slide 34: GEOLOGICAL AND PETROPHYSICAL DATA USED TO DEFINE FLOW UNITS
Flow
Units
Gamma Ray
Log
Petrophysical
Data
Pore
Types
Lithofacies
Core
1
2
3
4
5
Core
Plugs
Capillary
Pressure

vs k
Notes: <number>
Petrophysical analyses of core samples are used to identify reservoir flow units and non-flow units. The results are used to calibrate well logs, after which well logs can be used to map flow units throughout a field.

## Slide 35
Schematic Reservoir Layering Profile
in a Carbonate Reservoir
Baffles/barriers
3150
SA -97A
SA -251
SA -356
SA -71
SA -344
SA -371
SA -348
SA -346
SA -37
3200
3250
3300
3350
3100
3150
3250
3300
3250
3150
3200
3100
3150
3200
3250
3200
3250
3250
3350
3300
3150
3200
3250
3300
3100
3200
3250
3300
3350
3150
3200
3250
Flow unit
From Bastian and others
Notes: <number>
From studies of sedimentary facies, petrology, and petrophysics, we can correlate and map reservoir flow and non-flow (barrier/baffle) units to develop models for simulation. The example above shows carbonate flow (YELLOW) and non-flow (GREEN) reservoir units, Pozo Rica oil field, Mexico, based on core and well-log data. From an integrated reservoir study by H-RT.