## Slide 1: Paper and Thin Layer Chromatography (TLC)
Experiment 6
BCH 333
[practical]

## Slide 2
Objectives:
-Separation of amino acids using paper chromatography and TLC.

## Slide 3: :Chromatography
-is the collective term for a set of laboratory techniques for separate and identify the components of a mixture.

## Slide 4
General Principles:
-Separation of molecules :by distribution between a stationary phase and a mobile phase.
  -A stationary phase can be solid, gel, or liquid. Also called matrix, resin, or beads.
  -The mobile phase is the solvent and it is usually a liquid, but may also be a gas.
  -The compounds to be separated are considered solutes.
  -The separation of materials is based on differential partitioning [retardation]between the mobile and stationary phases.

## Slide 5
1-Paper chromatography [PC]:
- method for testing the purity of compounds and identifying substances.
- useful technique because it is relatively quick and requires small quantities of material.
substances are distributed between a stationary phase and a mobile phase.
[solutes are separated according to their solubility in mobile phase, or their attraction to the stationary phase].
The stationary phase:
is usually a piece of high quality filter paper.
[cellulose ]
polar substance
The mobile phase:
is a developing solution that travels up the stationary
phase, carrying the samples with it.
[shallow layer of solvent]

## Slide 7
Separation is depend on:
Components of the sample will separate on the stationary phase according to how strongly they adsorb to the stationary phase versus how much they dissolve in the mobile phase.
-This paper is made of cellulose [a polar substance] and the compounds within the mixture travel farther if they are non-polar. So, More polar substances bond with the cellulose paper more quickly, and therefore do not travel as far.
So:
Different compounds in the sample mixture travel at different rates due to
-differences in solubility in the solvent.
-differences in their attraction to the fibers in the paper.

## Slide 8: Paper Chromatography
-In this method, the solvent moves upward against gravitational force.
-The only force that cause the motion[of solvent and the compounds] is capillary force. So the speed of the process is slow.
Ascending:
Descending:
-In this method, the solvent is kept in a trough at the top of the chamber and is allowed to flow down the paper.
-The liquid moves down by capillary action as well as by the gravitational force.
-In this case, the flow is more rapid as compared to the ascending method.
Substances that cannot be separated by ascending method, can be separated by the above descending method.

## Slide 9
Descending Paper Chromatography

## Slide 10
2-Thin Layer Chromatography (TLC):
-The method is rapid and separations can be completed in less than one hour.
-TLC is a widely used.
-The stationary phase[Stationary phase: adsorbent]:
is a thin layer (0.25 – 0.5 mm) of adsorbent like silica gel - a polar substance- , [aluminium oxide or magnesium silicate] spread uniformly over the surface of a flat, inert surface of the glass plastic plate.
[The stationary phase+ support medium should be inert].
-Mobile phase: solvent.

## Slide 11
separation depend on:
-Partition of a solute between a moving solvent phase and a stationary aqueous phase. The solute therefore moves in the direction of a solvent flow at a rate determined by the solubility of the solute in the moving phase. Thus a compound with high mobility is more attracted to the moving solvent [mobile phase]than to the stationary phase.
Traveling of solvent via capillary action

## Slide 12
Factors effect the separation [resolution effects] :
1-Ion exchange effect: Any ionized impurities in the support medium will tend to bind or
attract oppositely charged ions and will therefore reduce the mobility of these solutes.
[resulting in bad resolution]
2- Temperature: since temperature can affect the solubility of a solute in a given solvent
temperature is also an important factor and often a chromatography laboratory has a fixed
temperature for optimum results.[increased temperature  increase solubility]
3- The molecular weight of a solute also affects the solubility and hence chromatographic
performance.[increased M wt less solubility].
4- Adsorption of compound (solute) onto support medium: Although the support medium
is inert, this is not always the case. If a solute tends to bind to the support
medium this will slow down its mobility in the solvent system.
5- Composition of the solvent: Since some compounds are more soluble in one solvent than in
the other the mixture of solvents used affect separation of the compounds.

## Slide 13
Thin layer chromatography[TLC]

## Slide 14
??

## Slide 15: Samples Analysis
-Amino acids  Specific color reagents are sprayed onto the plate or the paper [ninhydrin].
-sugars  spraying the plate or the paper with [aniline-diphenylamine].
-The paper or plate remaining after the experiment is known as the Chromatogram.

## Slide 16
Samples Analysis [Expression of the results]:
-Relative flow [Rf]:
-used to express the performance of a solute in a given solvent system/stationary medium.
Rf value may be defined as the ratio of the distance moved by a compound to that moved by the solvent.
Rf value is constant for a particular compound, solvent system and stationary phase.
Its value is always between zero and one
- Rf = Distance of migration of solute
Distance moved by solvent

## Slide 17
[Rf] Value:
-If Rƒ value of a solute is closer to zero, the solute has more attraction to stationary phase.
-If Rƒ value of a solute is closer to 1, then the solute has more affinity for the mobile phase and travels further.
-The final chromatogram can be compared with other known mixture chromatograms to identify sample mixes, using the Rf value in an experiment.

## Slide 19
paper chromatography. | (TLC)
-less required time. | -less required time than paper chromatography.
-It is fast. | -It is faster runs than paper,
-separate the sample. | -It has better separations than paper chromatography.
cellulose | Wide choice between different adsorbents[stationary phase].
Low resolution but also allow for quantitation. | It has better resolution and to allow for quantitation.
Expanded zonal spread[ not concentrated for quantitation analysis in need ]. | compact zonal spread[concentrated for quantitation analysis in need ].

## Slide 20
- Applications[TLC,PC]:
-identifying unknown compounds present in a given substance.
-qualitative and semi quantitation tests.
-separation of compounds in a sample.
-identify the purity of the sample.

## Slide 21
Phenylketonuria:
Non-functional phenylalanine hydroxylase enzyme.
This enzyme is necessary to metabolize the amino acid phenylalanine (Phe) to the amino acid tyrosine.
phenylalanine accumulates and is converted into phenylpyruvate (also known as phenylketone), which is detected in the urine.
Cystinuria:
Cystinuria is an inborn error of amino acid transport that results in the defective absorption by the kidneys of the amino acid called cystine. The name means "cystine in the urine.“
When the kidneys do not absorb cystine, this compound builds up in the urine.

## Slide 22
Questions:
-Silica gel is one of the stationary phases used in TLC which has an adsorbent property [ ].
-Rf for A = 0.6 and Rf for B=0.3. So, A has more affinity toward the stationary phase in compression with B [ ].
-it fine when we leave the lid of solvent chamber opened [ ].
-We should choose the solvent witch is suitable for solutes in that gives us a batter separation result [ ].
-when the solute is more attracted toward stationary phase it will migrate further [ ]
-Rf is some time equal to 1 [ ].

## Slide 23: http://www.uwplatt.edu/chemep/chem/chemscape/labdocs/catofp/chromato/tlc/tlc.htm