## Slide 1: 4th presentation
Radiographic technique of Ribs, Clavicle, scapula ,sternum, SCJs, ACJs

## Slide 2
BASIC | SPECIAL
AP posterior ribs (upper and lower ribs) PA anterior ribs (upper ribs) RPO, RAO ribs (upper and lower ribs) | 
AP Clavicle | PA Axial Clavicle
AP ACROMIOCLAVICULAR JOINTS (ACJs) | 
AP scapula lateral scapula RAO:LAO | 
RAO sternum Lateral sternum | 
PA bilateral sternoclavicular joints (SCJs) RA O sternoclavicular joints (SCJs) | 
Ribs, Clavicle, scapula ,sternum, SCJs, ACJs.

## Slide 3
  STERNUM (breast bone).
  12 PAIR OF RIBS.
  12 THORACIC VERTEBRA.
Bony Thorax (Anatomy)
  2 CLAVICLES
  2 SCAPULA

## Slide 4
AP posterior ribs (upper and lower ribs) ( Basic)
Film Size: 14x17 in. (35x43 cm). Crosswise or lengthwise.
SHIELDING: Shield gonadal region.
Patient Position: For upper ribs: Patient erect (preferred), specially in case of trauma to prevent lungs puncture by a fractured rib.
For Lower ribs: Patient supine.
Part Position: shoulders rotated interiorly to remove scapula away from the lung fields, Chin raised to prevent superimposition with upper ribs, patient looks straight ahead.
Distance: 100 cm or 40 in,
grid is used. kV(65 – 75) for above diaphragm,(75 – 85) for below diaphragm.
* C R: perpendicular to film.
CP :Upper ribs (above diaphragm): To 3or 4 in (8 – 10 cm )
below the jugular notch (level of T7 ).
Lower ribs (below diaphragm): Midway between
xiphoid and lower rib cage.
Collimation: collimate on four sides to area of interest
For upper ribs: Exposure on the arrested full inspiration
For lower ribs: Exposure on the arrested full expiration

## Slide 5
S S
above diaphragm :ribs 1 – 9 or 1 - 10 should be seen
below diaphragm ribs 8 - 12 should be seen.

## Slide 6
1
2
1= Posterior ribs
2= Anterior ribs

## Slide 7
PA anterior ribs (upper ribs) (Basic)
Film Size: 14x17 in. (35x43 cm). Crosswise or lengthwise
* SHIELDING: Shield gonadal region.
Patient Position: For upper ribs: Patient erect (preferred),or prone if necessary ,with arms down to the side.
Part Position: shoulders rotated anteriorly to remove scapula away from the lung fields.
No rotation of thorax or pelvis.
kV (65 – 75 for above diaphragm .
Distance: 100 cm or 40 in, grid.
CR: perpendicular to film.
CP: To T7 (7 to 8 in or 18 to20 cm below vertebra prominens as for PA chest)
Collimation: collimate on four sides to area of interest.
NB/ suspend respiration on inspiration.

## Slide 8
Structure shown:
ribs 1 - 9 or 10 visualized above diaphragm

## Slide 10
RPO, RAO ribs (upper and lower ribs) ( Basic)
Film Size: 14x17 in. (35x43 cm). lengthwise
SHIELDING: Shield gonadal region.
Patient Position: Upper ribs: Patient erect (preferred), specially in case of trauma to prevent lungs puncture by a fractured rib. An erect PA chest also recommended. Lower ribs: Patient supine, then rotated 45 posteriorly or interiorly.
Part Position: P O: Affected side should be close to cassette.
Part Position: AO: Affected side away from cassette, arm of elevated side raised above head, opposite arm extended down away from thorax, kV 65-75 (above diaphragm, 75 – 85 (below diaphragm).
CR: 90 to film center in each case.
CP: Upper ribs (above diaphragm): T7 ( 3to4 in(8-10 cm) below jugular notch).
Lower ribs: (below diaphragm): Midway between xiphoid process and lower rib cage.
RPO
RAO

## Slide 11
RPO , RAO ribs (upper and lower ribs) ( Basic)
RPO ribs (injury to right posterior ribs, above diaphragm).
RAO (injury to left anterior ribs, above diaphragm).
RPO
RAO
Rt
Rt
Affected side should be close to cassette
Affected side away from cassette
injury to the right side or pathology require RPO /LAO
injury to the left side or pathology require LPO /RAO
To move spine away from area of interest

## Slide 12
Rat
Rt

## Slide 13
RAO (injury to left anterior ribs, above diaphragm).
Affected side away from cassette

## Slide 14
AP Clavicle: ( Basic)
Film Size: 10x12 in. (24x30 cm). Crosswise.
SHIELDING: Shield gonadal region.
Patient Position: May be taken erect or supine.
Part Position: arms at sides, chin raised, back of shoulder in contact with the cassette or tabletop.
Distance: 100 cm or 40 in.
C R: AP: perpendicular to film or AP axial: 15- 30 cephalic.
C P: directed to midclavicle.
Collimation: collimate on four sides to area of interest.
Exposure on arrested inspiration.
15- 30 cephalic
perpendicular to film

## Slide 15
PA Axial Clavicle: S
*Film Size: 10x12 in. (24x30 cm). Crosswise
*SHIELDING: Shield gonadal region.
Patient Position: Patient erect, or lying down in prone position
Part Position: arms at sides, Head turned away from affected side.
*Distance: 100 cm or 40 in.
*Central Ray: 25 to 30 caudally.
Central Point: Mid shaft of clavicle.
Collimation: collimate on four sides to area of interest.
Exposure on arrested inspiration.
25 to 30 caudally.

## Slide 16
AP ACROMIOCLAVICULAR JOINTS (ACJs) ( Basic)
Film Size: 14x17 in. (35x43 cm). Crosswise.
SHIELDING: Shield gonadal region.
Done with /without stress markers weights (8 – 10 pounds, 10 – 15 for large adult patients).
Patient Position: Patient erect .
Part Position: back of shoulders against film, 2 films taken in the same position (one with the weights, other without), film 2” above shoulders.
Distance: 180 cm or 72 in.
Central Ray: 90 horizontal to film center.
Central Point: Midpoint between clavicles.
Collimation: Collimate on four sides to area of interest. Exposure on arrested inspiration.

## Slide 17
AP scapula ( Basic)
Film Size: 10x12in. (24x30cm). Lengthwise.
SHIELDING: Shield gonadal region.
Patient Position: May be taken erect or supine
( Erect is usually less painful for patient if condition allows).
Part Position: place posterior surface of shoulder in contact with film holder or table – top.
Gently abduct arm 90 degree and supinate hand.(abduction will move scapula laterally to clear more of thoracic structures.)
Distance: 100 cm or 40 in.
C R: perpendicular to film.
C P: mid scapular area 2inch inferior to coracoid process,
or to level of axilla and approximately 2in (5cm) medial
from lateral border of patient.
Collimation: collimate on four sides to area of interest.
Exposure on arrested inspiration.

## Slide 18
lateral scapula RAO:LAO ( Basic)
Film Size: 10x12 in. (24x30 cm)lengthwise.
SHIELDING: Shield gonadal region.
Patient Position: May be taken erect or supine ( Erect is usually less painful for patient if condition allows) Face patient toward cassette in anterior oblique position.
Part Position: hand patient reach across front of chest and grasp opposite shoulder. This best Demonstrates body of scapula.
affected arm drop, flex elbow, and place forearm behind lower back with arm partially abducted. This best Demonstrates acromion and coracoids processes.
Palpate border of scapular and rotate patient until the scapular is in true lateral position.
The average patient will be rotated 30 to45 degree from lateral position which result in a 45 to 60 anterior oblique position. lateral scapula
Distance: 100 cm or 40 in.
Central Ray: perpendicular to film.
Central Point: midvertebral border of scapula.
Collimation: collimate on four sides to area of interest. Exposure on arrested inspiration.
body of scapula
RAO

## Slide 20
RAO sternum (Basic)
Film Size: 10x12 in. (24x30 cm) lengthwise.
SHIELDING: Shield gonadal region.
Patient Position: Patient erect ( preferred). or Semiprone position .
Part Position: Patient erect with arms on sides, or semi prone with the left arm up and the right arm down by the side and slightly oblique (15 - 20, to the right side ).
Distance: 100 cm or 40 in.
Central Ray: perpendicular to film
Central Point: Center of sternum (midway between jugular notch and the xiphoid process).
Collimation: collimate on four sides to area of interest.
Breathing technique preferred if patient can cooperate.
( exposure on normal Quiet breathing), or else, during a suspended expiration.

## Slide 21
Lateral sternum (Basic)
Film Size: 10x12 in. (24x30 cm) lengthwise.
SHIELDING: Shield gonadal region.
Patient Position: May be taken erect ( preferred) or Lateral recumbent.
Part Position: Position patient with shoulders and arms drawn to back, or in a lateral recumbent (lying on the side, arms above the head), shoulders well back.
Distance: 150 to 180cm or 60 to 72in.to reduce magnification of sternum caused by
Increased OID.
Central Ray: perpendicular to film.
Collimation: collimate on four sides to area of interest.
Central Point: Center of sternum (midway between jugular notch and the xiphoid process). exposure during a suspended inspiration.

## Slide 22
Structure shown:
entire sternum with minimal overlap of soft tissue.

## Slide 23
PA bilateral sternoclavicular joints (SCJs) (Basic
Film Size: HD 18x24 cm.
SHIELDING: Shield gonadal region.
Patient Position: Patient prone.
Part Position: pillow for head ,which must be turned to one side, arms up beside the head.
Distance: 100 cm or 40 in.
C R: perpendicular to film..
CP: At level of T2-T3 3in (7 cm )distal to vertebra prominens.
Collimation: collimate on four sides to area of interest.
exposure done during suspended expiration..

## Slide 25
RA O sternoclavicular joints (SCJs) (Basic)
* Film Size: HD 18x24 cm Crosswise.
SHIELDING: Shield gonadal region.
Patient Position: Patient prone.
Part Position: rotated 15, up-side arm in front of the patient, opposite arm behind the Patient.
Distance: 100 cm or 40 in.
C R: perpendicular to film.
CP: At level of T2-T3 3in distal to vertebra prominens.
Collimation: collimate on four sides to area of interest.
exposure done during suspended expiration.