## Slide 1
Quality control & Statistics

## Slide 2
Definition: it is the science of gathering , analyzing, interpreting and representing data.
Example: introduction a new test
Steps:
study the publication.
Select the most practical one/s
Precision and accuracy must be evaluated.
Development of reference range to be compared with the manufacturer's as well as to be kept as a lab reference.
As the method been applied, precision and accuracy should be assessed to assure a reliable analysis.
Statistical Concept

## Slide 3: Types of Statistics:
1- Descriptive statistics
2- Inferential Statistics.
Descriptive statistics: used to summarize the important features of a group of data.
Descriptive statistics of groups of single observation. The statistical tests are mean, median, percentile, and standard deviation.

## Slide 4: Types of Statistics:
Descriptive statistics of groups of Paired observation:
* The most informative step in the evaluation of new analytical method is the comparison of methods experiment, in which patient specimens are measured by both the new and the old, or comparative method.
* The agreement between the tow methods may be estimated from the straight line that best fits the points, the visual estimation may be used to draw line, Linear Regression Analysis.

## Slide 5: Paired observation: (cont.)
* Linear regression assumes that there is no measurement error in the comparative method and the spread of the points around the regression line is due to random error.
* The Correlation Coefficient ‘r’: is the measure of the strength of the relationship between the Y and X variable (it’s value between -1 - +1) . A value of 0.1 indicates a perfect relationship.
2- Inferential Statistics
* Are used to compare the means or SD of two groups of data. The t-test is used to determine whether there is a statistically significant difference between the mean of two groups.
* The F-test is used for SD, the lower the probability the more statistically significant.

## Slide 6: Reference Interval (Normal Ranges)
A physician order a lab test for: diagnosis, screening, monitoring, determining prognosis, confirming a previously abnormal tests, education, and for medicolegal purposes.
* The first 4 are usually compared with a reference intervals.
Definition:
The usual values for healthy population. It could be constructed for ill population too.

## Slide 7
Factors for establishing reference intervals:
Make up of the reference population with respect to age, sex, and genetic and socioeconomic factors.
The criteria used for including or excluding individuals.
Physiological and environmental condition: date of collection, intake of food, time, drugs, smoking…ect.
Collection procedures and preparation of individuals.
The analytical method used.

## Slide 8
For a test that is used to diagnose a certain disease, the diagnostic sensitivity is the proportion of individuals with that disease who test positively with the test.
The Specificity of a test is defined as the proportion of individuals without the disease who test negatively for the disease.
Sensitivity % =
The number of diseasesd individuals with a positive test
Total number of diseasesd individuals tested
X 100
Specificity % =
The number of diseasesd individuals without the disease with a negative test test
Total number of diseasesd individuals tested without the disease
X 100

## Slide 13
ISO Documents - Laboratory
ISO 9001:1994 Quality Systems – Model for QA in design, development production, installation, and servicing
ISO/FDIS 15189 – Quality management in the clinical laboratory (1998)
ISO/IEC 17025 – General requirements for the competence of testing and calibration labs (1998)

## Slide 14
NCCLS: A Quality System Model for Health Care (HS 1-A)
The National Committee for Clinical Laboratory Standards
Lays out quality system model
Has applicability to all health care systems, including laboratory
Describes 12 quality system essentials
Applies quality design consistent with ISO 9000 series

## Slide 15
QUALITY ASSURANCE DEFINITION
All planned and systematic actions necessary to provide adequate confidence that goods or services will satisfy the customer’s needs.

## Slide 16
EXTERNAL QUALITY ASSESSMENT (EQA)
EQA REFERS TO A SYSTEM IN WHICH THE PERFORMANCE OF A LABORATORY IS ASSESSED
PERIODICALLY AND RETROSPECITIVELY
BY AN INDEPENDENT OUTSIDE AGENCY TO INDICATE TO THE LABORATORY STAFF WHERE THERE MAY BE SHORTCOMINGS AND HENCE INDICATES A NEED FOR IMPROVING AND/OR CHANGING IQC PROCEDURES.

## Slide 17
INTERNAL QUALITY CONTROL (IQC)
IQC REFERS TO THE SET OF PROCEDURES UNDERTAKEN BY THE LABORATORY STAFF FOR THE
CONTINUOUS AND IMMEDIATE
MONITORING OF LABORATORY WORK IN ORDER TO DECIDE WHETHER THE RESULTS ARE RELIABLE ENOUGH TO BE RELEASED.

## Slide 18
IMPLEMENTATION of the QUALITY SYSTEM
Planning what is to be done
Documenting the plan
Implementing the plan
Periodically auditing procedures to ensure the plan is still working and being used
Reviewing the plan periodically to confirm its continuing effectiveness

## Slide 19
Quality System Essentials
Organization
Personnel
Equipment
Purchasing and inventory
Process control
Information management
Documents and records
Occurrence Management
Internal assessment
Process improvement
Service and satisfaction
Facilities and Safety

## Slide 20
LABORATORY MANAGEMENT MUST COMMIT TO MEETING QUALITY NEEDS, ESTABLISH POLICIES, PROCESSES AND PROCEDURES
EVERY STAFF MEMBER IS RESPONSIBLE FOR THE QUALITY OF THEIR WORK.
EVERY STAFF MEMBER MUST BE AWARE OF THE QUALITY OBJECTIVES AND POLICIES OF THE LABORATORY

## Slide 21
Sources of Laboratory QS Guidance and Information
  World Health Organization (WHO)
  International Organization for Standardization (ISO)
  NCCLS
  CDC guidelines
  Professional & accrediting organizations
  National standards & regulations