## Slide 1: Odontotechnology
Semmelweis University, Faculty of Dentistry, Department of Prosthodontics
Head of Department: Prof. Dr. Pál Fejérdy
Head of Department of Prosthodontics Preclinical and General Dental Materials:
Dr. András Kóbor, Associate Professor
Lecturer:
Dr. Péter Kivovics Associate Professor Tutor: Dr. Judit Borbély
Head of Central Dental Laboratory:
Zoltán Hajdu dtm.
Dr. Mercédesz Linninger
Dr. Emese Ábrám
Dr. Ágnes Ágopcsa
Dr. Péter Faluhelyi
Dr. Péter Lukács
Dr. Orsolya Németh
Dr. Katalin Perger
Dr. János Schmidt
Dr. Borbála Soós
Dr. Örs Tollas

## Slide 2: REMOVABLE PARTIAL DENTURES
Semmelweis University
Department of Prosthodontics
Odontotechnology practice lectures

## Slide 3: Removable partial denture
an appliance which restores a partial loss of natural teeth and associated tissues
it can be removed from the mouth and replaced by the patient

## Slide 4: Support classification of partail dentures
Support: resistance to vertical components of masticatory force in a direction toward the basal seat
Support can be according to Cradock:
1. dental support
2. mucosal support
3. mixed: dental and mucosal/mucosal and dental support

## Slide 5: Support classification of partai dentures

## Slide 6: Support classification of partial dentures

## Slide 7: Retention
Retention: the resistance to movement of a removable partial denture from its supporting tissues

## Slide 8: The component parts of removable partial denture

## Slide 9: Parts of the baseplate
Saddle
Connector
Occlusal rest

## Slide 10: Materials of the baseplate
Acrylic
Metal
Metal-acrylic combination
(alloys used for partial denture fabricating: cobalt-chrome alloys, gold alloys and titanium)

## Slide 11: Saddle
Replaces the lost of the alveolar tissues and carries arteficial teeth (obligatory function)
Can take part in support and retention (optional function)
Types: 1. bounded
2. free end

## Slide 12: Connector
Connects the two sides of the denture (the saddles) together, provides the rigid unit of the dental appliance (obligatory function)
Can take part in the support and retention (optional function)

## Slide 13: Guidelines for designing the connector part
Protection of the periodontal tissues
Extension
Straight contour
Material-technology

## Slide 14: Guidelines for designing the connector part
the protection of the tissues of the marginal periodontium must be carried out

## Slide 15: Extension of the connector part
Reduction
The connector part must be rigid, the possibility of reduction depends on the type of the support

## Slide 16: Contour
With straight contour we provide the proper cleaning of the removable partial denture, and it is more comfortable for the patient (speech)

## Slide 17: Material and technology
The material of the baseplate is metal, except in the cases of mucosal and dental, and mucosal support

## Slide 18: Main types of the connector
Upper arch:
- butterfly (lateral edentulous areas)
- horseshoe (anterior edentulous area)
- fenestrated (decreasing the size of the
baseplate)
- sceletonized (fully tooth-supported)
Lower arch:
- lingual bar: most widely used

## Slide 19: Butterfly

## Slide 20: Horseshoe

## Slide 21: Fenestrated

## Slide 22: Sceletonized

## Slide 23: Lingual bar

## Slide 24: Occlusal rest
Provides the tooth support (obligatory funcion)
Can take part in avioding tilting (optional function)

## Slide 25: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
Medical and dental history; extra-and intraoral examination; Xray analysis; classify the dental condition (Kennedy, Fábián and Fejérdy)
Treatment planning
Primary impresion taking

## Slide 26: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
Materials used for primary impression taking:
  alginate
  silicones
  Taken by a stock tray !

## Slide 27: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
After pouring out the primary impression in the laboratory, we get the primary cast
On the primary cast we outline the borders of the special tray

## Slide 28: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
secondary impression taking by the dentist with special tray (silicones)

## Slide 29: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
On the secondary cast at the dental office we design the removable partial denture, outline the saddle areas, occlusal rests and the retainers
The secondary cast is the mastercast (made of stone or precise die stone)

## Slide 30: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
With the duplicaton of the mastercast we get the working cast for making the wax pattern and investing
Materials used for duplicating the mastercast:
  duplicating gels
  silicones
Images from Bego Virtual Academy

## Slide 31: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
On the surface of the workingcast the dental technician makes the wax pattern from prefabricated wax elements
Images from Bego Virtual Academy

## Slide 32: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
After sprueing the working cast is ready for investing
Images from Bego Virtual Academy

## Slide 33: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
Investing with flask
Investment materials used for cobalt-chromium alloys:
  Phosphate bonded
  Silica bonded
  Gypsum bonded
  Investing is carried out by vibration.
Images from Bego Virtual Academy

## Slide 34: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
deflasking
Images from Bego Virtual Academy

## Slide 35: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
finishing of the ready metal frame
(sandblasting, trimming, polishing)
Images from Bego Virtual Academy

## Slide 36: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
At the dental office we check the ready frameworks and determine the jaw relationship with wax occlusal rim and choose the sade
At the laboratory they set up the teeth

## Slide 37: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
After setting up the teeth we try in the trial denture at the office
Check up the occlusion, articulation, shade
Processing

## Slide 38: Procedures in the dental office and in the laboratory for fabricating a removable partial denture
Insertion