## Slide 1: SPECTROPHOTOMETRY

## Slide 2: Principle :
there is interaction between the light and sample particle , spectrophotometer is employed to measure the amount of light that a sample absorbs .

## Slide 3
spectrophotometer consists of two instruments:
1- spectrometer
for producing light of any selected color (wavelength
2- photometer
for measuring the intensity of light.
The instruments are arranged so that liquid in a cuvette can be placed between the spectrometer beam and the photometer

## Slide 4
The most common spectrophotometers are used in the UV and visible regions of the spectrum .

## Slide 5
Light source :
Two kinds of lamps
1- Deuterium lamp in UV- spectrophotometer
spectrophotometer - 2- tungsten lamp in visible

## Slide 6
Sample cell :
A container that contains a sample is usually called "cell“
two types are available:
1- glass used in visible spectrophotometer
2- quartz used in UV spectrophotometer .

## Slide 7: Application :
1- qualitative :
The wavelength of maximum conc. give information about structure in λ max
2- quantitative :
Determination of conc. By beer’s law
A = abc

## Slide 8
Sample and standard solution :
To measure the concentration of a substance, a sample of (unknown concentration) is compared with known concentration (standard solution) to determine the concentration .
The blank contain all the substance except the analyte