## Slide 1: Small Bowel procedures
Manal AlOsaimi

## Slide 2: Small Bowel Procedures
Barium meal follow through.
Enteroclysis
Intubation ( Small bowel enema).
Barium follow through (Small Bowel only Series).
1
2
3
4

## Slide 3: Anatomy

## Slide 4: Anatomy
Parts of S.I:
Duodenum: 1st,shortest,widest and most fixed.
Jejunum: 2/5 and feathery appearance.
Ileum: 3/5, longest, smooth no feathery appearance, and joins large intestine at ileocecal valve.

## Slide 6
Small Bowel Gas Pattern
Centrally located
Soft tissue across
entire lumen
Colon Gas Pattern
Peripheral Located
Mostly not overlapping
Haustra markings

## Slide 7
A: duodenum
C: jejunum
D:ileum
E: area of ileocecal valve
PA 30 mins

## Slide 8: To Prepare:
1
NPO
For 8 hrs.
2
Low residue diet
2 days before the procedure.
3
No smoking or chewing gum during the NPO period.
4
Void before the procedure
To avoid displacement of the ileum due to distended bladder
5
Enhance the rate of gastric emptying
Metoclopramide 20 mg orally, 20 min before examination

## Slide 9: 1. Ba Meal Follow through
Routine UGI first
Patient ingests a cup of Ba when UGI series is completed (note the time)
30 min PA radiograph (30 min after 1st Ba ingestion, usually 15 min after UGI series is completed)
Half-hour interval radiographs until Ba reaches large bowel (usually 2 hours)
If more time is needed(< 2hrs) 1-hour interval radiographs are obtained.
Optional: spot films of ileocecal valve using compression cone??
To separate the bowel loops that may obscure the terminal ileum

## Slide 10
PA 30 min 1 hr

## Slide 11
2 hr

## Slide 12: Ileocecal valve
Spot film with compression cone?
To separate the bowel loops that may obscure the terminal ileum

## Slide 13: 2. Ba Follow through (S.B only)
Plain radiograph(scout).
2 cups of Ba ingested (note the time.)
15 or 30 min radiograph (center to the iliac crest “high” to include the stomach, because most of the Ba is in the stomach and proximal S.B.)
Half-hour interval radiographs until Ba reaches large bowel (usually 2 hours)
If more time is needed(< 2hrs) 1-hour interval radiographs are obtained.

## Slide 14: 3. Enteroclysis
Injection of c/m into the S.B.
It is a Double contrast method used to evaluate the S.B.
the pt is intubated under flouroscopic control with a special catheter. Stomach → duodenum → duodenojujinal junction.
CM
  Thin BaSO4. ( Coats the mucosa).
  Air or Methylcellulose

## Slide 15: 3. Enteroclysis
Double Contrast

## Slide 16: 4. Intubation ( S.B enema)
It is a single contrast method where a nasogastric tube is passed through:
pt’s nose→esophagus→stomach→duodenum and into the jejunum. (RAO position is preferred ? )
To help pass the tube from stomach →duodenum by gastric peristalsis.
C.M: thin BaSO4 or water soluble iodinated c.m
diagnostic
Therapeutic

## Slide 17: 4. Intubation
Single Contrast

## Slide 18: Thank you