## Slide 1: Soil Water Relationships: Permeability, Drainability and Hydraulic Conductivity

## Slide 2: Objectives
Define water holding capacity and gravitational water.
Explain how water holding capacity and permeability is affected by soil type.
Define permeability.
Describe the effects of soil type on permeability.
Evaluate the drainability of soils.

## Slide 3: Objectives
Define the forces that act on soil water.
Discuss how water moves through the soil.
Measure the flow of water through different soil textures.

## Slide 4: Terms
Adhesion
Capillary Rise
Cohesion
Drainage
Gravitational Flow
Gravitational Water
Hydraulic Conductivity
Permeability
Saturation
Water Holding Capacity

## Slide 5: What is water holding capacity and what is gravitational water?
- Water holding capacity is the amount of moisture that is held by the soil available to the plants.
- Gravitational water is free water that moves downward through the soil due to gravity.

## Slide 6
Soils have different levels of water holding capacity largely determined by the texture of the soil.
Soil Texture is the relative amount of sand, silt and clay in the soil.
Hydraulic conductivity is a measure of the rate of water movement through the soil.

## Slide 7
The soil texture also affects pore space, a portion of the soil not occupied by solid material but filled with air or water.
The larger the soil particle the larger the pore spaces.
Small particles have more spaces but they are smaller in size.

## Slide 8: How is water holding capacity affected by soil type?
A. Soils of different types affect the water holding capacity.
  1.Soils with fine texture are composed mainly of clay and hold water very firmly. There is less gravitational water with fine textures.

## Slide 9
B. Soils with medium texture have intermediate amounts of sand and clay, with a large representation of silt.
  1. Medium soils hold water well but still allow movement downward.
C. Soils with coarse texture represent those soils that are largely composed of sand.
  1. Coarse soils will not hold water very firmly and have fast permeability.

## Slide 10
Water holding capacity is the amount of moisture able to be held by the soil that is available to plants.
Gravitational water is the free water that moves downward through the soil.
Both affect the workability and moisture availability to plants

## Slide 11: What is permeability?
Permeability is the movement of water through the soil, synonymous with hydraulic conductivity and drainability.

## Slide 12
Permeability allows movement of water and in many cases nutrients through the soil.
The movement of the nutrients through the soil can be significant if the soil has much permeability.

## Slide 13: SOIL PERMEABILITY RATES

## Slide 14: How is permeability affected by soil type?
Soil type can affect permeability.
Medium texture allows for moderate permeability.
Coarse soils have rapid permeability.

## Slide 15
Fine soils have slow permeability and do not drain well.
Drainage is the movement of excess water through the soil, removal of water from the soil.

## Slide 16: How can you evaluate the drainability of soils?
Soil drainability is measured by the speed of which a given amount of water passes through the soil.
In a laboratory situation one may take two different soils and set up an experiment to measure the drainability of each.

## Slide 17
On field conditions the drainability may be done by measuring the time it takes a soil to absorb 10 gallons of water as compared to another soil.
  This procedure is done often in landscaping situations to determine if amendments need to be added. Soil in the field is difficult to amend.

## Slide 18: Texture classification

## Slide 19: Textural Triangle

## Slide 20: What forces act on soil water?
There are two main forces which act on soil that relates to water.
  Adhesion is an attractive force that acts between two different substances. In soil water it is the attraction of soil to water.

## Slide 21
  Cohesion is a force that acts between molecules of similar substances. In the soil it is the attraction of water to itself.
The balance of these forces determine the availability of water to plants and how water moves through the soil.

## Slide 22: How does water move through the soil?
Water moves through the soil in many ways.
Soil pores fill with water as water enters the earth’s crust. Water moves through the soil both by capillary action and by gravity.

## Slide 23
Capillary rise is the movement of water through soil capillaries. Three soil water types determine this movement of water into the soil.
Capillary water is water that is held loosely by cohesive forces and is most readily available for plants.

## Slide 24
Hygroscopic water is held very firmly to the soil by adhesion.
Gravitational water is water that is pulled downward through a process called gravitational flow.

## Slide 25
Hydraulic conductivity is a trait of soil that relates to the ease of water movement through the soil. The higher the hydraulic conductivity the more water that is moved through the soil.
Eventually all of the pores in the soil are filled with water, which is saturation. The soil does not contain any air so plant growth is compromised.

## Slide 26
Capillary water is water that moves freely through the soil.
Gravitational water is water that leaves the soil caused by the forces of gravity.
The movement of water through the soil can be measured in several ways.

## Slide 27: How can you measure water through the soil?
The movement of water through the soil can be measured in several ways.
One method of measuring water movement is to measure the capillary action through a test tube full of soil.
Other methods include measuring the time it takes for soil to move through or by measuring permeability.

## Slide 28: Forces acting on soil and water
Two main forces act on soil and water.
  Adhesion is the force that acts upon two different substances, soil to water.
  Cohesion is the force that that acts upon two like substances, water to water.
Both forces affect how water moves through the soil.

## Slide 29: Water movement through soil
There are three main types of soil water:
  Hygroscopic water is water held very tightly to the soil particle.
  Capillary water is water that moves freely through the soil.
  Gravitational water is water that leaves the soil caused by the forces of gravity.

## Slide 30: Soil Permeability Rates